| NGN Management Focus Group | NGNMFG-OD-013-R2 |
| --- | --- |
|  |  | Virtual Meeting, 7 September 2005 |
| OUTPUT DOCUMENT |
| Source: | NGNMFG |
| Title: | NGN Management Specification Roadmap, version 1.0 |

# NGN Management Specification Roadmap

# 1.	Purpose and scope

The goal of the work of the NGN Management Focus Group (NGNMFG) is to "organize and undertake a centralized approach regarding specification of NGN management related to FCAPS interfaces, in particular to support the NGN Release 1". FCAPS interfaces are generally understood to include NE-OS, OS-OS, and NE/OS-WS interfaces in support of element, network, service, and business management.

This roadmap document provides the result of this work. It lists the existing specifications which the NGNMFG agreed to offer to the September 2005 meeting of ITU-T SG4 as candidates for a suite of management specifications. It identifies also the gaps which have to be filled.

The current content is relevant for NGN Release 1; information regarding later Releases will be added when needed.

# 2.	Workflow and specification architecture

The NGNMFG ToR lists a number of objectives. This list provides a structure for the workflow of the NGNMFG and provides simultaneously a high level architecture for the set of specifications to be generated by the NGNMFG.

The flow is from High Level Requirements (objective 1), via Management Requirements (objective 2), and Management Framework, Principle and Architecture (objective 3), to Protocol-neutral and Protocol-specific NGN Management Interface Specifications (objective 4).

Figure 1 visualizes the workflow which connects the objectives and, simultaneously, the dependencies between these specifications.

Figure 1: Specification Architecture

Each of the five rectangles in Figure 1 represents a group of specifications, which are contained in one or more documents.

The High Level Requirements are given from outside the NGNMFG, the most important source being the ITU-T NGN Focus Group (NGN FG). The documents containing the high level requirements are:

- Y.2001, General overview of NGN;

- Y.2011, General principles and general reference model for next generation networks;

- Y.NGN-FRA, NGN Functional Requirements and Architecture [2].

The task of the NGNMFG is to identify candidate documents for the remaining four groups. Candidates will be selected from existing documents, from documents which are under construction, or from planned documents. Only when no suitable candidate can be identified, the NGNMFG will generate a specification document.

The suite of candidate documents will be proposed to the September 2005 meeting of ITU-T SG4.

# 3.	Specification categories

The set of NGN Management specifications described in this roadmap is separated in four categories:

1) Specifications for NGN management (section 4.1):

Specifications are listed under this category if they have been written specifically for NGN management and their scope is the NGN as a whole, i.e. they are not related to a specific functional entity in the NGN.

Within this category, specifications are grouped according to their role in the specification architecture in Figure 1.

2) Generic telecommunications management specifications, reused for NGN (section 4.2):

Specifications will be listed under the first category, if they have not been written specifically for management of the NGN. The indication "NGN" does not appear anywhere in the titles of these documents, yet they are recognized as applicable for management of the NGN because of their generic applicability to telecommunications management.

Dependent on their main subject areas, specifications within this category are identified as generic or according to their relation with the FCAPS and other functional areas.

3) Specifications for the management of NGN functions (section 4.3):

Specifications will be listed under this category if their scope is the management of one or more specific functional entities in the NGN. This category includes specifications which have been written specifically for the management of NGN functions, and specifications which have been written for the management of non-NGN functional entities which are re-used in the NGN.

Specifications in this category are identified according to their main application area in terms of the functional entities of the NGN as they are defined in Y.NGN-FRA [2], Figure 3. These entities are:

- Service Stratum:

  - Application Functions

  - User Profile Functions

  - Service and Control Functions:

    - Other Multimedia Components

    - Streaming Services

    - PSTN/ISDN Emulation

    - IP Multimedia Component including PSTN/ISDN Simulations

- Transport Stratum:

  - Network Access Attachment Function

  - Resource and Admission Control Functions

  - Access Functions

  - Access Transport Functions

  - Edge Functions

  - Core Transport Functions

- CPE:

  - Legacy Terminals

  - Gateways

  - NGN Terminals

  - Customer Networks

4) Other relevant specifications (section 4.4):

Specifications, considered relevant for the management of the NGN, which do not belong to another category.

# 4.	Agreed specifications

The following tables list the specifications as agreed by the NGNMFG.

#### Editor's Note: Traceability?

## 4.1	Specifications for NGN management

| Subcategory | Document ID | Title | Notes/Issues |
| --- | --- | --- | --- |
| Requirements | ETSI TS 188 004 | NGN Management; OSS Vision |  |
|  | IETF RFC 3535 | Overview of the 2002 IAB Network Management Workshop |  |
|  | ITU-T M.3060 | Management of Next Generation Networks |  |
| Management Architecture | ITU-T M.3060 | Management of Next Generation Networks | harmonization issue with ETSI TS 188 001 (See also section 6.1) |
|  | ETSI TS 188 001 | NGN Management; OSS Architecture | harmonization issue with ITU-T M.3060 (See also section 6.1) |

## 4.2	Generic telecommunications management specifications reused for NGN

| Subcategory | Document ID | Title | Notes/Issues |
| --- | --- | --- | --- |
| Generic | ITU-T M.3050 series | Enhanced Telecom Operations Map | 1) Equal to TMF eTOM v4 GB921 2) NGN relationship explained in M.3060 and in TS 188 001 |
|  | TMF 053B, C, D, and F | NGOSS Technology-Neutral Architecture v4.5 |  |
| Fault | X.733.1 | Protocol-Neutral UML Description of the Alarm Reporting Function |  |
| Configuration |  |  |  |
| Accounting | ATIS-0300075-2005 and ATIS-0300075.1-2005 | Usage Data Management for Packet-Based Services - Service-Neutral Architecture and Protocol Requirements - Service-Neutral Protocol Specification for Billing Applications | harmonization issue with 3GPP IMS Charging specifications (See also section 6.3) |
| Performance |  |  |  |
| Security | M.3016 series | Security of the management plane | NGN relationship explained in M.3060 |
| Service Management | ITU-T M.3341 | QoS/SLA management service requirements |  |
|  | ITU-T M.3350 | Emergency telecommunication service management requirements |  |
| Protocol | IETF Netconf | NETCONF configuration protocol | for interfaces to the NE, for configuration |
|  | IETF STD 62 | Simple Network Management Protocol version 3 | for interfaces to the NE, primarily monitoring (including event reporting) |
|  | OASIS WSDM MUWS | WSDM Management Using Web Services (WSDM-MUWS) v1.0 | for non-NE interfaces |
| Interface definition language | IETF STD 58 | Structure of Management Information version 2 | to support SNMP; recommended MIBs are for further study |

## 4.3	Specifications for the management of NGN functions

| Subcategory | Document ID | Title | Notes/Issues |
| --- | --- | --- | --- |
| Core Transport Functions | ITU-T G.7718/Y.1709 | Framework for ASON Management |  |
|  | ITU-T G.7718.1/Y.1709.1 | Protocol-neutral management information model for the control plane view |  |
|  | TMF 513 | MTNM Business Agreement (part of TMF MTNM Solution Suite) | harmonization issue with 3GPP 32.111 and 32.671-675 (see also sections 6.2 and 6.4) |
|  | TMF 608 | MTNM Information Agreement (part of TMF MTNM Solution Suite) |  |
|  | TMF 814 | MTNM Solution Set in CORBA IDL with Supporting Documentation (part of TMF MTNM Solution Suite) |  |
|  | TMF 814A | MTNM Implementation Statement Templates for CORBA (part of TMF MTNM Solution Suite) |  |
| Access Transport Functions | TMF MTNM Solutions Suite (see Core Transport Functions) |
| Service Stratum | ATIS TMOC Usage Data Management specifications (see table 4.2) |  |  |
| IMS | 3GPP TS 32.111-1 to -4 | Fault Management IRP | harmonization issue with TMF MTNM Solution Suite (See also section 6.2) |
|  | 3GPP TS 32.301-304 | Notification IRP |  |
|  | 3GPP TS 32.311-314 | Generic IRP |  |
|  | 3GPP TS 32.601-604 | Basic CM IRP |  |
|  | 3GPP TS 32.621-625 | Generic NRM IRP |  |
|  | 3GPP TS 32.631-635 | Core NRM IRP |  |
|  | 3GPP TS 32.661-664 | Kernel CM IRP |  |
|  | 3GPP TS 32.671- 675 | State Management IRP | possible harmonization issue with TMF MTNM Solution Suite (See also section 6.4) |
|  | 3GPP TS 23.125, 32.240, 32.260, 32.296-299 | IMS Charging Management | harmonization issue with TMOC Usage Data Management specifications (See also section 6.3) |

## 4.4	Other relevant specifications

| Subcategory | Document ID | Title | Notes/Issues |
| --- | --- | --- | --- |
|  | IETF RFC 3444 | On the Difference between Information Models and Data Models |  |

# 5.	Gaps

The following table identifies areas for which suitable specifications candidate could not be identified. The NGNMFG has brought the gap areas to the attention of the organizations listed in the third column, on the assumption that they will address the gap.

| Area | Reference | Organization |
| --- | --- | --- |
| Exchange of service orders, trouble tickets, etc | NGNMFG-ID-028 NGNMFG-OD-006 | ITU-T SG4 |
| NGN function oriented NE MIBs | TBD | TBD |

# 6.	Harmonization Issues

## 6.1 	Management Architecture

ITU-T M.3060 and ETSI TS 188 001

## 6.2	Fault Management

TMF MTNM Solution Suite, 3GPP 32.111, and X.733.1 regarding alarm reporting

## 6.3	Accounting Management

3GPP Charging and TMOC Usage Data Management specifications

## 6.4	State Management

TMF MTNM Solution Suite and 3GPP 32.671-675

______________

### Annex 1: Organizations owning the listed specifications

In this document, abbreviated names are used to identify the organizations which own the contributed specifications. This appendix lists the abbreviations, the full names, and the urls of the websites of the contributing organizations.

| Acronym | Full name | Website |
| --- | --- | --- |
| 3GPP | 3rd Generation Partnership Project | www.3gpp.org |
| ATIS | Alliance for Telecommunications Industry Solutions | www.atis.org |
| ETSI | European Telecommunications Standards Institute | www.etsi.org |
| IETF | Internet Engineering Task Force | www.ietf.org |
| ITU-T | International Telecommunication Union | www.itu.int/itu-t |
| OASIS | Organization for the Advancement of Structured Information Standards | www.oasis-open.org |
| TMF | TeleManagement Forum | www.tmforum.org |

### Annex 2: Information about the listed specifications

Appendix 2 contains bibliographic information for each of the specifications listed in this document. This appendix is contained in a separate ppt file.

### References

[1]	NGN Management Focus Group, Terms of Reference

[2]	Y.NGN-FRA, Functional Requirements and Architecture of the NGN (FGNGN-OD-192R1)

______________

### Document history

| Version | Published in | Comments |
| --- | --- | --- |
| 0.0 | NGNMFG-ID-045 | input to 31 March 2005 meeting |
| 0.1 | NGNMFG-ID-045-R1 | output of 31 March 2005 meeting |
| 0.2 | NGNMFG-ID-045-R2 | output of 26 May 2005 meeting |
| 0.3 | NGNMFG-ID-045-R3 | output of 22 June 2005 meeting |
| 0.4 | NGNMFG-ID-045-R4 | output of 27 July 2005 meeting |
| 0.5 | NGNMFG-OD-010-R2 | output of 28 July 2005 meeting |
| 1.0 | NGNMFG-OD-013-R2 | output of 7 September 2005 meeting |

### Editors Notes: Document issues to be resolved

- It should be possible to package related specifications, like 3GPP IRPs and TMF BA/IA/SS

______________

# Footnotes

NGNMFG Terms of Reference, section 1 [1].