MPLS/FR Alliance Technical Committee

Contribution

Subject:	Soft Permanent Virtual Circuit Interworking between MPLS Pseudowires and ATM: Unmapped Mode

Contacts:	George Swallow (Cisco Systems)

Phone: +1 978 936 1398

E-Mail: swallow@cisco.com

Editor

Date:	July 2005

Location:	Ottawa, ON

Distribution:	Participants in the MPLS/FR Alliance Technical Committee

Abstract:	This is the baseline text for version 2.0 of fault management interworking for ATM/FR/Ethernet multiservice interworking.

Declaration of IPR:

The contributor has read and supports the MLPS/FR Alliance’s IPR Policy Statement.  To the best of the contributor’s knowledge, the contributing member: does not have any IPR that would be infringed by the Implementation Agreement proposed by any member.

Notice: This contribution has been created to assist the MPLS/FR Alliance.  This document is offered to the MPLS/FR Alliance solely as a basis for discussion and is not a binding proposal on the companies listed as resources above. Each company in the source list, and the MPLS/FR Alliance, reserves the rights to at any time to add, amend, or withdraw statements contained herein.

This Working Text represents work in progress by the MPLS/FR Alliance, and must not be construed as an official MPLS/FR Alliance Technical Document.  Nothing in this document is in any way binding on the MPLS/ Alliance or any of its members.  The document is offered as a basis for discussion and communication, both within and without the MPLS/FR Alliance.

For additional information contact:

The MPLS/FR Alliance, 39355 California Street,

Suite 307, Fremont, CA 94538

510-608-3997 phone

info@mplsforum.org

© 2005 MPLS/FR Alliance

Soft Permanent Virtual Circuit Interworking between MPLS Pseudowires and ATM: Unmapped Mode

Version 1.0

DRAFT
Baseline Text

MPLS/FR Alliance Technical Committee
July 2005

Note:	The user’s attention is called to the possibility that implementation of the MPLS implementation agreement contained herein may require the use of inventions covered by patent rights held by third parties. By publication of this MPLS implementation agreement the MPLS/FR Alliance makes no representation that the implementation of the specification will not infringe on any third party rights. The MPLS/FR Alliance take no position with respect to any claim that has been or may be asserted by any third party, the validity of any patent rights related to any such claims, or the extent to which a license to use any such rights may not be available.

Editor:

George Swallow Cisco Systems

For more information contact:

The MPLS/FR Alliance Suite 307 39355 California Street Fremont, CA 94538 USA Phone: +1 (510) 608-3997 FAX: +1 (510) 608-5917 E-Mail: info@mplsforum.org WWW: http://www.mplsforum.org/

Full Notice

Copyright © 2005 MPLS/FR Alliance.

All rights reserved.

This document and translations of it may be copied and furnished to others, and works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works.  However, this document itself may not be modified in any way, such as by removing the copyright notice or references to the MPLS/FR Alliance, except as needed for the purpose of developing MPLS implementation agreements (in which case the procedures copyrights defined by the MPLS/FR Alliance must be followed), or as required to translate it into languages other than English

This document and the information contained herein is provided on an "AS IS" basis and THE MPLS/FR ALLIANCE DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

Revision History

| Version | Change | Date |
| --- | --- | --- |
| Mpls2005.064.00 | Initial TC contribution created from mpls2005.021.00 | April 2005 |
| Mpls2004.064.01 | Baseline format applied to mpls2005.064.00 | July 2005 |
| Mpls2004.064.02 | Same as Mpls2004.064.01 | July 2005 |
| Mpls2004.064.03 | Updated with text on AII Formats | July 2005 |

Table of Contents

1	Introduction	2

2	Terminology	2

3	Problem Statement	3

3.1	Reference Network Diagram	3

4	Background on identifiers	4

4.1	Pseudowire Identifiers	4

4.2	ATM SPVC Identifiers	5

5	Proposed Solution	5

5.1	PSN / ATM Interface	5

5.2	Signaling	6

5.3	Mapping Identifiers	6

5.4	Configuration	9

5.5	Handling Re-assembly	10

6	Issues	11

7	References	11

# Introduction

[Editors’ Note:  This version represent a first attempt at aligning “L2 to MPLS Service Mediation Architecture” which is also a work-in-progress.  It is recognized that further alignment will be necessary as the two documents mature.]

In current ATM deployments, Soft Permanent Virtual Connections (SPVCs) are used to provision both Asynchronous Transfer Mode (ATM) Permanent Virtual Channel Connections (PVCC) and Permanent Virtual Path Connections (PVPC) and Frame Relay (FR) PVCCs.

Pseudowires over Multiprotocol Label Switching (MPLS) and L2TPv3 PSNs are current being introduced as backbone technologies to carry these same services.  Mechanisms are being developed to enable a flexible provisioning model that incorporates elements of the SPVC model in that configuration of the end service exists only at the end-points.  These mechanisms are described in the Pseudowire Control Protocol [1] and Provisioning Models and Endpoint Identifiers in L2VPN Signaling [4].

As services are migrated from ATM to PSNs, any reasonable deployment scenario mandates that there be a period of time (possibly protracted or permanent) in which services will need to be established and maintained between end-users where one end of a circuit is attached to an ATM network and the other end is attached to a PSN.

The requirements and architecture can be found in [6].  That document indicates that both mapped and unmapped modes will be supported.  This document describes the procedures for the unmapped mode of interworking Pseudowire Signaling and ATM Signaling across a UNI, AINI, or PNNI [2].

# Terminology

L2PE	Layer 2 Provider Edge, a customer facing node which is part of the L2 network

L2E	Layer 2 Edge, a node of the ATM network which is attached to a node of the MPLS/IP network

PSN	Packet Switched Network

MPE	MPLS/IP Provider Edge, a customer-facing node that is part of the MPLS/IP PSN

MME	MPLS/IP Mediation Edge, a node of the MPLS/IP PSN that is attached to a node of the L2 network

AI     	Attachment Identifier

AGI     Attachment Group Identifier

AII	Attachment Individual Identifier

SAI	Source Attachment Identifier

TAI	Target Attachment Identifier

SAII	Source Attachment Individual Identifier

TAII	Target Attachment Individual Identifier

PNNI	Private Network-Network Interface

UNI	User Network Interface

AINI	ATM Inter-Network Interface

PVCC	Permanent Virtual Channel Connection

PVPC	Permanent Virtual Path Connection

SPVC	Soft Permanent Virtual Connection

IE	Information Element

# Problem Statement

To facilitate the migration of ATM and Frame Relay SPVCs to a PSN carrying pseudowires, a means of interoperating ATM and LDP signaling needs to be defined.  Further this interoperation must preserve the essential reasons for using SPVCs, namely, keeping configuration limited to the edge nodes supporting a particular connection and allowing the network to be able to recover in the event of the failure of any facility between those two edge nodes.

It is also useful to perform reassembly of AAL5 frames of Frame Relay connections at the boundary between the ATM network and the PSN.  This serves to reduce dataplane protocol overhead in the PSN.

Finally, any solution must not preclude any existing services.  In particular, Frame Relay to ATM interworking is recognized to be in wide use.

## Reference Network Diagram

The diagram below shows an ATM network interfaced to a PSN.  A soft PVC is to be set up between the two customer facing edge nodes, L2PE, and MPE.  Two interconnections are shown, to indicate that the connection must be routable over either interconnection in the event of the failure of the preferred interconnection.  The 'M' (for MPLS/IP PSN) was chosen over 'P' (for PSN) to allow 'P' to stand for provider.

Figure 1: Service Mediation Network Reference

# Background on identifiers

## Pseudowire Identifiers

Pseudowires serve to connect a pair of attachment circuits (ACs).  In the context of this document these ACs are either Frame Relay DLCIs or ATM VPI/VCIs.  An AC is identified by an Attachment Identifier (AI) and the IP address of the egress MPE.  AIs are defined in [1]. An AI is a logical reference for both the physical/logical port as well as the virtual circuit.  That is an AC is fully identified by a node-ID (IP address) and an AI.

The AI has further structure to designate groups of identifiers and individual identifiers within a group, these are called attachment group identifiers (AGI) and attachment individual identifiers (AII), respectively.  When pairs of AIs are used in signaling, they are further designated by their role in the call, with the operative terms being source and target of the call.  Thus we also have the terminology, source attachment identifier (SAI), source attachment individual identifier (SAII), target attachment identifier (TAI), and target attachment individual identifier (TAII). The source and target designations are only relevant from the perspective of the pseudowire control protocol. For example, a node receiving an LDP label mapping message from a remote node will swap the SAI and TAI values when it sends a label mapping message in the reverse direction back to the originating node.

Attachment Identifiers (AIs) are carried in the Generalized ID FEC Element of LDP.  Each AI encoded as two fields, the Attachment Group Identifier (AGI) and an Attachment Individual Identifier (AII), each encoded using a type-length-value (TLV) format as defined in Section 5.2.2 of [1].  In particular:

Note that the interpretation of a particular field as AGI, SAII, or TAII depends on the order of its occurrence.  The type field identifies the type of the AGI, SAII, or TAII.

The rules for constructing the AGI and AII are left to the specification of applications and/or models.

## ATM SPVC Identifiers

In ATM, the identifying information of the attachment circuit at the destination interface consists of an ATM End-System Address (AESA) and the DLCI or VPI/VCI.  The AESA identifies both the destination node and port where the end-user is attached.  The DLCI or VPI/VCI are signaled in the Called party SPVC IE and are carried as literal values.  The Called party SPVC IE has two formats depending on whether the service being signaled is a Frame Relay SPVC or an ATM SPVC.  Furthermore, ATM SPVCCs and ATM SPVPCs are distinguished through the bearer class codepoint in the Broadband bearer capability IE.

AESAs are based on the NSAP address format.  Figure 2 shows the generic format.

|--AFI (Authority & Format Identifier)

|                                   Selector

|  |--IDP (Initial Domain Part)       |

V  V                                  V

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| |   |    H O - D S P    |   E S I   |0|

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

HO-DSP   High Order Domain Specific Part

ESI      End System Identifier

Figure 2:  Generic AESA Format

Although many formats are permitted within AESAs, all ATM Forum defined formats include a six byte End System Identifier or ESI.  The ESI's role is to identify a host.  Typically, the first 13 bytes of the AESA are common for all end systems attached to an ATM node.  This is the default behavior in PNNI.  In this case, the ESI is used to differentiate between end systems attached to the same switch.  From the point of view of the egress ATM switch, the ESI maps to a physical or logical port.

Thus common practice is to use the ESI to carry the port information.

# Proposed Solution

## PSN / ATM Interface

The interface between the ATM network and the PSN can be any of the following:

- ATM Forum User Network Interface (UNI)

- ITU-T User Network Interface (UNI)

- Private Network-Network Interface (PNNI)

- ATM Inter-Network Interface (AINI)

In the case of the UNI, there must be extensions to support the Called party soft PVPC or PVCC IE defined if not all of UNI 4.1.  (In this document we refer to the Called party soft PVPC or PVCC IE as simply the SPVC IE.)  There may be extensions to support:

the Calling party soft PVPC or PVCC IE,

signaled VPs, using the "transparent VP service" codepoint for the bearer class in the Broadband bearer capability IE,

crankback indication by setting the cause location in the Cause IE to a value other than "user", and

frame discard indication using either the Frame Discard bits or the ATM adaptation layer parameters IE.

## Signaling

In ATM soft PVCs are statically defined across the UNI interfaces, but are signaled across the ATM network using PNNI signaling.  For the signaling part, one edge node is configured to be active for the SPVC and the other is defined to be passive.  That is, one end always initiates the call.  ATM signaling creates a bidirectional circuit in a single pass.  Bandwidth parameters for each direction of the circuit are carried in the setup message.

A paradigm analogous to the active/passive roles in SPVC setup above for pseudowires is known as single sided provisioning.  These procedures are defined in Provisioning Models and Endpoint Identifiers in L2VPN Signaling [4] section 3.1.2.  A small difference exists here in that the "discovery" process occurs when an ATM SETUP message arrives.

It should be noted, that the pseudowire setup remains a pair of unidirectional labels assigned by two essentially independent label requests.  It is only the triggering of the reverse label request that is tied to the forward label request.  Further Pseudowire Signaling does not carry bandwidth parameters at all.

## Mapping Identifiers

In Pseudowire Control Plane Signaling, an IP address identifies the egress node, and the (T)AI identifies the egress port and DLCI or VPI/VCI.  In ATM, an AESA identifies both the egress node and port, and the DLCI or VPI/VCI is carried as a literal in the SPVC IE.

Two issues must be addressed.  First a mapping between ATM and IP addresses is needed.  Second a means of translating between the ATM port and SPVC IE and AIs.

### Mapping Addresses

OSI Network Service Access Point Addresses include an Authority and Format Identifier (AFI). The AFI value 35 has been assigned to the IANA. Within this format a two-octet Internet Code Point (ICP) field is available for assignment by the IANA. Currently there is one code point, 0, assigned for embedding IPv6 addresses.  A format and code point assignment has been proposed by the ATM Forum in [3].  That format is shown below.

|--AFI (Authority &

|       Format Identifier)          Selector

|  |--IDP (Initial Domain Part)       |

V  V |<---- HO-DSP ----->|<-- ESI -->|V

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|3|0 0|I P v 4|0 0 0 0 0 0|           |0|

|5|0 1|Address|0 0 0 0 0 0|           |0|

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

HO-DSP   High Order Domain Specific Part

ESI      End System Identifier

Figure 3: NSAP with Embedded IPv4 Address

While it is common practice to carry the port number in the ESI field, We note that there are six unused bytes in the HO-DSP as well as the Selector Byte which could be used in a situation where the ESI was not available.

The format to embed an IPv6 address in an NSAP address is defined in [RFC1888].  In this format the only unused space is the Selector Byte.  This allows for the identification of 256 ports.  If more ports are needed, multiple addresses must be assigned.

|--AFI (Authority &

|       Format Identifier)          Selector

|  |--IDP (Initial Domain Part)       |

V  V                                  V

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|3|0 0|    I P v 6   A d d r e s s    | |

|5|0 0|                               | |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Figure 4: NSAP with Embedded IPv6 Address

While it is expected that for IPv4 the ESI will commonly be used and for IPv6 the Selector Byte must be used, the discussion below will simply refers to a generic port field.

### Mapping the ESI and SPVC IEs to AIs

The AI is composed of an AGI and an AII.  In the single-sided signaling procedures documented in [4], the AGI serves a specific purpose.  Therefore, no special use of the AGI is made by this Implementation Agreement.  Rather, the MME is configured with an AGI and procedures of  [4] are followed.

The ESI and SPVC IE values are reformatted to form the AII.  The SPVC IE can carry either a Frame Relay DLCI or an ATM VPCI and optionally an ATM VCI.  These are reformatted to one of two AII Types, one for Frame Relay and one for ATM.  In the ATM format the presence or lack thereof of a VCI is inferred from the length field.

#### Frame Relay AII Format

0                   1                   2                     3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   AII Type    |     Length    |        Port Identifier        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                    Port Identifier (Cont.)                    |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     DLCI                      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

AII Type

[The value is to be assigned by IANA.]

Length

8 or 9 depending on the number of bytes in the DLCI field.

Port Identifier

From the destination NSAP address.  By default, the ESI value.  By configuration, any combination of NSAP fields.

DLCI

For a 10-bit DLCI, the value of the DLCI as a 16-bit number, i.e. the value of the DLCI in the SPVC IE right justified and padded on the left with zeroes.  For a 23-bit DLCI the value of the DLCI as a 24-bit number, i.e. the value of the DLCI in the SPVC IE right justified and padded on the left with zeroes.

#### ATM AII Format

0                   1                   2                     3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|   AII Type    |     Length    |        Port Identifier        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                    Port Identifier (Cont.)                    |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|              VPCI             |              VCI              |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

AII Type

[The value is to be assigned by IANA.]

Length

8 or 10 depending on the presence of the VCI field.

Port Identifier

From the destination NSAP address.  By default, the ESI value.  By configuration, any combination of NSAP fields.

VPCI

Value of the VPCI as a 16-bit number.

VCI

Value of the VCI as a 16-bit number.  For SPVPCs this field is omitted.

## Configuration and Procedures

L2PEs: For each Permanent Virtual Connection, the L2PE is configured with the target AESA and DLCI or VPI/VCI.

AEs: AEs are configured with the AESA prefix representing the set of PSN nodes reachable through its link(s) to the PSN.  Multiple prefixes may be configured to allow choices of optimum nodes to reach and to allow reachability to a larger set of nodes, should some other L2E or MME fail.  The advertisement into the ATM network's routing protocol (e.g.PNNI) should be withdrawn if the associated link(s) have failed.

MPEs: MPE require no special configuration.  They are simply configured with the (T)AII of each of their ACs.

MEs: MEs must be able to encode and parse the [to be assigned] AII types.  Associated with each of these AII type is an AII format (used to form TAIIs) and rules for how to extract the port from the ATM called party address.

### Procedures within the ATM Network

In an SPVC, one end is designated as the 'owner' and is responsible for initiating the connection.  In order to simplify the interworking, this solution proposes that SPVCs always be initiated from the ATM side.  This obviates any need to communicate bandwidth information across the PSN to the ATM network.

The AEs as the owner of the connection, initiates PNNI signaling as it normally would.  Finding a longest match associated with one or more of the AEs it performs normal PNNI routing selection and sends a SETUP message which includes the SPVC IE.

When the SETUP message arrives at the L2E, it performs normal PNNI signaling processing and forwards the message across the PNNI, AINI or UNI to the MME.

### Procedures for the MME

When the MME receives a SETUP message, performs ATM admission control.  Additionally, the MME may perform additional checks to determine if it has the necessary resources to support the pseudowire connection in the forward direction.  For example, in some network deployments it may determine if a PSN tunnel can be established in order to satisfy QoS or restoration requirements.

In the event that the call cannot be admitted, the MME SHOULD set an appropriate cause code, assuming that it is capable of supporting crankback procedures.

When the MME has successfully performed ATM admission control, it splices the call to a pseudowire using the signaling procedures of Provisioning Models and Endpoint Identifiers in L2VPN Signaling [4].  First, it extracts the destination IP address from the ATM called party address.  It then determines if a LDP session exists with this node.  If not, one is initiated.  It then examines the SPVC IE to determine the type of service that	 is being requested.  Based on the service type it selects AII type and format.  It then extracts the port, VPI, VCI, and/or DLCI information as appropriate to the service and formats an AII.  It formats an SAI using the same encoding rules, using the port the setup message was received on and the Connection Identifier. This AI becomes the handle that will be used to locate the context for this call.  It then sends a Label Mapping message to the target node.

When it receives a Label mapping message from the target node, it uses the TAI (i.e. what it sent as the SAI) to locate the call context and completes the ATM call.

### Procedures for the MPE

The procedures for the MPE follow [4] with no changes.  That is, the MPE uses the TAI to identify interface and DLCI or VPI/VCI.  No decoding of the TAII is necessary; the AI and AC are simply configured as in [4].

If the forward label mapping completed successfully, the MPE responds with an LDP label-mapping message in the reverse direction.  The same encapsulation as the forward direction MUST be signaled.

### Call Completion

When the MME receives the label mapping message, it uses the TAI to locate the context for this call and then completes the ATM call by sending a CONNECT message back to the L2PE.

## Handling Re-assembly

When an MME detects that the requested service is Frame Relay, by default it will perform AAL5 re-assembly for Frame Relay SPVCs.  In this case the AAL5 SDU frame mode encapsulation as defined in Encapsulation Methods for Transport of ATM Cells/Frame Over IP and MPLS Networks [5] is RECOMMENDED.

On a per ATM/PSN interface basis, an MME may be configured to not perform re-assembly for Frame Relay.  No per circuit selection is provided.  In this case the RECOMMENDED encapsulation is ATM N-to-1 Cell Mode.

Both ATM SPVCCs and SPVPCs are encapsulated using one of the cell- mode encapsulations.  The RECOMMENDED encapsulation is ATM N-to-1 Cell Mode.

# Issues

The Frame Relay format for the SPVC IE was added later.  Some ATM equipment still uses the ATM SPVC format with the DLCI encoded in the VPI/VCI fields.  To support these switches without change , and still allow AAL5 reassembly to be done at the MME, a means must be established to indicate to the MME that AAL5 reassembly is required.

# References

- Martini, L., et al.  Pseudowire Setup and Maintenance using LDP.  IETF, draft-ietf-pwe3-control-protocol-17.txt.  June, 2005.

- ATM Forum, af-pnni-0055.001, Private Network-Network Interface Specification Version 1.1, April 2002

- ATM Forum, str-cs-ipaddr-01.01, IP-Based Addressing Version 1.0, October 2003

- Rosen, E. et al. Provisioning Models and Endpoint Identifiers in L2VPN Signaling. IETF, draft-ietf-l2vpn-signaling-03.txt, February 2005.

- Martini, et al., Encapsulation Methods for Transport of ATM Cells/Frame Over IP and MPLS Networks, draft-ietf-pwe3-atm-encap-07.txt, October 2004.

- MFA, , L2 to MPLS Service Mediation Architecture, work-in-progress.

END OF DOCUMENT