ITU - Telecommunication Standardization Sector	Temporary Document 066(PLEN)

STUDY GROUP 15

Geneva, 15-26 October 2001

Question(s):	Q14/15

SOURCE*:	Editor G.7712/Y.1703

TITLE:	Draft Revision of G.7712/Y.1703 (ex.G.dcn), Version 1.1

__________________

This TD provides version 1.1 for draft Revision of G.7712/Y.1703 (ex.G.dcn).

ITU-T Draft New Recommendation G.7712/Y.1703

ARCHITECTURE AND SPECIFICATION OF DATA COMMUNICATION NETWORK

Summary

This Recommendation defines the architecture requirements for a Data Communications Network (DCN) which may support distributed management communications related to the Telecommunications Management Network (TMN), distributed signalling communications related to the Automatic Switched Transport Network (ASTN), and other distributed communications (e.g., Orderwire or Voice Communications, Software Download).  The DCN architecture considers networks that are IP-only, OSI-only, and mixed (i.e., support both IP and OSI). The interworking between parts of the DCN supporting IP-only, parts supporting OSI-only, and parts supporting both IP and OSI are also specified.

Various applications (e.g., TMN, ASTN, etc.) require a packet based communications network to transport information between various components.  For example, the TMN requires a communications network, which is referred to as the Management Communications Network (MCN) to transport management messages between TMN components (e.g., NEF component and OSF component).  ASTN requires a communications network, which is referred to as the Signaling Communications Network (SCN) to transport signaling messages between ASTN components (e.g., CC components).  This recommendation specifies data communication functions that can be used to support one or more application’s communications network.

The data communications functions provided in this recommendation support connection-less network services. Additional functions may be added in future versions of this recommendation to support connection-oriented network services.

Source and history

This Recommendation forms part of a suite of Recommendations covering transport networks.

| Document history |
| --- |
| Issue | Notes |
| 1.0 | Output of Q14/15 October 2001 meeting |
| 1.1 | Output of Q14/15 April 2002 meeting |

Keywords

Data Communication Network, Internet Protocol (IP), Open System Interface (OSI).

CONTENTS

1	Scope	5

2	References	5

3	Terms and definitions	6

4	Abbreviations	8

5	Conventions	10

6	DCN Characteristics	11

6.1	TMN Application	13

6.1.1	X Management Subnetwork Architecture	15

6.1.1.1	Topology for Management Subnetwork	17

6.1.2	Reliability of MCN	18

6.1.3	Security of MCN	19

6.1.4	MCN Data Communication Functions	19

6.2	ASTN Application	20

6.2.1	Topology of SCN	21

6.2.2	Reliability of SCN	24

6.2.3	Security of SCN	27

6.2.4	SCN Data Communication Functions	28

6.3	Other Applications Requiring Communication Networks	29

6.4	Separation of Various Applications	30

7	DCN Functional Architecture and Requirements	30

7.1	Specification of Data Communication Functions	31

7.1.1	ECC Access Function	31

7.1.2	ECC Data-Link Layer Termination Function	31

7.1.2.1	SDH ECC Data-Link Layer Termination Function	32

7.1.2.1.1	Mapping the SDH Data-Link Layer Frame into the ECC	32

7.1.2.1.2	SDH ECC Data-Link Layer Protocol Specification	33

7.1.2.1.2.1	IP-only Interface	33

7.1.2.1.2.2	OSI-only Interface	33

7.1.2.1.2.3	Dual Interface (IP + OSI)	33

7.1.3	[Network Layer PDU into ECC Data-Link Frame] Encapsulation Function	34

7.1.3.1	[Network Layer PDU into SDH ECC Data-Link Frame] Encapsulation Function	34

7.1.3.1.1	IP-only Interface	34

7.1.3.1.2	OSI-only Interface	35

7.1.3.1.3	Dual (IP+OSI) Interface	35

7.1.4	Ethernet LAN Physical Termination Function	35

7.1.5	[Network Layer PDU into Ethernet Frame] Encapsulation Function	36

7.1.6	Network Layer PDU Forwarding Function	36

7.1.7	Network Layer PDU Interworking Function	36

7.1.8	Network Layer PDU Encapsulation Function	36

7.1.9	Network Layer Tunneling Function	37

7.1.10	Network Layer Routing Function	37

7.1.10.1	Integrated ISIS Requirements	37

7.1.10.1.1	Network-layer Protocol Aware Adjacency Creation	37

7.1.10.1.2	ISIS Domain-wide IP Prefix Distribution	38

7.1.10.1.2.1	Configuration Prefixes	38

7.1.10.1.2.2	Tagging of Propogated Prefixes	38

7.1.10.1.2.3	Route Preference	39

7.1.11	IP Routing Interworking Function	39

7.1.12	[Applications to Network Layer] Mapping Function	39

7.2	Provisioning Requirements	40

7.3	Security Requirements	40

APPENDIX I	Constraints of OSPF/IntISIS Interworking Function.	37

APPENDIX II	Bibliography.	40

# 1	Scope

This Recommendation defines the architecture requirements for a Data Communications Network (DCN) which may support distributed management communications related to the Telecommunications Management Network (TMN), distributed signalling communications related to the Automatic Switched Transport Network (ASTN), and other distributed communications (e.g., Orderwire or Voice Communications, Software Download).  The DCN architecture considers networks that are IP-only, OSI-only, and mixed (i.e., support both IP and OSI). The interworking between parts of the DCN supporting IP-only, parts supporting OSI-only, and parts supporting both IP and OSI are also specified.

The DCN provides Layer 1 (physical), Layer 2 (data-link) and Layer 3 (network) functionality and consists of routing/switching functionality interconnected via links. These links can be implemented over various interfaces, including Wide Area Network (WAN) interfaces, Local Area Network (LAN) interfaces, and Embedded Control Channels (ECCs).

Various applications (e.g., TMN, ASTN, etc.) require a packet based communications network to transport information between various components.  For example, the TMN requires a communications network, which is referred to as the Management Communications Network (MCN) to transport management messages between TMN components (e.g., NEF component and OSF component).  ASTN requires a communications network, which is referred to as the Signaling Communications Network (SCN) to transport signaling messages between ASTN components (e.g., CC components).  This recommendation specifies data communication functions that can be used to support one or more application’s communications network.

The data communications functions provided in this recommendation support connection-less network services. Additional functions may be added in future versions of this recommendation to support connection-oriented network services.

# 2	References

The following ITU-T Recommendations, and other references contain provisions, which, through reference in this text, constitute provisions of this Recommendation. At the time of publication, the editions indicated were valid. All Recommendations and other references are subject to revision; all users of this Recommendation are therefore encouraged to investigate the possibility of applying the most recent edition of the Recommendations and other references listed below. A list of the currently valid ITU-T Recommendations is regularly published.

- ITU-T G.7070 - Network Node Interface for the Synchronous Digital Hierarchy.

- ITU-T G.7090 – Network Node Interface for the Optical Transport Network.

- ITU-T G.783 – Characteristics of synchronous digital hierarchy (SDH) equipment functional blocks

- ITU-T G.784 – Synchronous digital hierarchy (SDH) management

(	ITU-T G.798 – Characteristics of Optical Transport Networks (OTN) Hierarchy Equipment Functional Blocks.

- ITU-T G.8070 – Requirements for Automatic Switched Transport Networks (ASTN)

- ITU-T G.872 – Architecture of Optical Transport Networks.

- ITU-T G.874 – Optical Transport Network (OTN) management

- ITU-T G.8080 – Architecture for the Automatic Switched Optical Network (ASON)

- ITU-T G.7710 – Common Equipment Management Requirements

- ITU-T M.3010 – Principles for a Telecommunications management network

- ITU-T M.3013 – Considerations for a telecommunications management network

- ITU-T M.3016 – TMN security overview

- ITU-T Q.811 – Lower layer protocol profiles for the Q3 and X interfaces

- ITU-T X.263 – Information technology - Protocol identification in the Network Layer

- IETF RFC 0791 – Internet Protocol DARPA Internet Program Protocol Specification – September 1981

- IETF RFC 792 – Internet Control Message Protocol – September 1981

- IETF RFC 894 – A Standard for the Transmission of IP Datagrams over Ethernet Networks – April 1984

- IETF RFC 826 – An Ethernet Address Resolution Protocol – November 1982

- IETF RFC 1195 – Use of OSI IS-IS for Routing in TCP/IP and Dual Enviornments – December 1990

- IETF RFC 1122 – Requirements for Internet Hosts – October 1989

- IETF RFC 1172 – The Point-to-Point Protocol Initial Configuration Options – July 1990

- IETF RFC 1332 – The PPP Internet Protocol Control Protocol (IPCP) – May 1992

- IETF RFC 1377 – The PPP OSI Network Layer Control Protocol (OSINLCP) – November 1992

- IETF RFC 1661 – The Point-to-Point Protocol (PPP) – July 1994

- IETF RFC 1662 – PPP in HDLC-like Framing – July 1994

- IETF RFC 1812 – Requirements for IP Version 4 Routers – June 1995

- IETF RFC 2328 – OSPF Version 2 – April 1998

- IETF RFC 2460 – Internet Protocol, Version 6 (IPv6) Specification – December 1998

- IETF RFC 2463 – Internet Control Message Protocol (ICMPv6) for the Internet Protocol Version 6 (IPv6) Specification – December 1998

- IETF RFC 2472 – IP Version 6 over PPP – December 1998

- IETF RFC 2740 – OSPF for IPv6 – December 1999

- IETF RFC 2784 – Generic Routing Encapsulation (GRE)

- ISO/IEC 10589 – Information technology - Telecommunications and information exchange between systems - Intermediate system to Intermediate system intra-domain routing information exchange protocol for use in conjunction with the protocol for providing the connectionless-mode Network Service (ISO 8473) – 1992

# 3	Terms and definitions

This Recommendation uses terms defined in Recommendation G.709:

3.1	Optical Channel Data Unit (ODUk)

3.2	Optical Channel Transport Unit (OTUk)

3.3	Optical Overhead Signal (OOS)

This Recommendation uses terms defined in Recommendation G.784:

3.4	Data Communications Channel (DCC)

This Recommendation uses terms defined in Recommendation G.8070:

3.5	Automatic Switched Transport Network (ASTN)

3.6	Network – Network Interface (NNI)

3.7	User – Network Interface (UNI)

This Recommendation uses terms defined in Recommendation G.8080:

3.8	Call Controller (CallC)

3.9	Connection Controller (CC)

3.10	Connection Controller Interface (CCI)

3.11	Subnetwork Controller (SNCr)

This Recommendation uses terms defined in Recommendation G.874:

3.10	General Communications Channel (GCC)

3.11	General Management Communications Overhead (COMMS OH)

This Recommendation uses terms defined in Recommendation G.7710:

3.12	X Management Network

3.13	X Management Subnetwork

This Recommendation uses terms defined in Recommendation G.872:

3.14	Optical transport network (OTN)

This Recommendation uses terms defined in Recommendation M.3010:

3.15	Adaptation Device (AD)

3.16	Data Communications Function (DCF)

3.17	Mediation Device (MD)

3.18	Network Element (NE)

3.19	Network Element Function (NEF)

3.20	Operations System (OS)

3.21	Operations System Function (OSF)

3.22	Q-interface

3.23	Translation Function

3.24	Workstation Function (WSF)

This Recommendation uses terms defined in Recommendation M.3013:

3.25	Message Communications Function (MCF)

This Recommendation defines the following terms:

3.26	Data Communications Network (DCN): The DCN is a network that supports Layer 1 (physical), Layer 2 (data-link), and Layer 3 (network) functionality.  A DCN can be designed to support transport of distributed management communications related to the TMN, distributed signalling communications related to the ASTN, and other operations communications (e.g., orderwire/voice communications, software downloads, etc.).

3.27	Embedded Control Channel (ECC): An ECC provides a logical operations channel between NEs. The physical channel supporting the ECC is technology specific. Examples of physical channels supporting the ECC are; a DCC channel within SDH, GCC channel within OTN OTUk/ODUk, or the COMMS OH channel within the OTN OOS.

# 4	Abbreviations

This Recommendation uses the following abbreviations:

AD			Adaptation Device

ARP			Address Resolution Protocol

ASON			Automatic Switched Optical Network

ASTN			Automatic Switched Transport Network

ATM			Asynchronous Transfer Mode

CallC			Call Controller

CC			Connection Controller

CCI			Connection Controller Interface

CLNP			Connection-less Network Layer Protocol

CLNS			Connection-less Network Layer Service

COMMS OH	General Management Communications Overhead

DCC			Data Communications Channel

DCF			Data Communications Function

DCN			Data Communication Network

DF			Don’t Fragment

ECC			Embedded Control Channel

EMF			Equipment Management Function

E-NNI			External NNI

ES			End System

ES IS			End System to Intermediate System

GCC			General Communications Channel

GNE			Gateway Network Element

GRE			Generic Routing Encapsulation

HDLC			High Level Data Link Control

ICMP			Internet Control Message Protocol

ID			Identifier

IIH			ISIS Hello

IP			Internetwork Protocol

IPv4			Internetwork Protocol Version 4

IPv6			Internetwork Protocol Version 6

IPCP			Internet Protocol Control Protocol

I-NNI			Internal NNI

IntISIS			Integrated Intermediate System to Intermediate System

IS			Intermediate System

ISDN			Integrated Services Digital Network

ISH			ISO 9542 Intermediate System Hello

ISIS			Intermediate System to Intermediate System

IWF			Interworking Function

LAN			Local Area Network

LAPD			Link-Access Procedure D-Channel

LCN			Local Communications Network

LSP			Link State Protocol Data Unit

MAC			Media Access Control

MCF			Message Communications Function

MCN			Management Communication Network

MD			Mediation Device

MTU			Maximum Transmission Unit

NE			Network Element

NEF			Network Element Function

NNI			Network - Network interface

ODUk			Optical Channel Data Unit

OOS			OTM Overhead Signal

OS			Operations System

OSC			Optical Supervisory Channel

OSF			Operations System Function

OSI			Open System Interface

OSINLCP		OSI Network Layer Control Protocol

OSPF			Open Shortest Path First

OTM			Optical Transport Module

OTN			Optical Transport Network

OTUk			Optical Channel Transport Unit

NSAP			Network Service Access Point

PDU			Protocol Data Unit

PPP			Point-to-Point Protocol

RFC			Request For Comment

SCN			Signaling Communication Network

SDH			Synchronous Digital Hierarchy

SNCr			Subnetwork Controller

SP			Segmentation Permitted

TCP			Transmission Control Protocol

TF			Translation Function

TLV			Type Length Value

TMN			Telecommunications Management Network

TNE			Transport Network Element

UNI			User to Network Interface

WAN			Wide Area Network

WS			Work Station

WSF			Work Station Function

xMS			X Management Subnetwork

# 5	Conventions

The following conventions are used throughout this recommendation:

Mixed DCN:	A mixed DCN supports multiple network layer protocols (e.g., OSI and IPv4).  It is possible in a mixed DCN, that the path between two communicating entities (e.g., an OS and a managed NE) will traverse some parts that only support one network layer protocol (e.g., OSI) and other parts that only support another network layer protocol (e.g., IPv4). To provide communication between such entities, one network layer protocol should be encapsulated into the other network layer protocol at the boundary of those parts supporting different network layer protocols.

OSI-only DCN:	An OSI-only DCN supports only CLNP as the network layer protocol. Therefore the end-to-end path between two communicating entities (e.g., an OS and a managed NE) will support CLNP and encapsulation of one network layer protocol into another network layer protocol is not required to support such communications.

IPv4-only DCN:	An IPv4-only DCN supports only IPv4 as the network layer protocol. Therefore the end-to-end path between two communicating entities (e.g., an OS and a managed NE) will support IPv4 and encapsulation of one network layer protocol into another network layer protocol is not required to support such communications.

IPv6-only DCN:	An IPv6-only DCN supports only IPv6 as the network layer protocol. Therefore the end-to-end path between two communicating entities (e.g., an OS and a managed NE) will support IPv6 and encapsulation of one network layer protocol into another network layer protocol is not required to support such communications.

# 6	DCN Characteristics

Various applications (e.g., TMN, ASTN, etc.) require a packet based communications network to transport information between various components.  For example, the TMN requires a communications network, which is referred to as the Management Communications Network (MCN) to transport management messages between TMN components (e.g., NEF component and OSF component).  ASTN requires a communications network, which is referred to as the Signaling Communications Network (SCN) to transport signaling messages between ASTN components (e.g., CC components).  This recommendation specifies data communication functions that can be used to support one or more application’s communications network.

Figure 6-1 illustrates example applications that can be supported via the DCN.  Each application can be supported on separate DCNs or on the same DCN depending on the network design.

figure 6-1

Example Applications Supported By a DCN

The conceptual DCN is a collection of resources to support the transfer of information among distributed components. As discussed above, examples of distributed communication that can be supported by the DCN are distributed management communications related to the TMN and distributed signalling communications related to the ASTN. In the case of a DCN supporting distributed management communications, the distributed components are TMN components (NEs, ADs, OSs, MDs, and WSs containing TMN functions such as OSF, TF, NEF, WSF).  Recommendations M.3010 and M.3013 provide further specifications for the TMN functions. In the case of a DCN supporting distributed signalling communications, the distributed components are ASTN components (NEs containing ASTN SNCr functions).  Recommendation G.8070 and G.8080 provide further specifications for the ASTN functions.

A number of telecommunications technologies can support the DCN functions such as, circuit switching, packet switching, LAN, ATM, SDH, and the OTN . Important aspects of the DCN are the quality of service, information transfer rate, and diversity of routing to support specific operational requirements of the distributed communications supported across the DCN (e.g., distributed management communications, distributed signalling communications).

The goal of an interface specification is to ensure meaningful interchange of data between interconnected devices through a DCN to perform a given function (e.g., TMN function, ASTN function).  An interface is designed to ensure independence of the type of device or of the supplier.  This requires compatible communication protocols and compatible data representations for the messages, including compatible generic message definitions for TMN management functions and ASTN control functions.

The DCN is responsible for providing compatible communication at the network layer (Layer 3), data-link layer (Layer 2), and physical layer (Layer 1).

Consideration of interfaces should be given to compatibility with the most efficient data transport facilities available to each individual network element [e.g., leased circuits, circuit-switched connections, packet-switched connections, Signalling System No. 7, Embedded Communication Channels of the SDH, OTN, and ISDN access network D- and B-channels].

This recommendation specifies the lower three layers for data communication and therefore any interworking between protocols within the lower three layers. Such interworking is provided by the Data Communications Function (DCF).  Examples of such interworking are illustrated in Figure 6-2. Note that such interworking does not terminate the Layer 3 protocols.  One example is interworking between different physical layers via a common Layer 2 protocol (e.g., bridging MAC frames from a LAN interface to an ECC).  Another example is interworking between different data-link layer protocols via a common layer 3 protocol (e.g., routing IP packets from a LAN interface to an ECC).  The third example illustrated in Figure 6-2, shows interworking between different network layer protocols via a Layer 3 tunneling function (in this example OSI is encapsulated/tunnelled over IP, however IP over OSI encapsulation/tunneling is also possible).

The type of information transported between the distributed components depends on the type of interfaces supported between the components.  A DCN supporting distributed management communications related to the TMN needs to support the transport of information associated with the TMN interfaces defined in Recommendation M.3010. A DCN supporting distributed signalling communications related to the ASTN needs to support the transport of information associated with the ASTN interfaces defined in Recommendation G.8070.

Figure 6-2

Examples of DCN Interworking

## 6.1	TMN Application

The TMN requires a communications network, which is referred to as the Management Communications Network (MCN) to transport management messages between TMN components (e.g., NEF component and OSF component).  Figure 6-3 illustrates an example relationship of the MCN and the TMN. The interfaces between the various elements (e.g., OS, WS, NE) and the MCN as illustrated in Figure 6-3 are logical and can be supported over a single physical MCN interface or multiple MCN interfaces.

Figure 6-4 illustrates an example of a physical implementation of a MCN supporting distributed management communications.  Depending on the choice of implementation of the MCN, the physical elements may support any combination of ECC interfaces, LAN interfaces, and WAN interfaces.  Figure 6-4 also illustrates the types of management plane functional blocks that can be supported in various physical elements.  Refer to Recommendations M.3010 and M.3013 for detailed specifications regarding these management functional blocks.  A Data Communications Function (DCF) is part of each physical element and provides data communication functions.

figure 6-3

Example Relationship of TMN Interfaces and MCN

figure 6-4

Example of Physical Implementation of MCN Supporting TMN

### 6.1.1	X Management Subnetwork Architecture

In Figure 6-5, a number of points should be noted concerning the architecture of a X Management Subnetwork (xMS):

- Multiple NEs at a single site:

Multiple addressable SDH or OTN NEs may appear at a given site.  For example, in Figure 6-5 NEE and NEG may be collocated at a single equipment site.

- SDH/OTN NEs and their communication functions:

The message communications function of an SDH or OTN NE terminates (in the sense of the lower protocol layers), routes or otherwise processes messages on the ECC, or connected via an external interface.

- All NEs are required to terminate the ECC. This means that each NE must be able to perform the functions of an OSI end system or IP host.

- NEs may also be required to route ECC messages between ports according to routing control information held in the NE.  This means that an NE may also be required to perform the functions of an OSI intermediate system or IP router.

- SDH/OTN inter-site communications:

The inter-site or inter-office communications link between SDH/OTN NEs may be formed from the SDH/OTN ECCs.

- SDH/OTN intra-site communications:

Within a particular site, SDH/OTN NEs may communicate via an intra-site ECC or via an Local Communications Network (LCN).  Figure 6-5 illustrates both instances of this interface.

NOTE – A standardized LCN for communicating between collocated network elements has been proposed as an alternative to the use of an ECC.  The LCN would potentially be used as a general site communications network serving SDH, OTN, and non-SDH/OTN NEs (NNEs).

figure 6-5

TMN, Management Network and Management Subnetwork Model

#### 6.1.1.1	Topology for Management Subnetwork

Figure 6-6 illustrates example MCN topologies such as linear, ring, mesh, and star utilizing ECCs and/or Local Communication Networks (LCN) (e.g., Ethernet LAN) as the physical links interconnecting the Network Elements. Figure 6-7 illustrates how a Management Subnetwork could be supported on each topology.  Common to each topology is the dual Gateways (GNE1 and GNE2) which allows reliable access to the NEs within the Management Subnetwork. Another common aspect to each of the example topologies is that each topology allows multiple diverse paths between any NE within the Management Subnetwork and the Operation System (OS).

Figure 6-6

Example Topologies

figure 6-7

Supporting a Management Subnetwork on Various Topologies

### 6.1.2	Reliability of MCN

A MCN should be designed to prevent a single fault from making the transfer of critical management messages impossible.

A MCN should be designed to ensure that congestion in the MCN does not cause the blocking or excessive delay of network management messages that are intended to correct a failure or fault.

OSs and NEs that provide an emergency function may require alternate or duplicate access channels to the MCN for redundancy.

### 6.1.3	Security of MCN

See M.3016 for MCN security requirements.

### 6.1.4	MCN Data Communication Functions

The DCF within the TMN entities shall support End System (ES) (in OSI terms) or Host (in IP terms) functionality.

- When the DCF within the TMN entities support ECC interfaces, the following functions are required to be supported:

- ECC Access Function (as specified in Section 7.1.1)

- ECC Data-Link Termination Function (as specified in Section 7.1.2)

- [Network Layer PDU into ECC Data-Link Layer] Encapsulation Function (as specified in Section 7.1.3)

- When the DCF within the TMN entities support Ethernet LAN interfaces, the following functions are required to be supported:

- Ethernet LAN Physical Layer Termination Function (as specified in Section 7.1.4)

- [Network Layer PDU into Ethernet Frame] Encapsulation Function (as specified in Section 7.1.5)

The DCF within the TMN entities may operate as an Intermediate System (IS) (in OSI terms) or as a Router (in IP terms). The DCF within TMN entities that operate as IS/Routers must be capable of routing within their Level 1 area and therefore must provide the functionality of a Level 1 IS/Router. Additionally, the DCF within a TMN entity may be provisioned as a Level 2 IS/Router, which provides the capability of routing from one area to another. The functionality of a Level 2 IS/Router is not needed in the DCF of all TMN entities. An example of a DCF supporting Level 2 IS/Router functionality might be the DCF within a gateway NE.

- When the DCF within the TMN entities operate as an IS/Router, the following functions are required to be supported:

- Network Layer PDU Forwarding Function (as specified in Section 7.1.6)

- Network Layer Routing Function (as specified in Section 7.1.10)

The DCF within a TMN entity that supports IP may be connected directly to a DCF in a neighboring TMN entity that supports only OSI.

- When the DCF within a TMN entity that supports IP is connected directly to a DCF in a neighboring TMN entity that supports only OSI, the following function is required to be supported in the DCF supporting IP:

- Network Layer PDU Interworking Function (as specified in Section 7.1.7)

The DCF within a TMN entity may have to forward a Network Layer PDU across a network that does not support the same Network Layer type.

- When the DCF within a TMN entity must forward a Network Layer PDU across a network that does not support the same Network Layer type, the following functions are required to be supported:

- Network Layer PDU Encapsulation Function (as specified in Section 7.1.8)

- Network Layer PDU Tunneling Function (as specified in Section 7.1.9)

The DCF within a TMN entity that supports IP using OSPF routing may be connected directly to a DCF in a neighboring TMN entity that supports IP using IntISIS.

- When the DCF within a TMN entity that supports IP using OSPF routing is connected directly to a DCF in a neighboring TMN entity that supports IP using IntISIS, the following function is required to be supported in the DCF supporting OSPF:

- IP Routing Interworking Function (as specified in Section 7.1.11)

## 6.2	ASTN Application

ASTN requires a communications network, which is referred to as the Signaling Communications Network (SCN) to transport signaling messages between ASTN components (e.g., CC components).

Figure 6-8 illustrates an example relationship of the SCN and the ASTN. The interfaces between the various elements and the SCN as illustrated in Figure 6-8 are logical and can be supported over a single physical SCN interface or multiple SCN interfaces.

Figure 6-9 illustrates an example of a physical implementation of a SCN supporting distributed signalling communications.  Depending on the choice of implementation of the SCN, the physical elements may support any combination of ECC interfaces, LAN interfaces, and WAN interfaces. Figure 6-9 also illustrates the types of control plane functional blocks that can be supported in various physical elements.  Refer to Recommendations G.8070 and G.8080 for detailed specifications regarding these control functional blocks.  A Data Communications Function (DCF) is part of each physical element and provides data communication functionality.

figure 6-8

Example Relationship of ASTN Interfaces to SCN

figure 6-9

Example of Physical Implementation of SCN Supporting ASTN

### 6.2.1	Topology of SCN

Figure 6-10 illustrates example topologies such as linear, ring, mesh, and star utilizing ECCs and/or Local Communication Networks (LCN) (e.g., Ethernet LAN) as the physical links interconnecting the Network Elements. Figure 6-11 illustrates how an ASTN Signalling Network could be supported on each topology.  Common to each topology is that alternate diverse paths exist between the communicating entities (i.e., the ASTN capable NEs).  Note that to support alternate diverse paths between communicating ASTN NEs under a linear topology, an external WAN link could be provided between the edge ASTN NEs.

Figure 6-10

Example Topologies

figure 6-11

Supporting an ASTN Signalling Network on Various Topologies

Figure 6-12 illustrates how the ASTN Signalling Network could consist of three different portions; the customer-network portion, the intra-administrative domain portion, and the inter-administrative domain portion. This example shows a mesh topology utilizing ECCs, Local Communication Networks (e.g., Ethernet LAN), and Leased Lines (e.g., DS1/E1, VC-3/4) as the physical links interconnecting the ASTN NEs.  The topology of the intra-administrative domain portion allows I-NNI signalling to have alternate diverse paths between two communicating ASTN NEs. The topology of the inter-administrative domain portion depends on agreements between Administrative Domains A and B. This example illustrates dual access points between the Administrative Domains. The topology of the Customer – Network portion depends on agreements between the customer and service provider. This example illustrates a single access point between the customer and the network.

figure 6-12

Example SCN

### 6.2.2	Reliability of SCN

Figure 6-13 illustrates ASTN control messages being transported over a SCN. The figure illustrates the following logical interfaces:

UNI – User - Network Interface.

NNI – Network - Network Interface.

CCI – Connection Controller Interface.

figure 6-13

ASTN Interfaces Supported on SCN

In this example, the UNI, NNI, and CCI logical interfaces are carried via the SCN network. The SCN may consist of various subnetworks, where logical links in some subnetworks may share common physical routes with the transport network but such is not required or excluded.

It is possible for the SCN to experience an independent failure from the transport network. Such a scenario is illustrated in Figure 6-14 and Figure 6-15. In this example, which focuses on ASTN messages transported over the SCN, an independent failure to the SCN would affect new connection set-up and connection tear-down requests.

figure 6-14

SCN Failure Impacting Signalling Interface

figure 6-15

SCN Failure Impacting CCI Interface

As indicated above, it is also possible for some logical links within the SCN to share common physical routes with the transport network. In this case, it is possible for the SCN to experience a failure that is not independent from the transport network (i.e., failure interrupts both SCN traffic as well as transport traffic), as shown in Figure 6-16. In this example, which focuses on ASTN messages transported over the SCN, such a failure may impact restoration when ASTN is used to provide restoration of existing connections. It is therefore critical for the SCN to provide resilliency when transporting restoration messages.

figure 6-16

SCN Failure Impacting Both Signalling and Data Interfaces

If the ASTN application is only used to provide connection-setup and teardown, a connection-less SCN may be sufficient. However, if the ASTN application is also used to provide restoration, a connection-oriented SCN may be required.  A connection-oriented SCN would require specification of additional functions to support connection-oriented network services.

The SCN reliability requirements are as follows:

The SCN shall support various levels of restoration depending on the reliability requirements of the communicating components for which it provides transport (i.e., restoration can be supported between those communicating components requiring highly reliable communications without requiring restoration to be supported among all communicating components).

The SCN may provide transport for restoration messages. In such a case the SCN shall provide restoration speeds, which allow proper operation of the connections for which the restoration messages control.

### 6.2.3	Security of SCN

A SCN supporting ASTN messages may provide connectivity between different administrative domains to support the transport of UNI or E-NNI messages (i.e., messages which cross administrative boundaries). I-NNI messages are only allowed within a single administrative domain.  When a SCN provides connectivity between administrative boundaries there must be precautions taken such that only those messages (e.g., E-NNI messages) that are allowed to pass between the two administrative domains are able to cross the interface while other messages which are not allowed to pass between administrative domains (e.g., I-NNI messages) are prevented from crossing the interface. Figure 6-17 illustrates an example where a SCN supporting the transport of ASTN messages is interconnected to multiple administrative domains.  The SCN needs to ensure that only a select set of messages which are allowed by the administrative parties on either side of the interface are actually able to pass across the interface.

figure 6-17

Security Aspects of SCN

### 6.2.4	SCN Data Communication Functions

The DCF within the ASTN entities shall support End System (ES) (in OSI terms) or Host (in IP terms) functionality.

- When the DCF within the ASTN entities support ECC interfaces, the following functions are required to be supported:

- ECC Access Function (as specified in Section 7.1.1)

- ECC Data-Link Termination Function (as specified in Section 7.1.2)

- [Network Layer PDU into ECC Data-Link Layer] Encapsulation Function (as specified in Section 7.1.3)

- When the DCF within the ASTN entities support Ethernet LAN interfaces, the following functions are required to be supported:

- Ethernet LAN Physical Layer Termination Function (as specified in Section 7.1.4)

- [Network Layer PDU into Ethernet Frame] Encapsulation Function (as specified in Section 7.1.5)

The DCF within the ASTN entities may operate as an Intermediate System (IS) (in OSI terms) or as a Router (in IP terms). The DCF within ASTN entities that operate as IS/Routers must be capable of routing within their Level 1 area and therefore must provide the functionality of a Level 1 IS/Router. Additionally, the DCF within an ASTN entity may be provisioned as a Level 2 IS/Router, which provides the capability of routing from one area to another. The functionality of a Level 2 IS/Router is not needed in the DCF of all ASTN entities.

- When the DCF within the ASTN entities operate as an IS/Router, the following functions are required to be supported:

- Network Layer PDU Forwarding Function (as specified in Section 7.1.6)

- Network Layer Routing Function (as specified in Section 7.1.10)

The DCF within a ASTN entity that supports IP may be connected directly to a DCF in a neighboring ASTN entity that supports only OSI.

- When the DCF within an ASTN entity that supports IP is connected directly to a DCF in a neighboring TMN entity that supports only OSI, the following function is required to be supported in the DCF supporting IP:

- Network Layer PDU Interworking Function (as specified in Section 7.1.7)

The DCF within a ASTN entity may have to forward a Network Layer PDU across a network that does not support the same Network Layer type.

- When the DCF within a ASTN entity must forward a Network Layer PDU across a network that does not support the same Network Layer type, the following functions are required to be supported:

- Network Layer PDU Encapsulation Function (as specified in Section 7.1.8)

- Network Layer PDU Tunneling Function (as specified in Section 7.1.9)

The DCF within a ASTN entity that supports IP using OSPF routing may be connected directly to a DCF in a neighboring ASTN entity that supports IP using IntISIS.

- When the DCF within an ASTN entity that supports IP using OSPF routing is connected directly to a DCF in a neighboring ASTN entity that supports IP using IntISIS, the following function is required to be supported in the DCF supporting OSPF:

- IP Routing Interworking Function (as specified in Section 7.1.11)

## 6.3	Other Applications Requiring Communication Networks

Besides TMN and ASTN applications, other applications such as voice communications (e.g., orderwire), software downloads, operator specific communications, require a communications network to provide transport of information between components.

## 6.4	Separation of Various Applications

Depending on the network design, network size, link capacity, security requirements and performance requirements, various levels of separation between the multiple applications (e.g., TMN, ASTN) are possible.  The level of separation that is provided is a choice that is made among operators and vendors when designing the network. The following are examples of various levels of separation.

Option A:  The DCN can be designed such that the MCN, SCN, and other applications (e.g., operator specific communications) are supported on the same layer 3 network (e.g., share the same IP network).

Option B:  The DCN can be designed such that the MCN, SCN, and other applications (e.g., operator specific communications) are supported on separate layer 3 networks, however they may share some of the same physical links.

Option C:  The DCN can be designed such that the MCN, SCN, and other applications (e.g., operator specific communications) are supported on separate physical networks (i.e., separate layer 3 networks that do not share any of the same physical links).

# 7	DCN Functional Architecture and Requirements

The DCN architecture requirements in this section apply to IP-only Domains, OSI-only Domains, and mixed IP+OSI domains.  The DCN architecture requirements are technology independent. Technology specific recommendations such as Recommendation G.784 for SDH and Recommendation G.874 for OTN will specify which requirements are applicable for that particular technology.

The DCN is aware of Layer 1, Layer 2, and Layer 3 protocols and is transparent to upper-layer protocols used by the applications for which it transports.

A DCN may be designed such that only IP is supported.  A DCN supporting only IP may consist of various subnetworks using different physical and data link layer protocols, however all subnetworks will support IP as the network layer protocol.

However, since embedded DCN networks support OSI, some DCNs may consist of parts that support IP-only, parts that support OSI-only, and parts that support both IP and OSI.

Those parts of the DCN supporting IP (i.e., either those parts supporting only IP or those parts supporting IP and OSI) may consist of DCFs that support IP-only (i.e., a single stack IP-only DCFs) and/or DCFs supporting IP and OSI (e.g., a dual-stack DCF which is capable of routing both IP and OSI packets).  Those parts of the DCN supporting only OSI, would consist of DCFs that support OSI-only (i.e., a single stack OSI-only DCF).

Figure 7-1 illustrates the functional architecture of the DCN.  As discussed above, the DCN may be composed of parts that only support IP, parts that only support OSI, and parts that support both IP and OSI.  An Inter-working Function (IWF) between those parts of the DCN supporting IP only, OSI only, and IP and OSI, and mapping functions which map applications to the IP layer are also specified. To provide such transport, the DCN supports Layer 1 (physical), Layer 2 (data-link), and Layer 3 (network) functionality. The architecture requirements for those parts of the DCN supporting IP only, OSI only as well as the requirements for inter-working between those parts of the DCN supporting IP only, OSI only, and IP and OSI) are specified. The cloud in Figure 7-1, representing the IP only part of the DCN, is an abstract view of the DCN and therefore may also apply to a single IP NE interconnected to OSI NEs via an IWF.

figure 7-1

Functional Architecture of DCN

## 7.1	Specification of Data Communication Functions

This section provides specifications for various data communication functions related to ECC interfaces, Ethernet LAN interfaces, and network layer capabilities.

### 7.1.1	ECC Access Function

An ECC Access Function provides access to the ECC bit stream. This function is defined in technology specific equipment recommendations (e.g., G.783, G.798).  The bit rates and definitions of the various ECCs (e.g., DCC, GCC, and COMMS OH in OSC) is provided in the technology specific recommendations (e.g., G.784, G.874).

### 7.1.2	ECC Data-Link Layer Termination Function

An ECC Data-Link Layer Termination Function provides the common data-link layer processing regardless of the network layer PDU encapsulated within the Data-Link Layer Frame. The mapping of the Data-Link Layer Frame into the ECC is also provided by this function. This function is specified in the technology specific recommendations. However, the specification for the SDH ECC Data-Link Layer Termination Function is provided below.

#### 7.1.2.1	SDH ECC Data-Link Layer Termination Function

##### 7.1.2.1.1	Mapping the SDH Data-Link Layer Frame into the ECC

The HDLC framed signal is a serial bit stream containing stuffed frames surrounded by one or more flag sequences. The HDLC framed signal format is defined in ITU-T Recommendation Q.921 for LAPD and RFC 1662 for PPP in HDLC framing.  A HDLC frame consists of N octets as presented in Figure 7-2.  The HDLC frame is transmitted right to left and top to bottom.  A 0 bit is inserted after all sequences of five consecutive 1 bits within the HDLC frame content (octets 2 to N-1) ensuring that a flag or abort sequence is not simulated within a frame.

The mapping of the HDLC framed signal into the DCC channel is bit-synchronous (rather than octet-synchronous) since the stuffed HDLC frame does not necessarily contain an integer number of octets as a consequence of the 0 insertion process.  Therefore there is no direct mapping of a stuffed HDLC frame into bytes within a DCC channel. The HDLC signal generator derives its timing from the ServerLayer/DCC_A function (i.e., the DCC_CI_CK signal) for SDH.  The following ServerLayer/DCC_A functions are defined in Recommendation G.783; MSn/DCC_A function, MS256/DCC_A function, and RSn/DCC_A function.

The HDLC frame signal is a serial bit stream and will be inserted into the DCC channel such that the bits will be transmitted on the STM-N in the same order that they were received from the HDLC frame signal generator.

figure 7-2

HDLC Frame Format

##### 7.1.2.1.2	SDH ECC Data-Link Layer Protocol Specification

The three types of interfaces identified are; IP-only interfaces, OSI-only interfaces, and Dual interfaces (Dual interfaces are interfaces that can carry both IP and OSI packets).  When carrying only IP over the DCC, PPPinHDLC framing shall be used as the data-link layer protocol.  Since Dual Interfaces can carry both IP and OSI, it is possible for a Dual Interface to be connected to either an IP-only interface, an OSI-only interface, or another Dual interface.  OSI-only interfaces exist in networks today, and the data-link protocol used on such interfaces is LAPD as defined in Recommendation G.784.  To allow Dual Interfaces to connect to either an IP-only interface or an OSI-only interface, the data-link layer protocol supported on a Dual Interface must be configurable to support either PPPinHDLC or LAPD.  An exception is allowed for embedded SDH NEs supporting LAPD in hardware that are upgraded to support Dual Interfaces.  To limit the amount of hardware upgrades it is allowed for upgraded SDH NEs to support only LAPD.

###### 7.1.2.1.2.1	IP-only Interface

IP-only interfaces are illustrated in Figure 7-3.

figure 7-3

IP-only Interface

IP-only interfaces shall use PPP as per RFC 1661.

###### 7.1.2.1.2.2	OSI-only Interface

OSI-only interfaces are illustrated in Figure 7-4.

figure 7-4

OSI-only Interface

OSI-only interfaces shall use LAPD as per Recommendation G.784.

###### 7.1.2.1.2.3	Dual Interface (IP + OSI)

Dual interfaces (Dual interfaces are interfaces that can carry OSI and IP packets) can be connected to IP-only interfaces, OSI-only interfaces, or other Dual interfaces.  To allow Dual interfaces to be connected to other IP-only interfaces or other OSI-only interfaces, the data-link protocol on the Dual interface must be configurable to switch between PPP in HDLC framing (as per RFC 1662) and LAPD (as per G.784) as illustrated in Figure 7-5.  Note that embedded SDH NEs supporting LAPD in hardware that are upgraded to support IP are not required to support PPP in HDLC framing on its dual interfaces.  Therefore its dual interfaces are only required to support LAPD.

figure 7-5

Dual Interface

Dual interfaces supporting PPP shall use PPP as per RFC 1661.

Dual interfaces supporting LAPD shall use LAPD as per Recommendation G.784.

### 7.1.3	[Network Layer PDU into ECC Data-Link Frame] Encapsulation Function

A [Network Layer PDU into ECC Data-Link Frame] Encapsulation Function encapsulates and unencapsulates the Network Layer PDU into the Data-Link Frame. This function also processes the protocol identifier. This function is defined in the technology specific recommendations. However, the specification for the [Network Layer PDU into SDH ECC Data-Link Frame] Encapsulation Function is provided below.

#### 7.1.3.1	[Network Layer PDU into SDH ECC Data-Link Frame] Encapsulation Function

The specification of the [Network Layer PDU into SDH ECC Data-Link Frame] Encapsulation Function for IP-only interfaces, OSI-only interfaces, and Dual Interfaces is provided below.

##### 7.1.3.1.1	IP-only Interface

IP-only interfaces must use only IP/PPPinHDLCframing/DCC as per RFC 1662.

An IP-only interface is defined as follows:

The Transmit End:

- Shall put IPv4 packets directly into PPP Information Field as per RFC 1661 with the IPv4 protocol value as per RFC 1332 into the PPP Protocol Field.

- Shall put IPv6 packets directly into PPP Information Field as per RFC 1661 with the IPv6 protocol value as per RFC 2472 into the PPP Protocol Field.

The Receive End:

- An IPv4 packet is identified if the PPP Protocol Field has the IPv4 protocol value as per RFC 1332.

- An IPv6 packet is identified if the PPP Protocol Field has the IPv6 protocol value as per RFC 2472.

##### 7.1.3.1.2	OSI-only Interface

OSI-only interfaces must use only OSI/LAPD/DCC as per Recommendation G.784.

An OSI-only interface is defined as follows:

The Transmit End:

- Shall put OSI packets directly into LAPD payload as per Recommendation G.784

The Receive End:

- Shall inspect the protocol identifier located in the first octet of the LAPD payload.  The value of this identifier is consistent with the values assigned in ISO 9577/ ITU-T X.263.  If the PDU received is for a protocol not supported by the receiver, then the PDU shall be discarded.

##### 7.1.3.1.3	Dual (IP+OSI) Interface

A Dual interface supporting PPP as the data-link protocol is defined as follows:

The Transmit End:

- Shall put OSI packets directly into PPP Information Field as per RFC 1661 with the OSI protocol value as per RFC 1377 into the PPP Protocol Field.

- Shall put IPv4 packets directly into PPP Information Field as per RFC 1661 with the IPv4 protocol value as per RFC 1332 into the PPP Protocol Field.

- Shall put IPv6 packets directly into PPP Information Field as per RFC 1661 with the IPv6 protocol value as per RFC 2472 into the PPP Protocol Field.

The Receive End:

- An OSI packet is identified if the PPP Protocol Field has the OSI protocol value as per RFC 1377.

- An IPv4 packet is identified if the PPP Protocol Field has the IPv4 protocol value as per RFC 1332.

- An IPv6 packet is identified if the PPP Protocol Field has the IPv6 protocol value as per RFC 2472.

A Dual interface supporting LAPD as the data-link protocol is defined as follows:

The Transmit End:

- Shall put OSI packets directly into LAPD payload as per G.784.

- Shall put IP packets directly into LAPD payload, with a one octet protocol identifier prepended.  This identifier will be consistent with the ISO 9577/ITU-T X.263 assigned values for IPv4 and IPv6.

The Receive End:

- Shall inspect the protocol identifier located in the first octet of the LAPD payload.  The value of this identifier is consistent with the values assigned in ISO 9577/ ITU-T X.263.  If the PDU received is for a protocol not supported by the receiver, then the PDU shall be discarded.

### 7.1.4	Ethernet LAN Physical Termination Function

An Ethernet LAN Physical Termination Function terminates the physical ethernet interface.

One or more of the following rates shall be supported: 1 Mbps, 10Mbps, 100 Mbps.

Access to terminated ECC channels is allowed by Network Elements supporting Ethernet LAN interfaces. Not all network elements supporting ECC channels need to support Ethernet LAN ports, as long as there is an ECC path from a Network Element terminating the ECC channel and another Network Element providing Ethernet LAN ports.

### 7.1.5	[Network Layer PDU into Ethernet Frame] Encapsulation Function

This function encapsulates and unencapsulates a Network Layer PDU into an 802.3 or Ethernet (version 2) frame.

It shall encapsulate Network Layer PDUs into 802.3 or Ethernet (version 2) frames according to the following rules.

- It shall encapsulate and unencapsulate CLNP, ISIS, and ESIS PDUs into 802.3 frames as per Recommendation Q.811.

- It shall encapsulate and unencapsulate IP packets into Ethernet (version 2) frames as per RFC 894.

- IP addresses shall be mapped to ethernet MAC addresses utilizing the Address Resolution Protocol in RFC 826.

It shall determine the received frame type (802.3 or Ethernet version 2) as per Section 2.3.3 in RFC 1122.

### 7.1.6	Network Layer PDU Forwarding Function

The Network Layer PDU Forwarding Function forwards network layer packets.

If this function forwards CLNP packets, it shall forward CLNP packets as per Recommendation Q.811.

If this function forwards IPv4 packets, it shall forward IPv4 packets as per RFC 791.

If this function forwards IPv6 packets, it shall forward IPv6 packets as per RFC 2460.

The preferred addressing format is IPv6. The IP routing protocol should be able to deal with IPv6 and IPv4 addressing.

### 7.1.7	Network Layer PDU Interworking Function

The Network Layer PDU Interworking Function ensures neighbouring DCF functions running different network layer protocols can communicate. The DCF supporting IP is required to support OSI to allow communication to the neighbouring DCF supporting only OSI.

### 7.1.8	Network Layer PDU Encapsulation Function

The Network Layer PDU Encapsulation Function encapsulates and unencapsulates one network layer PDU into another network layer PDU.

CLNP packets shall be encapsulated over IP using Generic Routing Encapsulation (GRE), as specified in RFC 2784, as payload in an IP packet using an IP protocol number of 47 (decimal) and with the DF (Don't Fragment) bit not set. As per RFC 2784, the GRE shall contain an Ethertype to indicate what network layer protocol is being encapsulated. The industry standard for OSI Ethertype, which is 00FE (hex) shall be used.

IP packets shall be encapsulated over CLNS using GRE, as specified in RFC 2784, as the data payload of a CLNP Data Type PDU as specified in ISO/IEC 8473-1, using an NSAP selector value of 47 (decimal) and with the SP (segmentation permitted) flag set.

IP packets shall be encapsulated over IP using GRE, as specified in RFC 2784, as payload in an IP packet using an IP protocol number of 47 (decimal) and with the DF (Don't Fragment) bit not set.

As an option, the Network Layer PDU Encapsulation function may forward PDUs across incompatible nodes via the automatic encapsulation procedure described in Annex B. Note that a DCF supporting the automatic encapsulation procedure described in Annex B is compatible with and can be deployed in the same area as a DCF that does not support the automatic encapsulation procedure.

### 7.1.9	Network Layer Tunneling Function

The Network Layer PDU Tunneling Function provides a static tunnel between two DCFs supporting the same network layer PDU.For a tunnel with a configured MTU size, any IP packet that cannot be forwarded over the tunnel because it is larger than the MTU size, and has its DF bit set, should be discarded, and an ICMP unreachable error message (in particular the “fragmentation needed and DF set" code) should be sent back to the originator of the packet.

### 7.1.10	Network Layer Routing Function

The Network Layer Routing Function routes network layer packets.

A DCF supporting OSI routing shall support ISIS as per ISO 10589.

A DCF supporting IP routing shall support Integrated ISIS (see Section 7.1.10.1 for Integrated ISIS requirements) and may also support OSPF as well as other IP routing protocols.

#### 7.1.10.1	Integrated ISIS Requirements

A DCF supporting Integrated ISIS shall support RFC 1195.

A DCF supporting Integrated IS-IS shall support Three-way Handshaking on all point-to-point links (see Annex A for Three-way Handshaking requirements).  Three-way handshaking modifies the adjacency creation and maintenance behaviour specified in ISO/IEC 10589.

##### 7.1.10.1.1	Network-layer Protocol Aware Adjacency Creation

The DCF shall include a “protocols supported” TLV in al IIH and ISH PDUs on all interfaces, and in all LSPs with LSP number 0, as per RFC 1195.

On receipt of an IS-IS ISH or IIH PDU the DCF shall inspect the PDU to see if it contains a “protocols supported” TLV.  This shall take place on all interfaces, whether LAN, DCC or other links.  If an ISH or IIH PDU does not contain a “protocols supported” TLV, then it shall be treated as if it contains a “protocols supported” TLV containing only the NLPID for CLNP.

The DCF shall compare the NLPIDs listed in the “protocols supported” TLV (assuming only CLNP if none is present) with the network layer protocols that the DCF is itself capable of forwarding.

If no adjacency exists with the neighbor that sent the ISH or IIH, and if the DCF is not capable of forwarding any of the network layer protocols listed in the “protocols supported” TLV of the ISH or IIH received from the neighbor, then the DCF shall not form an adjacency with that neighbor.

If an adjacency does exist with the neighbor that sent the ISH or IIH, and if the DCF is not capable of forwarding any of the network layer protocols listed in the “protocols supported” TLV of the ISH or IIH received from the neighbor, then the DCF shall delete the adjacency with that neighbor and generate a ProtocolsSupportedMismatch Event.

If the DCF is itself capable of forwarding one or more of the network layer protocols listed in the “protocols supported” TLV of a received ISH or IIH, then the DCF shall process the ISH or IIH as normal.

The DCF shall not consider the value of the “protocols supported” TLV of LSPs during this process.

A DCF that cannot forward CLNP PDUs shall ignore ESH PDUs and consequently shall not advertise reachability to OSI End Systems.

##### 7.1.10.1.2	ISIS Domain-wide IP Prefix Distribution

DCFs supporting Level-1, level-2 Integrated IS-IS shall support the advertising of configured IP destination prefixes learned via level-2 into level-1 LSPs, as well as IP destination prefixes learned via level-1 into level-2 LSPs. The default behaviour, when no IP destination prefixes have been configured, shall be to not propagate any level-2 prefixes into level-1 LSPs, while all Level-1 learned prefixes shall be propagated into level-2 LSPs.

###### 7.1.10.1.2.1	Configuration Prefixes

The operator shall provision two tables that control the propagation of prefixes. One table shall control propagation from Level-1 to Level-2, while the other controls propagation from Level-2 to Level-1.

###### 7.1.10.1.2.2	Tagging of Propogated Prefixes

Since propagating prefixes from Level-2 into Level-1 and subsequently from Level-1 back into Level-2 can introduce routing loops, a tag is necessary to identify the source of the prefix.  This tag, called the up/down bit, is stored in the previously unused high-order bit (bit 8) of the Default Metric field in IP Reachability TLVs and IP External Reachability TLVs.  Existing implementations of IS-IS that support RFC 1195 will not be impacted by the redefinition of this bit as RFC 1195 requires it to be set to zero when originating LSPs, and ignored upon receipt. Further information is available in RFC 2966.

IP Reachability TLVs and IP External Reachability TLVs shall be processed in the same manor.  The type of TLV received will be the same type used when the prefix is propagated from the Level-2 to a Level-1 area, as well as from a Level-1 area to the Level-2.

This is different than RFC 1195, which limited IP External Reachability TLVs to appearing only in level-2 LSPs.

7.1.10.1.2.2.1	Transmission of LSPs with IP Reachability TLVs and IP External Reachability TLVs

As with normal RFC 1195, the value of the up/down bit shall be zero for all IP TLVs in Level 2 LSPs.  The value of the up/down bit shall be zero for Level 1 LSPs originated within a Level 1 area.

The up/down bit shall be set to one in an IP TLVs in level-1 LSP when a Level-1,level-2 Integrated IS-IS NEs is propagating a configured prefix from level-2 to level-1.

7.1.10.1.2.2.2	Reception of LSPs with IP Reachability TLVs and IP External Reachability TLVs

A DCF supporting Integrated IS-IS shall ignore the value of the up/down bit when developing routes for use within a Level-1 area or for the Level-2.

A DCF supporting Level-1, Level-2 Integrated IS-IS that receives an LSP with an IP TLV for a prefix that matches an entry in the Level-1 to Level-2 Propagation table shall advertise the appropriate prefix from Level-1 to Level-2.

A DCF supporting Level-1, Level-2 Integrated IS-IS that receives an LSP with an IP TLV with the up/down bit set to one shall never use the prefix for propagation of information from Level-1 to Level-2.

7.1.10.1.2.2.3	Use the up/down bit in Level-2 LSPs

The use of up/down bit in Level-2 LSPs is for further study.

###### 7.1.10.1.2.3	Route Preference

Given that prefixes can now be propagated from Level-2 to Level-1, the Route Preferences specified in RFC 1195 must be updated to take into account this new source.  The resulting Route Preference order is as follows:

- L1 intra-area routes with internal metric
L1 external routes with internal metric

- L2 intra-area routes with internal metric
L2 external routes with internal metric
Inter-area routes propagated from L1 into the L2 with internal metric
Inter-area external routes propagated from L1 into the L2 with internal metric

- Inter-area routes propagated from L2 into an L1 area with internal metric
External routes propagated from L2 into an L1 area with internal metric

- L1 external routes with external metric

- L2 external routes with external metric
Inter-area external routes propagated from L1 into the L2 with external metric

- Inter-area external routes propagated from L2 into an L1 area with external metric

### 7.1.11	IP Routing Interworking Function

A DCF supporting the IP Routing Interworking Function shall support route filtering mechanisms per Sections 7.5 and 7.6 of RFC 1812 so that networks with two routing protocols can be connected via more than one exchange point.

### 7.1.12	[Applications to Network Layer] Mapping Function

OSI applications running over (a part of) the DCN that only supports IP may be mapped into IP as specified in the paragraph of Recommendation Q.811 dealing with RFC 1006/TCP/IP protocol profile. Such a mapping is a Layer 4 solution and is therefore outside the scope of this recommendation.  Another option for carrying OSI applications across (a part of) the DCN that only supports IP is to provide OSI over IP Layer 3 encapsulation as specified in Section 7.1.8.

The mapping of IP applications over (a part of) the DCN supporting IP shall be in accordance with IP suite specifications.

## 7.2	Provisioning Requirements

Every NE must support the creation of an interface that does not have any physical manifestation. This interface must be provisionable with an IP address.

The LSP size shall be configurable.

This allows the MTU size within the domain to be set.

Area ID provisioning per interface, including ECC channels and LAN, is required for OSPF.

## 7.3	Security Requirements

Care must be taken to avoid unwanted interactions (addresses, etc.) between a public IP network and a DCN supporting IP.

Annex A

Requirements for Three-way Handshaking

The Three-way handshaking procedure is based upon and designed to compatible with the IETF IS-IS Working Group’s Three-way Handshaking function.

A1	Point-to-Point Three-way Adjacency TLV

A DCF supporting Integrated IS-IS shall include a TLV in all point-to-point IIH PDUs. The structure of the TLV shall be:

Type = 0xF0 (decimal 240)

Length = 5 to 17 octets

Value:

Adjacency Three-way State (one octet):

0 = Up

1 = Initializing

2 = Down

Extended Local Circuit ID of four octets

Neighbor System ID of zero to eight octets if known

Neighbor Extended Local Circuit ID of four octets if known

The Extended Local Circuit ID shall be assigned by the DCF when the circuit is created, and the DCF shall use a different value for each point-to-point circuit that it has.

The Adjacency Three-way State reported in the TLV shall be as specified in Section A2.

A2	Adjacency Three-way State

A DCF supporting Integrated IS-IS shall for each point-to-point circuit have an adjacency three-way state. This state is different to the state specified in ISO/IEC 10589.

If no adjacency exists on a link then the adjacency three-way state shall be set to “Down”.

If a DCF receives an ISH on a point-to-point link and this results in a new adjacency being created with adjacency state “Initializing”, then the adjacency three-way state shall be set to “Down”.

If a DCF receives a point-to-point IIH that does not contain a three-way adjacency TLV, then the DCF shall behave as per ISO/IEC 10589, but shall include the TLV in IIH PDUs on that link reporting the adjacency three-way state as “Down”.

If a DCF receives a point-to-point IIH PDU that contains a three-way adjacency TLV, then the DCF shall behave differently to ISO/IEC 10589 IIH PDU processing as follows:

If the Neighbour System ID and the Neighbour Extended Local Circuit ID fields of the TLV are present and if either Neighbour System ID does not match the ID of the DCF, or the Neighbour Extended Local Circuit ID does not match the Extended ID of the DCF, then the IIH PDU shall be discarded and shall not be processed.

If the IIH PDU results in the ISO/IEC 10589 state tables producing an “Up” or “Accept”, and if the received Adjacency Three-way State is “Down”, then the DCF shall set its adjacency three-way state to “Initializing”.

If the IIH PDU results in the ISO/IEC 10589 state tables producing an “Up” or “Accept”, and if the received Adjacency Three-way State is “Initializing”, then the DCF shall change its adjacency three-way state from “Down” or “Initiailizing” to “Up” and generate an “AdjacencyChangeState(Up)” event.

If the IIH PDU results in the ISO/IEC 10589 state tables producing an “Up” or “Accept”, and if the received Adjacency Three-way State is “Initializing”, then if the DCF already has an adjacency three-way state of “Up”, it shall maintain the adjacency three-way state of “Up”.

If the IIH PDU results in the ISO/IEC 10589 state tables producing an “Up” or “Accept”, and if the received Adjacency Three-way State is “Up”, then if the DCF already has an adjacency three-way state of “Down”, it will generate an “AdjacencyStateChange(Down)” event with the reason “Neighbor restarted” and the adjacency shall be deleted with no further IIH PDU processing taking place.

If the IIH PDU results in the ISO/IEC 10589 state tables producing an “Up” or “Accept”, and if the received Adjacency Three-way State is “Up”, then if the DCF already has an adjacency three-way state of “Initializing”, then it will change its adjacency three-way state to “Up” and generate an “AdjacencyChangeState(Up)” event.

If the IIH PDU results in the ISO/IEC 10589 state tables producing an “Up” or “Accept”, and if the received Adjacency Three-way State is “Up”, then if the DCF already has an adjacency three-way state of “Up”, it shall maintain the adjacency three-way state of “Up”.

Following the comparison of source ID from the PDU with the local system ID and manipulation of the Circuit ID shall not be performed.

If the IIH PDU results in the ISO/IEC 10589 state tables producing an “Up” or “Accept” then the DCF shall:

copy the adjacency areaAddressOfNeighbour entries from the Area Addresses field of the PDU,

set the holdingTimer value of the Holding Time field from the PDU, and

set the neighbourSystemID to the value of the Source ID field from the PDU

as per ISO/IEC 10589.

Annex B

Requirements for Automatic Encapsulation

B1	Introduction

This document provides a specification for an InterWorking Function that enables nodes that support routing of differing incompatible network layer protocols, such as CLNS, IPv4 or IPv6 to be present in a single IS-IS level-1 area or level-2 subdomain, and which automatically tunnels one network layer protocol over another as required, provided that all of the nodes support IS-IS or Integrated IS-IS routing.

B2	Scope

This proposal applies only to protocols present in the embedded DCC channels that are found in SDH/SONET optical and electrical signals.  It does not necessarily apply to non-SDH/SONET routers that may be used between management workstations and SONET/SDH networks - what might be referred to as the ‘external’ or ‘access’ DCN.  However, it is possible that a router may be directly connected to the SDH/SONET network and may run Integrated IS-IS and act as an InterWorking Function instead of an SDH /SONET node.  In this case the external router effectively becomes part of the DCC network and this document applies to it.

B3	Definitions

  - InterWorking Function

An InterWorking Function is a function that enables a node to connect both to OSI nodes and to IP nodes. It also enables a node to forward and receive CLNS packets across IP capable nodes using RFC 1702 encapsulation and / or forward and receive IP packets across OSI capable nodes using RFC 3147 encapsulation.

- IP-only node

An IP-only node is a node that can natively route IP packets on any port but not CLNS packets. The term does not define whether the IP packets are IPv4 or IPv6.

- OSI-only node

An OSI-only node is a node that can natively route CLNS packets on any port but not IP packets.

- IP capable node

An IP capable node is a node that is able to route IP packets on any port, and may or may not be able to route CLNS packets too. The term does not define whether the IP packets are IPv4 or IPv6.

- OSI capable node

An OSI capable node is a node that is able to route CLNS packets on any port, and may or may not be able to route IP packets too.

- Dual node

A dual node is a node that can natively route two network layer protocols on any port. This term is typically used to indicate either a node that routes both CLNS and IPv4, or alternatively a node that routes both IPv4 and IPv6.

- Multilingual node

A multilingual node is a node that can natively route two or more network layer protocols natively on any port.

- Split stack node

A split stack node is a node that initiates and terminates packets of a network-layer protocol internally that is not available natively on its DCC channels.

B4	Abbreviations

CLNS	ConnectionLess mode Network Service

LSP	Link State Protocol Data Unit

IP	Internet Protocol

IS	Intermediate System

IS-IS	Intermediate System to Intermediate System

MTU	Maximum Transmission Unit

OSI	Open Systems Intercoonect

PDU	Protocol Data Unit

NLPID	Network-Layer Protocol Identifier

NSAP	Network Service Access Point

SID	System Identifier

SPF	Shortest Path First

TLV	Type Length Value

B5	References

[1]	RFC 1195 http://www.ietf.org/rfc/rfc1195.txt

[2]	ISO/IEC 10589

[3]	RFC 1702 http://www.ietf.org/rfc/rfc1702.txt

[4]	RFC 3147 http://www.ietf.org/rfc/rfc3147.txt

[5]	ISO/IEC 9542

[6]	ISO 9577 or ITU-T X.263

[7]	ITU-T G.7712

B6	Discussion

B6.1	Introduction

Integrated IS-IS as specified in RFC 1195 [1] was originally designed to be able to route IP and CLNS using a single routing protocol, and a single SPF algorithm. For this it represents IPv4 addresses and subnet masks as a 64 bit number which is then treated by the SPF algorithm as if it were an OSI End System address. Integrated IS-IS nodes are required to have an IS-IS Area Address and a System Identifier, which is treated in the same way as an NSAP address is in an OSI-only node. Integrated IS-IS nodes then form adjacencies and flood System Identifiers and metrics throughout their level-1 area (level-1 routers) or their level-2 subdomain (level-2 routers) in the same way as OSI-only IS-IS nodes.

SIDs (System Identifiers) and metrics to other SIDs are flooded throughout a level-1 area or level-2 subdomain using LSPs (Link State PDUs) that are common to both IS-IS and Integrated IS-IS nodes. IP specific information is then added to these LSPs using TLV extensions that are understood only by IP capable nodes. OSI-only routers cannot decode these TLVs but still flood them onwards to all of their adjacencies. In this way an SPF tree can be built by any IS-IS or Integrated IS-IS node whether it can route CLNS, IPv4 or IPv6. OSI-capable nodes will calculate shortest paths to OSI End Systems, IPv4-capable nodes will calculate shortest paths to IPv4 addresses or prefixes and IPv6-capable nodes will calculate shortest paths to IPv6 addresses or prefixes.

One consequence of this is that an OSI-only node will calculate a shortest path to an OSI End System that goes through an IP-only node, even though that IP-only node cannot forward CLNS packets. Similarly an IP-only node will calculate a shortest path to an IP destination that goes through an OSI-only node, even though the OSI-only node cannot forward IP packets. Thus an OSI-only capable node must not be placed in a part of a network where there is any possibility of it being on the shortest path to IP destinations, and an IP-only node must not be placed in a part of the network where there is any possibility of it being on the shortest path to an OSI End System.

The Integrated IS-IS algorithm can only use a single SPF algorithm for two or more network layer protocols due to an assumption that all network-layer protocols have access to the same resources, in other words the same network with the same topology. Thus Integrated IS-IS requires any node in a level-1 area or level-2 subdomain to be able to route any network layer protocol that is present in the area or domain respectively.

For this reason RFC 1195 [1] places topological restrictions on networks that are routed by Integrated IS-IS, requiring that all of the nodes support both IP and CLNS in an area that have both CLNS traffic and IP traffic present in them.

Consequently, according to RFC 1195 [1], if one node is upgraded and forwards IP packets, then all of the others in the level-1 area or level-2 subdomain must also be upgraded.

The solution proposed here allows this topological restriction to be removed, and it automatically encapsulates CLNS packets inside IP packets for forwarding across IP-only nodes and encapsulates IP packets inside CLNS packets for forwarding across OSI-only nodes. The solution proposed here is fully compatible with existing OSI-only nodes, which will not require any upgrade. It places one requirement upon IP-only nodes above those in RFC 1195 [1], but is required to be present on all dual or multilingual IP and OSI routers in a level-1 area or level-2 subdomain that employ the solution. Dual routers that support this feature may still be placed in a level-1 area or level-2 subdomain with other Integrated IS-IS nodes that do not support this feature, but in this case the topological restrictions of RFC 1195 [1] will then still apply.

B6.2	The Basic Concept

This feature takes advantage of the fact that all Integrated IS-IS and IS-IS nodes share basic topology information in the same way, and of the behaviour that OSI-only nodes will attempt to forward a packet across an IP-only node and vice versa, even though that node is incapable of actually forwarding the packet. Normally this would result in packet loss, but this InterWorking Function results in packets being encapsulated before being forwarded across incompatible nodes rather than being lost.

When two islands of IP capable Integrated IS-IS nodes are connected using a central network that supports only OSI, and if all of the nodes participate in the same area (for level-1 nodes), then the IP capable nodes will receive the LSPs from all of the other IP capable nodes, even those in the other island, as well as the LSPs from all of the OSI-only nodes in the middle. Thus they calculate shortest paths across the OSI-only nodes for all of the IP destinations in the island on the far side. It is only when an IP capable node actually forwards an IP packet to an OSI-only node that things go wrong, and the packet is lost. Hence the topological restrictions in RFC 1195 [1].

The above simple networks are illegal topologies according to RFC 1195 [1]. In the top network IP packets will be routed from one side of the network to the other, but on arrival at the OSI-only node will be discarded. Similarly on the bottom network CLNS packets will be routed from one side of the network to the other, but on arrival at the IP-only node will be discarded. The InterWorking Function specified here corrects this behaviour.

This InterWorking Function resides in the dual nodes, and enables them to recognise that a particular neighbour will discard certain traffic, and so to encapsulate it into a form that will not be discarded. This ‘repairs’ the network so that the part of network between the dual nodes acts as if it is comprised of all dual nodes, when in actual fact one or more of the nodes are not dual.

This InterWorking Function does not alter the path that a packet will take across the network; any individual packet will still cross the network using the shortest path as calculated by the normal IS-IS SPF algorithm.

This InterWorking Function does two basic things. Firstly it forces traffic to go through nodes that support both IP and OSI whenever the shortest path takes traffic across a boundary between IP capable and OSI capable parts of an area. Secondly it forces those dual nodes to encapsulate a packet if necessary so that it can be forwarded by nodes that do not support that network layer protocol. This encapsulation takes place only when necessary, and thus these tunnels are automatically created and are dynamic. The tunnels are not maintained in any way and exist only as entries in forwarding tables. Lastly as packets still cross the network along the shortest path that each node calculates normally, and as all of the nodes have a basic routing protocol in common, there is no need for IS-IS packets to traverse these tunnels, only IP and CLNS traffic is encapsulated.

B6.3	Requirements for OSI-only nodes

OSI-only nodes are required to be conformant to ISO/IEC 10589 [2].

B6.4	Requirements for IP-capable nodes

IP-only nodes are required to be conformant to RFC 1195 [1].

In particular, IP-capable nodes are required to ignore the “protocol supported” TLV in LSPs of nodes that they are considering as candidates for shortest paths when running the SPF algorithm.

An IP-capable node that only includes IP-capable nodes in its SPF calculation is not conformant to RFC 1195 [1], where it states:-

From page 26 of RFC 1195 [1]: “The Dijkstra computation does not take into consideration whether a router is IP-only, OSI-only, or dual. The topological restrictions specified in section 1.4 ensure that IP packets will only be sent via IP-capable routers, and OSI packets will only be sent via OSI-capable routers.”

The InterWorking Function described in this document is compatible with RFC 1195 implementations that conform to the above statement.  An implementation that only includes IP-capable nodes in its SPF calculation will not view automatically generated tunnels as being a suitable route, and so will not take advantage of this InterWorking Function.

One requirement in addition to RFC 1195 [1] is described below:-

This solution is dependant upon IP packets arriving at an OSI-only node only having first gone through a dual node, and upon CLNS packets arriving at an IP-only node only having first gone through a dual node. These dual nodes are then responsible for encapsulating these packets so that they can be forwarded.

Therefore an IP-only node must never have an adjacency with an OSI-only node.

If this solution is used to mix IPv4 and IPv6 nodes in the same level-1 area or level-2 subdomain then similarly an IPv4-only node must never have an adjacency with an IPv6-only node.

Thus Integrated IS-IS nodes are required to check whether a neighbouring node supports the network layer protocol that they support. If there is no network layer that both nodes support in common, then the node must refuse the adjacency.

Integrated IS-IS requires all Hello PDUs to contain a “protocols supported” TLV. This TLV must be inspected by nodes that conform with this document, and if none of the network layers that the node supports are listed, then the node must refuse the adjacency. Absence of the “protocols supported” TLV in a Hello PDU indicates that the neighbouring node is an OSI-only node.

This requirement has been addressed in the current version of G.7712 in section 7.1.10.1

Alternatively an operator may manually ensure that nodes that do not support a network layer protocol in common do not have adjacencies.

B6.5	Requirements for automatically encapsulating dual or multi-lingual nodes

If this feature is to be used in a level-1 area or level-2 subdomain then nodes that support more than one network layer protocol, but that do not have this InterWorking Feature may be used with caution. A safer alternative is to either to comply with the topological restrictions of RFC 1195, or to use only dual or multilingual nodes that contain this InterWorking Function.

B6.5.1	Encapsulation capability TLV

Dual or multilingual nodes that support this InterWorking Function will include a new TLV in LSPs with LSP number equal to zero. The new TLV will have the following structure:-

Code:	16 (decimal)

Length: The length of the value

Value:	A variable length part containing the following:-

Sub-TLV type:	1

Sub-TLV length:	3 times the number of encapsulation modes in the sub-TLV

Sub-TLV value:-

47 indicating that the next two bytes are a GRE encapsulation

The NLPID of a packet that may be encapsulated (inner)

The NLPID of a packet that transports the encapsulated packet (outer)

Bytes 4,5,6: 	A second encapsulation mode (if needed)

Bytes 7,8,9:	A third encapsulation mode (if needed)

Etc.

The NLPIDs that are used SHALL be those as specified in ISO 9577 [6].  Nodes that transmit this TLV SHALL indicate the formats that a node can both receive and transmit.  Nodes must be able to both automatically encapsulate and automatically unencapsulate the formats that are described in the TLV, so that traffic may be received and so that traffic may return in the reverse direction.

It is recommended that dual nodes are able to encapsulate/unencapsulate A over B, and B over A (where A and B are the two supported network layer protocols) making two encapsulation modes in a typical dual node.

For example the contents of the TLV for a typical OSI and IPv4 dual node will be:-

16: the code

8: the value length (in this example)

1: sub-TLV type 1

6: sub-TLV length (in this example)

47: next two bytes are a supported GRE mode

129: IPI for CLNP from ISO 9577

204: IPI for IPv4 from ISO 9577

47: next two bytes are a supported GRE mode

204: IPI for IPv4 from ISO 9577

129 IPI for CLNP from ISO 9577

An OSI, IPv4, IPv6 trilingual node will thus typically use six encapsulation modes to indicate CLNP over IPv4, CLNP over IPv6, IPv4 over CLNS, IPv4 over IPv6, IPv6 over CLNS, and IPv6 over IPv4, giving a value length of 20.

This TLV will not be included in pseudonode LSPs.

A dual node that does not have any IPv4 addresses must not place any encapsulation formats in its TLV of type equal 16 that include IPv4 as an encapsulation transport (outer) NLPID until such time as an IPv4 address is provisioned and advertised.

A dual node that does not have any IPv6 addresses must not place any encapsulation formats in its TLV of type equal 16 that include IPv6 as an encapsulation transport (outer) NLPID until such time as an IPv6 address is provisioned and advertised.

B6.5.2	Forwarding Process

As this InterWorking Function does not modify the path that a packet follows, a dual or multilingual node may calculate a shortest path for an IP packet that results in the next hop being an OSI-only node.

When this happens the dual or multilingual node must not simply forward a packet to an adjacent node that does not support that type of network layer protocol. Instead the dual or multilingual node must encapsulate the packet inside a new packet of a type that the next hop does support. The criteria for whether an adjacent node does or does not support a particular network layer protocol is whether that network layer protocol is listed in the “protocols supported” TLV in IS-IS Hello PDUs received from the node on the adjacency which is the next hop for that destination.

This new packet requires a network layer protocol, a destination address, and a source address to encapsulate the original packet.

The network layer protocol of the new packet must be one that is supported by the next hop as defined by the “protocols supported” TLV of Hello PDUs received from the next hop.

The destination address of the new packet must be equal to the identity of the next node along the shortest path to the original destination that has transmitted an encapsulation mode that has both the type of network layer protocol that the original packet is as the encapsulated (inner) NLPID, and a network layer protocol that is supported by the next hop (as defined by the “protocols supported” TLV of Hello PDUs received from the next hop) as the encapsulation transport (outer) NLPID.

This must be achieved by inspection of the new TLV of type equal to 16 from LSPs received from each node in the path to the destination, until the first is found that meets the above requirement.

When inspecting TLVs of type equal to 16, a node SHALL ignore any sub-TLVs that it does not understand, and shall jump to the next sub-TLV and SHALL inspect that, either until it finds all of the encapsulation modes that it is looking for, or until it reaches the end of the TLV.

The source address of the new packet must be equal to the identity of the node that constructs the new encapsulation packet.

If a dual or multilingual node can forward a packet without encapsulation because the next hop supports that type of packet, then the dual or multilingual node must forward the packet without encapsulating it.

A dual or multilingual node might send LSPs containing IP reachability from an IP-only node on to a split stack node or vice versa, and consequently might then be required to encapsulate packets headed for a split stack node, or unencapsulate packets received from a split stack node.

Thus a split stack node must also follow the same process of inspecting LSPs of nodes between itself and the destination looking for a node that has a suitable encapsulation format.

Note that a split stack node can receive an IPv4 packet only encapsulated inside CLNS for example. In this case the split stack node will transmit only “CLNS” in the “protocols supported” field of its Hello packets, and will only include one encapsulation mode in its TLV of type equal 16 in its LSPs. This single encapsulation mode will specify IPv4 as the encapsulated (inner) packet NLPID and CLNS as the encapsulation transport (outer) packet NLPID.

B6.5.3	Receipt Process

When a dual or multilingual node receives a packet that is destined for itself, it must inspect that packet to see if it has another packet encapsulated inside it. The resultant unencapsulated CLNS, IPv4 or IPv6 packet must then be forwarded as normal. If the resultant unencapsulated packet then contains another packet destined for this node then the process repeats; this is because multiple layers of encapsulation may require unencapsulation at a single node.

IS-IS packets are not compatible with IP packets and cannot be forwarded across the public Internet or other IP-only networks. This is a security advantage as it makes it difficult for a malicious entity to remotely launch IS-IS packets at IS-IS or Integrated IS-IS nodes across the public Internet. In order not to remove this advantage, then, if an IS-IS or ES-IS packet arrives encapsulated inside another packet destined for a node then the node must discard it, unless it came from a node with which this node has a manually provisioned tunnel with IS-IS provisioned to run across it. Optionally an error report may be raised informing the network manager of information such that a packet was received and dropped, where it came from, or that it is a potential malicious event.

All dual or multilingual nodes in a level-1 area or level-2 subdomain must support GRE encapsulation as specified in G.7712. Therefore a dual or multilingual node that supports OSI and IP must support encapsulation and unencapsulation of CLNS packets using RFC 1702 [3] and must support encapsulation and unencapsulation of IP packets using RFC 3147 [4]. A dual or multilingual node that supports IPv4 and IPv6 must support encapsulation and unencapsulation of IP packets using RFC 1702 [3] for encapsulation of IPv6 inside IPv4, or IPv4 inside IPv6.

B6.5.4	MTU Size and Fragmentation Requirements

The encapsulation of one packet inside another may result in a new packet that is longer than the MTU size of the link over which this new packet must be forwarded. This new RFC 1702 [3] or RFC 3147 [4] packet must not be discarded, therefore these packets must not have the Don’t Fragment bit set if they are IPv4 packets and must have the Segmentation Permitted flag set if they are CLNS packets.

The resultant encapsulation packets must then be fragmented before being forwarded if the packet is now longer than the MTU limit of the link.

It is not necessary to fragment a packet before encapsulating it, as the resultant encapsulation packet will be fragmented if necessary.

B6.5.5	Requirements for dual or multi-lingual nodes that broadcast (LAN) interfaces

B6.5.5.1	Psuedo-node election process

According to G.7712 [7], IP-only nodes are not allowed to form an adjacency with OSI-only nodes, and IPv4-only nodes are not allowed to form an adjacency with IPv6-only nodes.

Therefore when IP-only and OSI-only nodes are connected to the same LAN and in the same level-1 area or level-2 subdomain, then the IP-only nodes will form adjacencies with one another and will elect a pseudonode whilst the OSI-only nodes will form separate adjacencies and may well elect a different pseudonode. Therefore there may be two separate pseudonodes on the LAN, one for the OSI-capable nodes and one for the IP-capable nodes.

A similar thing may happen if IPv4-only and IPv6-only nodes are connected to the same LAN.

A dual or multilingual node must therefore take part in these separate pseudonode election processes independently for each network layer that it supports. A level-1/level-2 multilingual node must take part in two pseudonode election processes for each network layer protocol that it supports (one for level-1 and one for level-2).

Each pseudonode on the LAN residing on a node of a network layer protocol compatible with the multilingual node will have an adjacency with the multilingual node. Thus on an IP & OSI LAN the dual node will correctly be the one that has valid adjacencies both with the IP pseudonode and with the OSI pseudonode (if multiple pseudonodes are present on the LAN). The dual node will have an adjacency with the IP pseudonode and with the OSI pseudonode, but the IP pseudonode will not have a direct adjacency with the OSI pseudonode, and vice versa, but will instead gain connectivity only through the dual node.

A dual node may be elected as the Designated Router by the IP-capable nodes on the LAN, but not by the OSI-capable nodes; in this case the dual node must create a pseudonode, but the pseudonode must declare adjacencies in its LSPs ONLY with the IP-capable nodes on the LAN.

Similarly a dual node may be elected as the Designated Router by the OSI-capable nodes on the LAN, but not by the IP-capable nodes; in this case the dual node must create a pseudonode, but the pseudonode must declare adjacencies in its LSPS ONLY with the OSI-capable nodes on the LAN.

A dual node may be elected as the Designated Router both by the IP-capable and by the OSI-capable nodes on the LAN; in this case the dual node must create a pseudonode that declares adjacencies in its LSPs to all of the nodes on the LAN.

In essence a dual or multilingual node takes part in a separate election process for each network layer protocol that it supports, and if it wins any of the elections then it creates a pseudonode, but the pseudonode will declare adjacencies in its LSPs only with the set or sets of nodes that elected it.

Consequently OSI-only or IP-only nodes may receive LSPs from a pseudonode that lists adjacencies to nodes on the LAN that they cannot see. If a packet should need to be forwarded via such a node then it SHOULD be sent to the Designated IS as per ISO/IEC 10589 section C.2.5 item “h”, and as per RFC 1195 [1] section C.1.4 step 0 clause 8 on page 73.  Note that these clauses in ISO/IEC 10589 and RFC 1195 are non-normative.  It is possible that there are implementations that do not exhibit this behaviour.  Such an implementation will drop packets rather than send traffic to a dual node for automatic encapsulation, if the dual node is the Designated Router, and if non-compatible nodes on the same LAN are on the shortest path.

Implementers and operators therefore have a choice to make, the choice is:-

- Set the priority of dual or multilingual nodes to a high value. This results in single pseudonode appearing on the LAN, supported by a dual or multilingual node. The disadvantage of this approach is that there is a small chance that a legacy implementation exists on the LAN that does not forward traffic to a dual node if a non-compatible node on the LAN is on the shortest path.

Or

- Set the priority of dual or multilingual nodes to a low value. This results in one pseudonode appearing on the LAN for every network-layer protocol supported, explicitly sending traffic for non-compatible nodes through a dual or multilingual node.  This improves interoperability but doubles the amount of LSPs transmitted onto the LAN, reducing scalability.

It is recommended that the priority of dual and multilingual nodes is operator configurable.

B6.5.5.2	LSP update process

ISO/IEC 10589 [2] states in section 7.3.15.1 that an LSP received that does not come from a valid adjacency must be discarded.  A strict OSI-only implementation will therefore reject LSPs that are transmitted onto a LAN interface by an IP-only node, as the IP-only node has rejected the adjacency as per G.7712[7].  Thus the OSI-only node can receive such an LSP only from a dual node.  Without modified behaviour the dual node will only forward such an LSP during periodic LSP database synchronisation.

Dual or multilingual nodes that conform to this document are therefore required to have modified LSP flooding behaviour so that OSI-only or IP-only nodes do not need to wait for the next LSP database synchronisation event.

Dual or multilingual nodes that conform to this document must check incoming LSPs that arrive on LAN interfaces to see if they come from a neighbour that supports all of the network layer protocols that the dual or multilingual node does.  This must be achieved by inspection of the “protocols supported” TLV in Hello packets received from that neighbour.

If the LSP is received from a neighbour that does support all of the network layer protocols that the dual or multilingual node supports, then the dual or multilingual node shall behave as per ISO/IEC 10589 and unset the SRM flag for that LSP on that LAN interface if it already has the LSP, or shall flood it out of all other interfaces if it does not already have the LSP.

If the LSP is received from a neighbour that does not support all of the network layer protocols that the dual or multilingual node supports, and, if it does not already have the LSP then the dual or multilingual node shall set the SRM flag for that LSP on the LAN interface over which the LSP was received, in addition to all other interfaces, resulting in the dual or multilingual node re-transmitting the LSP onto the LAN.

In this way if an LSP is transmitted onto the LAN by an IP-only node, then one of the dual or multilingual nodes will re-transmit the LSP, so that it may be received on a valid adjacency by OSI-only nodes on the LAN and vice versa.

B6.5.5.3	Redirects

If a dual router originates an ICMP redirect request, the request must not redirect IP packets from an IP capable node to a non-IP capable node.  Likewise if a dual router originates ISO/IEC 9542[5] Redirect PDUs, the redirect must not redirect CLNS packets from an OSI capable node to a non-OSI capable node.

B6.5.5.4	Mixing of RFC 1195 only and automatically encapsulating nodes on a LAN

A dual node that is conformant to RFC 1195 [1] but not to this document must not reside on a LAN in the same level-1 area or level-2 subdomain as both IP-only and OSI-only nodes, as it may forward IP traffic to an OSI-only node, or CLNS traffic to an IP-only node, resulting in packet loss.

A dual node that is conformant to RFC 1195 [1] but not to this document may reside on a LAN in the same level-1 area or level-2 subdomain as a dual node supporting this InterWorking Function.

Additionally it may reside on a LAN with an OSI-only node if it can forward only CLNS traffic to that node, an IPv4-only node if it can forward only IPv4 traffic to that node, or an IPv6-only node if can forward only IPv6 traffic to that node.

B6.6	Requirements for split stack nodes

A split stack node initiates and terminates packets of a network-layer protocol type that it cannot forward natively in its DCC channels. Therefore the only way that such a node may initiate or terminate such packets is if they are in an encapsulated form.

This solution is particularly useful for adding an IP card into a predominantly OSI node, or a node that will be installed into an existing OSI network, for example. It may also be easier to upgrade an OSI gateway NE to a split stack node, rather than to a dual node, so that IP traffic can get in and out of the network for which the node is a gateway.

The split stack node must be able to internally route any packets that it receives that are of a network-layer protocol equal to one of those listed in the “protocols supports” TLVs of its IS-IS LSPs.

A split stack node must use the “protocols supported” TLV in IS-IS Hello PDUs to indicate only the network-layer protocols that it can receive and forward natively on any individual interface (or not support this TLV if it is an OSI-only interface).

i.e. an IP-over-OSI node can route CLNS natively in its DCC channels, and can route IP traffic that arrives for it in IP-over-OSI RFC 3147 tunnels, or possibly an Ethernet interface.

Thus a split stack node may indicate one network layer protocol in the “protocols supported” TLV of Hello packets on one interface, and a different network layer protocol in the “protocols supported” TLV of Hello packets on another interface.  Such a node would be able to route both network layer protocols internally, and so would advertise both in the “protocols supported” TLV of its LSPs.

A split stack node must use IP reachability TLVs in IS-IS LSPs to indicate the address range of encapsulated packets that it is able to terminate.

A split stack node might receive IP reachability extensions from an IP-only node, via a dual or multilingual node. Therefore the split stack node must be able to send traffic to a destination via a dual node, which it will use to unencapsulate its packets. To achieve this a split stack node must search for the next node along the path to each destination capable of unencapsulation, or for a split stack destination, in exactly the same way that a dual node does.

When a split stack node receives a packet that is destined for itself, it must inspect that packet to ascertain whether it has another packet encapsulated inside it. If so then the packet will be processed internally, unless it is an IS-IS or ES-IS packet in which case it must be discarded (unless a manually provisioned tunnel exists with IS-IS provisioned to run across it) in the same way as it would be by a dual node.

In the same way as a dual or multilingual node, a split stack node must support RFC 1702 [3] or RFC 3147 [4] encapsulation.

B6.7	Use of Integrated IS-IS nodes in mixed areas that do not conform to this document

Nodes that are conformant to RFC 1195 [1] but that are not conformant to this document may be used in mixed level-1 areas or level-2 subdomains with care with the restrictions below:-

Integrated IS-IS nodes that support only one network layer protocol but which do not conform with this document may still be used in an level-1 area or level-2 subdomain, but the network manager must manually ensure that such a node does not have any adjacencies with other nodes that might forward packets to it that it does not support.

Integrated IS-IS nodes (or clusters of nodes) that support more than one network layer protocol but which do contain the feature described in this document are still subject to the topological restrictions of RFC 1195. This means that the network manager must ensure that such a node cannot pass packets to a neighbouring node that cannot forward that type of packet.

i.e. dual(nc) signifies a dual Integrated IS-IS node that conforms to RFC 1195 [1], but that does not conform to this document

OSI----dual----dual(nc)----dual----IP is a safe combination

OSI----dual----dual(nc)----dual(nc)----dual(nc)----dual----IP is a safe combination

IPv4----dual----dual(nc)----dual----IPv6 is a safe combination

Dual(nc)----dual----OSI----dual----dual(nc) is a safe combination

OSI---IPv4&OSI---IPv4&OSI(nc)---IPv4&IPv6(nc)---IPv4&IPv6---IPv6 is not a safe combination

OSI--IPv4&OSI--IPv4&OSI(nc)--IPv4&IPv6&OSI--IPv4&IPv6(nc)--IPv4&IPv6--IPv6 is a safe combination

B6.8	Requirements for level 1, level 2 nodes

It is recommended that nodes that support both level-1 and level-2 routing, and that are present in a level-1 area or level-2 subdomain in which this InterWorking Function is used either:-

Support all network layer protocols that are present in both the level-1 and the level-2 subdomain in which the node participates and support the features described in this document.

or

Support all network layer protocols that are present in both the level-1 and the level-2 subdomain in which the node participates and be either directly connected to, or connected through continuous strings of other nodes that support all network layer protocols in the area, to a node that supports this feature and that supports all of the network layer protocols in the area.

i.e. (nc) signifies an Integrated IS-IS node that conforms to RFC 1195 [1], but that does not conform to this document:-

L2_subdomain----dualL1/L2----any_node is safe

L2_subdomain----dualL1/L2(nc)----dual---any_node is safe

L2_subdomain----dualL1/L2(nc)----dual(nc)----dual---any_node is safe

L2_subdomain----dualL1/L2(nc)----non-dual is not safe (unless RFC 1195 [1] restrictions apply)

However, it is understood that a gateway, and therefore a L1,L2 router, may be an existing OSI-only device. In this case it is possible to have IP and autoencapsulation in the area by using the following method, with care:-

One or more dual nodes in the area may be chosen as gateways for IP packets. These nodes will be configured to advertise a default route (0.0.0.0) into the area to attract all “out of area” IP traffic to them. These nodes will then forward all “out of area” traffic across a manually provisioned RFC 3147 tunnel, which passes through the level-1,level-2 OSI-only node to another dual node outside of the area.

The dual node that is outside of the area must have a prefix manually provisioned into it to attract all IP traffic bound for the area to it, and send it over the tunnel into the area. Optionally a mechanism, such as an IP routing protocol may be provisioned across the tunnel so that each end may see if the other is alive; however if Integrated IS-IS is used then it must be a different routing instance to that used generally in the area, as it is effectively a different routeing domain.

If such a mechanism is used then if the far end disappears, the dual node inside the area should stop advertising a default route, and the dual node outside of the area should stop advertising the prefix that represents the nodes in the area. In this way redundant IP gateways can be provisioned.

Note that RFC1195 [1] states that default routes should not be advertised within level-1 LSPs. This solution requires that this rule be broken.  Normally a level-1 RFC 1195 node would consider a level-1,level-2 node to be its default route. This solution requires that this behaviour be overwritten by receipt of a default route advertisement in a level-1 LSP. If this is not possible then a work-around is for the IP gateway nodes to be configured with a selection of static routes that cover all possible “out of area” destinations that an IP stack in the area is likely to try to reach.

B6.9	Requirements for the level 2 subdomain

It is acceptable to route all protocols present natively in the level-2 subdomain, as per RFC 1195 [1], in which case none of the level-2 nodes need to support this InterWorking Function, but all of them must support all of the network layer protocols present.

Alternatively it is acceptable to use level-2 nodes that support less than all of the network layer protocols present in the domain, in which case the level-2 dual or multilingual nodes will be required to support this InterWorking Function so that packets may be automatically encapsulated in order to pass through such nodes.

APPENDIX I

Constraints of the Interworking Functions in DCN

(This Appendix does not form an integral part of this Recommendation)

figure i-1

Interworking Scenarios

General Assumptions:

DCN covers the IWF for layer 2-3 of the IP-OSI stacks. Interworking mechanisms that apply to other layers are out of the scope of this recommendation (i.e. mediation).

-See section 7.1.7 for a definition of interworking.

Tunnels are based on RFCs.

The IP-only NE’s support IP routing and may contain redistribution between integrated ISIS and OSPF

Common to all scenarios:

Dynamic routing is accomplished through the use of route redistribution of IP address information between OSPF and ISIS NE’s.   Route redistribution is preformed on the OSPF nodes between the pairs; (R,P), (S,C), (M,K), (N,L).

Scenario 1: OSI based management system connected to node A:

There must be at least one tunnel configured from B to one or more of Y or Z.

There must be a tunnel configured from B to X.

There must be a tunnel configured from B to F

There must be at least one tunnel configured from B to one or more of W, V or T.

The above tunnels will probably have IS-IS running across them (inside the tunnel), however inter-domain routing techniques is also a possibility. Under some conditions some tunnels could become congested as a result of routing choices.

An OSI based management system now has CLNS connectivity to any OSI-only or dual stack NE in the network, but does not have connectivity with IP-only NEs. Although an OSI based manager will be able to sent CLNS packets to a dual stack NE, it will not be able to manage it unless it is OSI manageable.

Scenario 2: IP based management systems connected to node B.

In this particular network, IP traffic can be forwarded from B to all IP NEs without requiring tunnels. OSPF NEs P, C, M, and N  must support redistribution of IP routes into Integrated IS-IS. Filters will have to be configured on OSPF nodes P, C, M, and N in order to stop routing loops from forming.

An IP based management system now has IP connectivity to any IP-only or dual stack NE in the network, but does not have connectivity with OSI-only NEs. Although an IP based manager will be able to send IP packets to a dual stack NE, it will not be able to manage it unless it is IP manageable.

Scenario 3: OSI based management systems connected to node C.

NE C cannot provide OSI connectivity, and so CLNS packets cannot be forwarded, therefore an OSI based management system cannot function at this location.

Scenario 4: IP based management systems connected to node E.

NE E cannot provide IP connectivity, and so IP packets cannot be forwarded, therefore an IP based management system cannot function at this location.

Scenario 5: OSI based management systems connected to node F.

CLNS traffic can pass through NE F to OSI network 2 without requiring tunnels as NE F can forward CLNS packets natively.

There must be a tunnel configured from F to B.

There must be at least one tunnel configured from F to one or more of Z or Y.

There must be a tunnel configured from F to X.

There must be at least one tunnel configured from F to one or more of W, V or T.

The above tunnels will probably have IS-IS running across them (inside the tunnel), however interdomain routing techniques are also a possibility. Under some conditions some tunnels could become congested as a result of routing choices.

An OSI based management system now has CLNS connectivity to any OSI-only or dual stack NE in the network, but does not have connectivity with IP-only NEs. Although an OSI based manager will be able to sent CLNS packets to a dual stack NE, it will not be able to manage it unless it is OSI manageable.

Scenario 6: IP based management systems connected to node G.

In this particular network, IP traffic can be forwarded from G to all IP NEs without requiring tunnels. OSPF NEs P, C, M, and N must support redistribution of IP routes into Integrated IS-IS. Filters will have to be configured on each OSPF nodes P, C, M, and N in order to stop routing loops from forming.

An IP based management system now has IP connectivity to any IP-only or dual stack NE in the network, but does not have connectivity with OSI-only NEs. Although an IP based manager will be able to send IP packets to a dual stack NE, it will not be able to manage it unless it is IP manageable.

APPENDIX II

Example implementation of Automatic Encapsulation

1. Introduction

This appendix is not a requirement but gives brief example details on how a node may be implemented with respect to one aspect of the feature specified in this document.

The simplest way (but not the only way) for a node to calculate the next node along the shortest path to the final destination of a packet that can unencapsulate is to modify the SPF algorithm to achieve this.

The algorithm can be modified to find the next node along the shortest path to the destination that can accept IP over OSI encapsulated traffic, and the next node along the shortest path to the destination that can accept OSI over IP encapsulated traffic.  Note that these two may be the same node, or may be two separate nodes.   A modified Dijkstra algorithm is provided below that achieves this.

This additional process only need happen when the next hop does not support the network layer protocol of the type that corresponds to the destination address for that path. If the next hop does support that type of network layer protocol (as specified in the “protocols supported” TLV present in IS-IS Hello PDUs received from that node) then packets to that destination may simply be forwarded natively and forgotten, and so the search for a node along the path that can unencapsulate is not necessary.

The algorithm must then identify an IP address for this next unencapsulation node if the destination of the path is an OSI End System, and must then identify an OSI address for this next unencapsulation node if the destination of the PATH is an IP address.

Failure to find an IP address for this next unencapsulation node indicates a configuration error in that node (no IP address); this may optionally result in an error message being sent to the network administrator. Packet loss will result if a CLNS packet requires tunnelling to that node over IP, as without an IP destination address encapsulation may not be possible and the packet will be discarded instead.

Failure to find a node that can unencapsulate indicates a network design error, more specifically a failure to conform to the topological restrictions stated in this document.  This should result in a “destination unreachable” error report.

For each IP destination that requires encapsulation to get beyond the next hop, the node can then put a marker in the IP forwarding table indicating the OSI destination address that must be used to encapsulate all IP packets destined for that address.

For each OSI destination that requires encapsulation to get beyond the next hop, the node can then put a marker in the OSI forwarding table indicating the IP destination address that must be used to encapsulate all OSI packets destined for that address.

A node that supports IPv4, IPv6 and OSI may find two addresses (for example an IPv4 address and an IPv6 address) that could be used to encapsulate. In this case it may choose either as long as it results in a packet that is of a network layer protocol type that the next hop supports (as specified in the “protocols supported” TLV present in IS-IS Hello PDUs received from that node).

2. Updates to Dijkstra’s Algorithm

The following appendix contains the full Dijkstra’s algorithm including extensions to support auto-tunnelling.  It is based on the algorithm as specified in RFC1195.  The algorithm shown is suitable for a dual IPv4 and CLNS auto-tunnelling node.  Changes to this algorithm are shown in Bold Italic

The algorithm produces a PATHS database containing for each destination the identity of the first node from S to N capable of unencapsulating IP over OSI and the identity of the first node from S to N capable of unencapsulating OSI over IP.

For each IP destination, the first node from S to N capable of unencapsulating IP over OSI may have its OSI address loaded into the IP forwarding table as the destination address to be used in any CLNP packet used to encapsulate IP over OSI, if the next hop does not support IP.

For each OSI End System, the first node from S to N capable of unencapsulating OSI over IP may have one of its IP addresses loaded into the OSI forwarding table as the destination address to be used in any IP packet used to encapsulate OSI over IP, if the next hop does not support OSI.

2.1 Changes to Database

The PATHS and TENTS database should be updated to contain an extension to the {Adj(N)}, element of the triple. The adjacency N element will contain two corresponding Dual Protocol Support (IDP(N)-ODP(N)) entries which will represent the System ID of the first Dual router on the path from S to N capable of de-encapsulating IP over OSI tunnelled packets (IDP(N)) and the System ID of the first dual router on that path from S to N capable of de-encapsulating OSI over IP tunnelled packets (ODP(N). If no *DP(N) router exists on the PATH then this value will be set to zero. If multiple Adj(N) entries exist in either the TENTS or the PATHS database then each adjacency will have corresponding *DP(N) entries. Thus each triple will take the format <N,d(N),{Adj(N)-IDP(N)-ODP(N)}>

If the value of IDP(N) is set to 0 then this means that no dual router exists on the path to the destination capable of de-encapsulating and encapsulating IP over OSI packets.

If the value of ODP(N) is set to 0 then this means that no dual router exists on the path to the destination capable of de-encapsulating and encapsulating OSI over IP packets.

2.2 Changes to Algorithm

The SPF algorithm specified in section C.2.3 of [1] is amended to appear as follows:

Step 0: Initialize TENT and PATHS to empty. Initialize tentlength to

[internalmetric=0, externalmetric=0].

(tentlength is the pathlength of elements in TENT that we are

examining.)

1) Add <SELF,0,W-0-0> to PATHS, where W is a special value indicating

traffic to SELF is passed up to internal processes (rather than

forwarded).

2) Now pre-load TENT with the local adjacency database (Each

entry made to TENT must be marked as being either an End System

or a router to enable the check at the end of Step 2 to be made

correctly - Note that each local IP reachability entry is

included as an adjacency, and is marked as being an End System).

For each adjacency Adj(N) (including level 1 OSI Manual

Adjacencies, or level 2 OSI enabled reachable addresses, and

IP reachability entries) on enabled circuits, to system N of

SELF in state "Up" compute:

d(N) = cost of the parent circuit of the adjacency (N),

obtained from metric.k , where k = one of {default metric,

delay metric, monetary metric, error metric}

Adj(N)-IDP(N)- ODP(N) = the adjacency number of the adjacency to N ,

the SID of the next-hop router along the path to the neighbour capable of

de-encapsulating IP over OSI packets and the SID of the next-hop router

along the path to the neighbour capable of de-encapsulating OSI over IP packets .

In this case i.e. during initialisation both DP values will be set to 0

3) If a triple <N,x,{Adj(M)-IDP(N)-ODP(N)}> is in TENT, then:

If x = d(N), then {Adj(M)-IDP(N)-ODP(N)} <--- {Adj(M)-IDP(M)-ODP(M)}

U {Adj(N)-IDP(N)-ODP(N)}.

4) If N is a router or an OSI End System entry, and there are now

more adjacencies in {Adj(M)} than maximumPathSplits, then remove

excess adjacencies as described in Clause 7.2.7 of [1]. If N

is an IP Reachability Entry, then excess adjacencies may be

removed as desired. This will not effect the correctness of

routing, but may eliminate the determinism for IP routes (i.e.,

IP packets still follow optimal routes within an area, but

where multiple equally good routes exist, will not necessarily

follow precisely the route that any one particular router

would have anticipated).

5) If x < d(N), do nothing.

6) If x > d(N), remove <N,x,{Adj(M)-IDP(M)-ODP(M)}> from TENT and add the triple

<N,d(N),{Adj(N) -IDP(N)-ODP(N)}>.

7) If no triple <N,x,{Adj(M) -IDP(M)-ODP(M) }> is in TENT, then add

<N,d(N),{Adj(N) -IDP(N)-ODP(N)}> to TENT.

8) Now add systems to which the local router does not have adjacencies,

but which are mentioned in neighbouring pseudonode LSPs. The

adjacency for such systems is set to that of the designated router.

Note that this does not include IP reachability entries from

neighbouring pseudonode LSPs. In particular, the pseudonode LSPs

do not include IP reachability entries.

9) For all broadcast circuits in state "On", find the pseudonode

LSP for that circuit (specifically, the LSP with number zero and

with the first 7 octets of LSPID equal to LnCircuitID for that

circuit, where n is 1 (for level 1 routing) or 2 (level 2

routing)). If it is present, for all the neighbours N reported in

all the LSPs of this pseudonode which do not exist in TENT add

an entry <N,d(N),{Adj(N) -IDP(N)-ODP(N)}> to TENT, where:

d(N) = metric.k  of the circuit.

Adj(N) = the adjacency number of the adjacency to the DR.

10) Go to Step 2.

Step 1: Examine the zeroeth link state PDU of P, the system just

placed on PATHS (i.e., the LSP with the same first 7 octets of LSPID

as P, and LSP number zero).

- If this LSP is present and the “Infinite Hippity Cost” bit is clear

For each Adj(*) – IDP(*) – ODP(*) pair in the PATHS database for P.

If this is not a pseudo-node LSP and if IDP(*) is equal to zero then check

the unencapsulation capability field of the LSP, if it supports IP over OSI

then set the IDP(P) value for this adjacency to be the system ID of P.

if ODP(*) is equal to zero then check

the unencapsulation capability field of the LSP, if it supports OSI over IP

then set the IDP(P)value for this adjacency to be the system ID of P

2) If this LSP is present, and the "Infinite Hippity Cost" bit is

clear, then for each LSP of P (i.e., all LSPs with the same

first 7 octets of LSPID and P, irrespective of the value of

LSP number) compute:

dist(P,N) = d(P) + metric.k(P,N)

for each neighbour N (both End System and router) of the system P. If

the "Infinite Hippity Cost" bit is set, only consider the End System

neighbours of the system P.

Note that the End Systems neighbours of the

system P includes IP reachable address entries included in the LSPs

from system P. Here, d(P) is the second element of the triple

<P,d(P),{Adj(P)-IDP(P)-ODP(P)}>

and metric.k(P,N) is the cost of the link from P to N as reported in

P's link state PDU.

3) If dist(P,N) > MaxPathMetric, then do nothing.

4) If <N,d(N),{Adj(N) – IDP(N)-ODP(N)}> is in PATHS, then do nothing.

Note: d(N) must be less than dist(P,N), or else N would not

have been put into PATHS. An additional sanity check may be

done here to ensure that d(N) is in fact less than dist(P,N)

6) If a triple <N,x,{Adj(N) -IDP(N)-ODP(N)}> is in TENT, then:

a) If x = dist(P,N), then {Adj(N), IDP(N)-ODP(N)} <--

{Adj(N) -IDP(N)-ODP(N)} U {Adj(P) -IDP(P)-ODP(N)}.

Note that even if the value of Adj(N) is equal to the value Adj(P)

but the corresponding values of either IDP(P) or ODP(P) and IDP(N)

or ODP(N) are different

then this should be treated as a different adjacency and will represent

a different path to the destination.

b) If N is a router or an OSI end system, and there are now more

adjacencies in {Adj(N)} than maximumPath Splits, then remove

excess adjacencies, as described in clause 7.2.7 of [1]. For

IP Reachability Entries, excess adjacencies may be removed as

desired. This will not effect the correctness of routing, but

may eliminate the determinism for IP routes (i.e., IP packets

will still follow optimal routes within an area, but where

multiple equally good routes exist, will not necessarily follow

precisely the route that any one particular router would have

anticipated).

c) if x < dist(P,N), do nothing.

d) if x > dist(P,N), remove <N,x,{Adj(N)- IDP(N)-ODP(N)}> from TENT, and add

<N,dist(P,N),{Adj(P)- IDP(P)-ODP(P)}>

7) if no triple <N,x,{Adj(N)}> is in TENT, then add

<N,dist(P,N),{Adj(P)}> to TENT.

Step 2: If TENT is empty, stop. Else:

1) Find the element <P,x,{Adj(P)-IDP(P)-ODP(P)}>, with minimal x as follows:

a) If an element <*,tentlength,*> remains in TENT in the list for

tentlength, choose that element. If there are more than one

elements in the list for tentlength, choose one of the elements

(if any) for a system which is a pseudonode in preference to one

for a non-pseudonode. If there are no more elements in the list

for tentlength, increment tentlength and repeat Step 2.

b) Remove <P,tentlength,{Adj(P)-IDP(P)-ODP(P)}> from TENT.

c) Add <P,d(P),{Adj(P) -IDP(P)-ODP(P)}> to PATHS.

d) If this is the Level 2 Decision Process running, and the system

just added to PATHS listed itself as Partition Designated Level 2

Intermediate system, then additionally add <AREA.P,d(P),{Adj(P)}>

to PATHS, where AREA.P is the Network Entity Title of the other

end of the Virtual Link, obtained by taking the first AREA

listed in P's LSP and appending P's ID.

e) If the system just added to PATHS was an end system, go to

step 2. Else go to Step 1.

NOTE - In the level 2 context, the "End Systems" are the set of

Reachable Address Prefixes (for OSI), the set of Area Addresses with

zero cost (again, for OSI), plus the set of IP reachability entries

(including both internal and external).

APPENDIX III

Commisioning Guide for SDH NEs in Dual RFC 1195 Environment
and Impact of Automatic Encapsulation Option

1. Introduction

This appendix provides guidance on installing Integrated IS-IS nodes in a dual IPv4 and OSI network, and on how to use the optional automatic encapsulation feature described in Annex B.

2. Integrated IS-IS without automatic encapsulation

2.1 Introduction and Rules of RFC 1195

Integrated IS-IS as specified in RFC 1195 [1] was originally written as a dual routing protocol.  Specifically it was written to be able to route both IPv4 and CLNP using a single SPF calculation, a single set of metrics for both IP and CLNP, and, a single set of Hellos and LSPs.

More specifically, Integrated IS-IS routers conforming to RFC 1195[1] calculate shortest paths across a level-1 area or level-2 sub-domain without considering whether any candidate router can actually forward a specific type of packet.

This is clearly stated in RFC 1195 [1] in section 3.10:-

"The Dijkstra computation does not take into consideration whether a router is IP-only, OSI-only, or dual. The topological restrictions specified in section 1.4 ensure that IP packets will only be sent via IP-capable routers, and OSI packets will only be sent via OSI-capable routers."

With Integrated IS-IS, a router is just a router.  The assumption is that any router in the network can handle any type of packet that is thrown at it.

Therefore Integrated IS-IS routers calculate routes, and forward packets based on this assumption, and it is the responsibility of an operator to make sure that the assumption is actually true.

Thus there are the topological restrictions of RFC 1195.  Failure to enforce the topological restrictions of RFC 1195 may result in packet loss, as packets disappear into the black-hole of a router that simply discards packets that it cannot forward, as it does not support them.

In a simple single level-1 area network, the rules are quite simple.  These are:-

1.	If IPv4 packets are to be forwarded in an area, then all of the routers in the area must be able to forward IPv4 packets.

2.	If CLNP packets are to be forwarded in an area, then all of the routers in the area must be able to forward CLNP packets.

3.	If both IPv4 and CLNP packets are to be forwarded in an area, then all of the routers in the area must be dual, i.e. able to forward both.

Thus it is fairly easy to classify IS-IS level-1 areas into the classes "OSI-only area", IP-only area", and "Dual area".

This is shown in figure 1.

Figure 1

2.2 Level 2 Subdomain

If a larger network is needed, requiring level-2 routing, then the level-2 subdomain forwards packets between the level-1 areas, and thus must support all of the types of packet present in all of those level-1 area.  The rules for the level-2 subdomain are:-

1.	If IPv4 packets are forwarded in any of the areas (IP-only or Dual areas), then all of the routers in the level-2 subdomain must be able to forward IPv4.

2.	If CLNP packets are forwarded in any of the areas (OSI-only or Dual areas), then all of the routers in the level-2 subdomain must be able to forward CLNP.

Therefore, if any of the areas are dual, or if both OSI-only and IP-only areas exist, then, the routers in the level-2 subdomain must be dual.  This is illustrated in figure 2.

Figure 2

2.3 Level 2 Subdomain with External Routers running Integrated IS-IS

Many operators currently run level-1 IS-IS routing in their OSI-only SDH NEs, and then link up multiple areas using level-2 IS-IS routing in an external router network.

If an operator wishes to use a similar model for a dual network then they can run level-1 Integrated IS-IS in each area, and level-2 Integrated IS-IS in an external router network.  This gives a very similar network to the previous one, as shown in Figure 3

Figure 3

2.4 External Routers running OSPF or other IP Routing Protocols

Many operators currently run level-2 IS-IS in their external routers, and OSPF or other routing protocols for IP.  In this case the external router must remain as the level-2 router for the SDH NEs, and so for a dual area must be a dual Integrated IS-IS router.  However the router may be configured to route all IP packets using OSPF by configuring redistribution of IP routes between IS-IS and OSPF.  In this way all IP packets will be OSPF routed, whilst CLNP packets continue to be level-2 IS-IS routed.  This is shown in figure 4.

Figure 4

Note that the Integrated IS-IS stack in the external routers will not be aware that the level-2 subdomain is meant only for CLNP packets.  The OSPF learned routes must therefore be redistributed into Integrated IS-IS with a low default metric, to make them more attractive to IP packets than the level-2 sub-domain.

3. Integrated IS-IS with Automatic Encapsulation

3.1 Introduction and Affect on Topological Restrictions

The automatic encapsulation option allows the topological rules of RFC 1195 to be broken.  Automatic encapsulation effectively makes a node, or group of nodes appear to be able to forward packets that actually they cannot.

This is shown in figure 5.

Figure 5

This group of nodes will now forward both IPv4 and CLNP packets, as long as the packets enter at point A or B, through one of the automatically encapsulating nodes.

The group of nodes may now safely be put into a dual area or a dual level-2 subdomain, as the pair of automatically encapsulating nodes will forward IPv4 packets by encapsulating them inside CLNP packets, so that they will be forwarded by the OSI-only NEs rather than being discarded.

A valid dual area may now look something like that shown in figure 6.

Figure 6

Note that the OSI-only nodes must not be directly connected to one of the dual nodes that do not have the automatic encapsulation option.  It is only the presence of the automatic encapsulating nodes that prevent IPv4 packets from being sent to an OSI-only node.

A dual node may be connected directly to an OSI-only node if it is also treated as an OSI-only node, as shown in figure 7.

Figure 7

In this case the network acts as a dual network for packets going from point A to B, but IPv4 packets cannot reach the central dual node.  This dual node is inside an OSI-only sub-network.  This dual node will be able to forward CLNP packets only, and must be CLNS managed.  There must be no other connections to the central dual node, as, if IPv4 packets were introduced at the central node, then they might be forwarded to an OSI-only node and be discarded.

3.2 Getting IP Traffic In and Out of the SDH Embedded Network

3.2.1 IP Capable Gateway NE

Both IP and CLNP packets must be able to enter and leave a dual area, whether or not automatic encapsulation is used.  Normally traffic enters and leaves an IS-IS area via level-1,level-2 routers.  These are routers that participate both in the level-1 area and in the level-2 subdomain.

The simplest way to build this is to ensure that any level-1,level-2 routers are dual, as shown in figure 8.

Figure 8

3.2.2 OSI Only Gateway NE

Occasionally automatically encapsulating nodes will be used to upgrade an existing OSI-only area to make it effectively into a dual area.  In this case the gateway nodes may have to remain as OSI-only nodes.  In such a case a network can be built as shown in figure 9.

Figure 9

In this network the CLNP packets that need to leave the level-1 area continue to go to the OSI level-1,level-2 router.  The nodes that have a manual tunnel leading out of the level-1 area advertise this as a default route.  Consequently the IP-capable nodes will all add an entry to the bottom of their routing table telling them to send all IPv4 packets to one of the nodes that has the manual tunnel, unless they have a more specific route.  In this way an IPv4 packet is never sent to a level-1,level-2 node, but is always sent across one of the manual tunnels.

The router in the Access DCN that terminates the manual tunnel does not need to run Integrated IS-IS.  It may run any IP routing protocol that an operator wishes to use.  In this way an existing network that uses OSPF and level-2 IS-IS in the Access DCN, and level-1 IS-IS in the SDH NEs may have the level-1 areas upgraded to dual areas with little impact on the existing OSI-only SDH NEs or on the Access DCN.

APPENDIX IV

Bibliography

(This Appendix does not form an integral part of this Recommendation)

- IETF RFC 1006 – ISO Transport Service on top of the TCP Version: 3 – May 1997

- IETF RFC 2966 – Domain-wide Prefix Distribution with Two-Level IS-IS – October 2000

______________

# Comments

Noticed this acronym was missing. I used the one provided in ISO 10589.

Corrected mistake.

Corrected mistake.

Added text based on COM 15-53-E (related to auto-encapsulation procedure)

Added text based on COM 15-67-E (clarification – no technical changes)

Added Section 7.1.10.1.1 based on COM 15-66-E (clarification – no technical changes)

Text modified based on COM 15-67-E (updated based on improvements made in IETF (see draft-ietf-isis-3way-05.txt).  No technical changes.

This sentence does not make sense.  Need clarification.