MFA Forum Technical Committee

Contribution

Subject:	Straw Ballot text for the Packet Based GMPLS Client to Network Interconnect (CNI)

Contacts:	Rao Cherukuri	David Sinicrope

Phone: +1 919 807 0023	Phone: +1 919 472 9967

E-Mail:cherukuri@juniper.net	E-Mail:david.sinicrope@ericsson.com

Juniper Networks	Ericsson IP Infrastructure

Date:	November, 14, 2006

Location:	Conference Call Output

Distribution:	Participants in the MFA Forum Technical Committee

Abstract:	This contribution contains the edited result of the conference call for the Packet Based GMPLS Client to Network Interconnect (CNI) based on Q4 2006 meeting and subsequent editing.

Declaration of IPR:

The contributor has read and supports the MFA Forum’s IPR Policy Statement.  To the best of the contributor’s knowledge, the contributing member: does not have any IPR that would be infringed by the Implementation Agreement proposed by any member.

Notice: This contribution has been created to assist the MFA Forum.  This document is offered to the MFA Forum solely as a basis for discussion and is not a binding proposal on the companies listed as resources above. Each company in the source list, and the MFA Forum, reserves the rights to at any time to add, amend, or withdraw statements contained herein.

This Working Text represents work in progress by the MFA Forum, and must not be construed as an official MFA Forum Technical Document.  Nothing in this document is in any way binding on the MFA Forum or any of its members.  The document is offered as a basis for discussion and communication, both within and without the MFA Forum.

For additional information contact:

The MFA Forum, 39355 California Street,

Suite 307, Fremont, CA 94538

510-608-3997 phone

info@mfaforum.org

© 2006 MFA  Forum

MFA Forum

Packet Based GMPLS Client to Network Interconnect (CNI)

MFAF X.0.0

Proposed Final Ballot Text

MFA Forum Technical Committee
November 2006

Note:	The user’s attention is called to the possibility that implementation of the MFA Forum implementation agreement contained herein may require the use of inventions covered by patent rights held by third parties. By publication of this MFA Forum implementation agreement the MFA Forum makes no representation that the implementation of the specification will not infringe on any third party rights. The MFA Forum take no position with respect to any claim that has been or may be asserted by any third party, the validity of any patent rights related to any such claims, or the extent to which a license to use any such rights may not be available.

Editors:

Rao Cherukuri Juniper Networks, Inc. David A. Sinicrope Ericsson Inc.

For more information contact:

The MFA Forum Suite 307 39355 California Street Fremont, CA 94538 USA Phone: +1 (510) 608-3997 FAX: +1 (510) 608-5917 E-Mail: info@mfaforum.org WWW: http://www.mfaforum.org/

Full Notice

Copyright © 2006 MFA Forum.

All rights reserved.

This document and translations of it may be copied and furnished to others, and works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works.  However, this document itself may not be modified in any way, such as by removing the copyright notice or references to the MFA Forum, except as needed for the purpose of developing MPLS implementation agreements (in which case the procedures copyrights defined by the MFA Forum must be followed), or as required to translate it into languages other than English

This document and the information contained herein is provided on an "AS IS" basis and THE MFA FORUM DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

Table of Contents

1	Introduction	5

1.1	Purpose	5

1.2	Overview	5

1.3	Scope	6

1.4	Requirements	6

2	Definitions	7

2.1	Acronyms	7

3	Normative References	8

4	Reference Architecture	9

5	Supported Layer 2 Encapsulations of MPLS Packets	10

6	User Plane	10

7	Signaling and Control	10

7.1	MPLS Client-Network Signaling	10

7.2	GMPLS Signaling Channel	11

7.3	Routing and Addressing	11

7.4	QoS and Traffic Engineering	11

7.4.1	Multi-class LSPs	12

8	OAM	12

8.1	Access Link integrity	12

8.2	LSP OAM	13

9	Switched LSP Signaling	13

9.1	Explicit Routing Object (ERO)	13

9.1.1	ERO Sender Processing	13

9.1.2	ERO Receive Processing	13

9.2	Record Routing Object (RRO)	14

9.3	Notification	14

9.4	Connection Deletion with PathErr	14

9.5	Signaling extensions for Multi-class LSPs	14

9.5.1	Setup and holding preemption priorities	14

9.5.2	Extended Classtype object	15

9.5.3	RSVP signaling extension	16

9.5.4	RSVP error processing	16

A	Appendix A – Alternate OAM Mechanisms for the CNI (informative)	18

A.1	Access Link integrity	18

A.2	LSP OAM	18

Revision History

| Version | Change | Date |
| --- | --- | --- |
| MFAF X.0.0 | Initial version |  |

# Introduction

## Purpose

The purpose of this specification is to define an MPLS-based Client to Network Interconnect (CNI) for establishing GMPLS Traffic Engineered (TE) Label Switched Paths (LSPs).  The CNI provides an interface to an IP-MPLS Network for interconnection of client equipment.  The client equipment can be Customer Premise Equipment (CPE) or other network elements in an IP-MPLS network.  The CNI supports switched GMPLS-TE LSPs.  Provisoned LSPs are for further study.

## Overview

Many services such as LAN inter-connect, audio and video streaming, VoIP telephony and multimedia conferencing use protocols that require quality of service in the network.  The purpose of the CNI is to provide a means to create and manage a TE-LSP overlay network. This overlay network interconnects client equipment over an MPLS network, providing bandwidth guarantees, and enhanced resiliency features.

Generalized Multiprotocol Label Switching (GMPLS) defines both routing and signaling protocols for the creation of Label Switched Paths (LSPs) in various transport technologies.  In the overlay model, the network nodes act more as a closed system.  The client nodes do not participate in the routing protocol instance that runs among the network nodes; in particular, the client-nodes are unaware of the internal topology of the network.  At the CNI, it is not desirable to have the client equipment participate in the internal control protocols of the MPLS network.  Allowing such participation has the effect of exposing the internal IP-MPLS network topology to the client, introducing scalability and security concerns.  For these reasons, this document uses the GMPLS overlay model as its basis.

One example of a deployment scenario that uses the overlay model in this context is the interconnection of media gateways over an IP-MPLS network.

This document is organized as follows:

Section 4 describes the reference architecture for the GMPLS CNI.  It shows the placement and relationship of the client and network equipment as well as which elements take part in the CNI protocols.

Section 5 describes layer 2 interfaces and section 6 describes the data plane.

Section 7 defines the general signaling protocol, principles and procedures used at the GMPLS CNI.  These include signal messaging, addressing and QoS.

Section 8 defines the OAM procedures for dynamic LSPs.

Section 9 defines the specific protocol used to provide PSC LSP services using the GMPLS CNI.

Note: Where this document discusses LSPs it is implied that they are GMPLS-TE LSPs.

## Scope

The CNI supports client to client LSPs for transport of MPLS encapsulated traffic across an IP-MPLS network.  The client equipment can be Customer Premise Equipment (CPE) or other network elements in an IP-MPLS network.

This document uses GMPLS RSVP-TE procedures between a client and a network based on the overlay model defined in GMPLS UNI [RFC 4208].  This specification differs from [RFC 4208] with regards to the following:

- Only packet switched LSPs are considered in this specification.

- Multi-class QoS parameters for each LSP are added.

The connections referred to in this specification can be either unidirectional packet switch LSPs as defined by [RFC 3209] or bidirectional packet switch LSPs as defined by [RFC 3471].]

All signaling procedures are identical to the GMPLS extensions specified in [RFC 3473], except as noted in this specification.  Where the network uses MPLS-TE signaling, the PE routers are expected to perform the translation.

In most cases the transport IP-MPLS network can be that of a service provider or a private network that uses the CNI for its own purposes, but other uses of the CNI are not precluded.

The CNI provides the client equipment with the following:

- A unidirectional or bidirectional transport connection, for transmission and reception of variable length MPLS packets over supported layer 2 technologies.  The layer 2 technologies supported are listed in section ‎5.

- A means of requesting traffic engineered packet switched LSP establishment, monitoring LSP state and LSP clearing, without participating in the internal routing of the IP-MPLS network.

OAM protocols and procedures may be carried within the LSP end-to-end and are therefore transparent to the network.

Note: For this version of the document, only one Autonomous System Number (ASN) is used in the Explicit Route Object (ERO) processing.

## Requirements

- The routing topology of the provider network must not be visible to the client.  At the CNI, explicit routing is limited to  specifying a transit network selection via an AS identifier.

- The CNI must support Packet Switched LSPs over GMPLS-TE capable interfaces.

- The CNI only supports the IP based addressing scheme.

- The client equipment must be kept agnostic of the provider MPLS network internal addressing space.

- Network equipment should allow for different client and network internal addressing spaces.

- The CNI must support requests for both bi-directional LSPs and uni-directional LSPs.

- The Generic Label format defined in [RFC 3032] must be used as the label format for the CNI.

# Definitions

Must, Shall or Mandatory — the item is an absolute requirement of this specification.

Should — the item is desirable.

May or Optional — the item is not compulsory, and may be followed or ignored according to the needs of the implementer.

## Acronyms

| Acronym | Description |
| --- | --- |
| AS | Autonomous system |
| ASN | Autonomous system Number |
| ATM | Asynchronous Transfer Mode A |
| BW | Bandwidth A |
| BFD | Bidirectional Forwarding Detection A |
| CE | Customer Edge |
| CNI | Client to Network Interconnect |
| CPE | Customer Premise Equipment |
| CT | Class-Type |
| ERO | Explicit Routing Object |
| FEC | Forwarding Equivalency Class |
| FR | Frame Relay |
| GMPLS | Generalize Multiprotocol Label Switching |
| IANA | Internet Assigned Number Authority |
| IEEE | Institute of Electrical and Electronics Engineers |
| IETF | Internet Engineering Task Force |
| IP | Internet Protocol |
| LER | Label Edge Router |
| LSB | Least Significant Bit |
| LSP | Label Switched Path |
| LSR | Label Switching Router |
| MPLS | Multi Protocol Label Switching |
| MSB | Most Significant Bit |
| OAM | Operations, Administration and Management |
| PE | Provider Edge |
| POS | Packet over SONET / SDH |
| PPP | Point to Point Protocol |
| PSB | Path State Block |
| PSC | Packet Switch Capable |
| PSN | Packet Switched Network |
| QoS | Quality of Service |
| RFC | Request for Comments |
| RSVP-TE | Resource ReserVation Protocol – Traffic Engineering |
| SDH | Synchronous Digital Hierarchy |
| SMI | Structure of Management Information |
| SONET | Synchronous Optical NETwork |
| TE | Traffic Engineering |
| TLV | Type, Length, Value |
| UNI | User to Network Interface |
| VOIP | Voice Over Internet Protocol |

# Normative References

[RFC 1661]	Simpson, W., The Point-to-Point Protocol (PPP), STD 51, RFC 1661, July 1994.

[RFC 1662]	Simpson, W., PPP in HDLC-like Framing, STD 51, RFC 1662, July 1994.

[RFC 2210]	J. Wroclawski, The Use of RSVP with IETF Integrated Services, RFC 2210, September 1997.

[RFC 2615]	Malis, A., et al, PPP over SONET/SDH, RFC 2615, June 1999.

[RFC 3031]	E. Rosen, et al., Multiprotocol Label Switching Architecture, RFC 3031, January 2001.

[RFC 3032]	E. Rosen (ed.), et al., MPLS Label Stack Encoding, RFC 3032, January 2001

[RFC 3035]	B. Davie, et al., MPLS using LDP and ATM VC Switching, RFC 3035, January 2001

[RFC 3209]	D. Awduche, et al., RSVP-TE: Extensions to RSVP for LSP Tunnels, RFC 3209, December 2001.

[RFC 3471]	L. Berger, et al., Generalized Multi-Protocol Label Switching (GMPLS), RFC 3471, January 2003

[RFC 3473]	L. Berger, et al., Generalized Multi-Protocol Label Switching (GMPLS) Signaling Resource ReserVation Protocol-Traffic Engineering (RSVP-TE) Extensions, RFC 3473, January 2003

[RFC 3936]	K. Kompella, J. Lang, Procedures for Modifying the Resource reSerVation Protocol (RSVP), RFC 3936, October 2004

[RFC 4124]	F. Le Faucheur, et al., Protocol Extensions for Support of Diffserv-aware MPLS Traffic Engineering, RFC 4124, June 2005

[RFC 4182]	E. Rosen, Removing a Restriction on the use of MPLS Explicit NULL, RFC 4182, September 2005.

[RFC 4208]	G. Swallow, et al Generalized Multiprotocol Label Switching (GMPLS) User-Network Interface (UNI): Resource ReserVation Protocol-Traffic Engineering (RSVP-TE) Support for the Overlay Model, RFC 4208.

[RFC 4379]	K. Kompella, G. Swallow, Detecting Multi-Protocol Label Switched (MPLS) Data Plane Failures, RFC 4379, February 2006

[STD 55]	C. Brown, A. Malis, Multiprotocol Interconnect over Frame Relay, RFC 2427, September 1998

[IEEE 802.3]	IEEE 802.3 Series.

[IEEE 754]	IEEE Standard for Binary Floating-Point Arithmetic,  ANSI/IEEE Std 754-1985

[I.363.5]	ITU-T Recommendation, B-ISDN ATM Adaptation Layer Specification: Type 5 AAL, August 1996.

[Q.922]	ITU-T Recommendation, Digital Subscriber Signalling System No. 1 (DSS 1) Data Link Layer – ISDN Data Link Layer Specification for Frame Mode Bearer Services, 1992.

# Reference Architecture

Figure 1 identifies the Reference Architecture for the GMPLS CNI.  The provider network is a GMPLS or MPLS based Packet Switched Network (PSN) and contains a number of Label Switching Routers (LSRs).  The network equipment consists of customer-facing LSRs are known as Provider Edge (PE) LSRs.  The client equipment that directly interacts with the MPLS network is known as Customer Edgeequipment (CE).  The interface defined in this document is the interface between the PE and CE and constitutes the GMPLS CNI reference point.

The signaling, routing and data connections used in the IP-MPLS network to support the LSPs offered across the CNI are outside the scope of this specification.  It is intended that the resulting LSP parameters signaled over the CNI will be supported by network mechanisms used to provide the LSP.

The CNI defines protocols to address support for client-network scenarios, including cases where there are inherent trust boundaries.

Figure 1.  MPLS CNI  -- Reference Model

Figure 2.  Protocol stack for MPLS Datapath

Figure 2 shows the protocol stack for the MPLS data path.

# Supported Layer 2 Encapsulations of MPLS Packets

- PPP [RFC 1661, RFC 1662]

- POS [RFC 2615],

- 10/100/1G/10G Ethernet [IEEE 802.3],

- Frame Relay [Q.922, STD 55],

- ATM AAL5 [I.363.5].

# User Plane

The user plane for the CNI uses the following specifications for encapsulation format:

- RFC 3032 [RFC 3032]

- RFC 4182 [RFC 4182]

The LSP characteristics are defined by the parameters in the Senders_TSpec.  See [RFC 2210] for details.

# Signaling and Control

## MPLS Client-Network Signaling

RSVP with Traffic Engineering extensions (RSVP-TE) has been defined for establishing connections subject to routing constraints in an MPLS network [RFC 3209].  The RSVP-TE definition includes additional procedures, messages and object formats as extensions to the base RSVP definition.  Generalized MPLS (GMPLS) extensions for RSVP-TE signaling [RFC 3471] [RFC 3473] extend RSVP-TE signaling procedures and objects to cover different types of switching applications.

This specification only supports Packet Switch Capable (PSC) mode.  The PSC interfaces are capable of switching packets based on MPLS shim label.

The GMPLS CNI signaling protocol is based on and compatible with GMPLS signaling [RFC 3471] [RFC 3473].    The mechanisms for the CNI signaling are in line with the RSVP model, namely, there is a single end-to-end user connection.

The transport network in the provider network is a GMPLS or MPLS-TE based packet switched network that must support request for uni-directional LSPs and may support requests for bi-directional LSPs

This CNI signaling also specifies the optional extensions necessary to set up multi-class, diffserv-aware traffic engineered label switched paths (LSPs).  A multi-class diffserv-TE LSP carries traffic from multiple traffic classes and is set up along a path that satisfies the bandwidth constraints defined for each of the classes it carries (see section ‎7.4).

The following sections modify the GMPLS specification [RFC 3473] for use in the GMPLS CNI.  If a section in the GMPLS specification is not mentioned, then it is used as is.

## GMPLS Signaling Channel

The CE and PE nodes are inter-connected by point-to-point interfaces.  The signaling channel is “in-band”, i.e., the labeled packets share the same access connection as the RSVP-TE signaling.

## Routing and Addressing

The routing topology of the provider network is not visible to the client.

A client is identified by either a single IP address representing its Node-ID, or by one or more numbered TE links that connect the client to the PE.

A client need only know its own address, a reachable address of the adjacent PE-node, and know the address of any other client to which it wishes to connect.  The addresses listed above must be configured on each client.

A PE need only know (and track) the addresses on interfaces attached to clients, as well as the Node IDs of these attached clients. In addition, the IP/MPLS network needs to know reachability to the interface addresses and Node IDs of other PEs to which an attached client is permitted to connect.

When forming a Sender_Template the ingress client includes either its Node-ID or the address of one of its numbered TE links. In the latter case the connection will only be made over this interface.

When forming a Session_Object, the ingress client includes either the Node-ID of the egress client or the address of one of the egress client’s numbered TE links. In the latter case the connection will only be made over this interface. The Extended_Tunnel_ID of the Session_Object is set to either zero or to an address of the ingress client.

## QoS and Traffic Engineering

Diffserv Aware Traffic Engineering [RFC 4124] defines the protocol extensions for setting up diffserv-aware traffic engineered LSPs. An LSP set up according to [RFC 4124] carries traffic from a one diffserv class type “N” and is set up along a path that satisfies the bandwidth constraints specified for this class.

In [RFC 4124], the Path message will include the Class-Type (CT) field set to “N” and only a single class-type object is allowed in a Path message.  In this case, there is one and only one class-type configured per LSP.

For purposes of this specification, QoS and traffic engineering requests for LSP setup must also be able to use multi-class LSPs as defined in the next section.

### Multi-class LSPs

In some scenarios it is required to allow traffic with different diffserv behaviors to be mapped to the same LSP.  In this case, multiple Class-Types are configured per LSP.  The LSP must be traffic engineered according to the bandwidth constraints for class individually.

Although, a multi-class LSP is always an E-LSP, an LSP that is signaled using the extensions defined in this specification (see section ‎9.5) is not required to request bandwidth for multiple Class Types. As a special case, when the request is for a single Class-Type, the LSP behaves as a single-class LSP.  Conceptually, single-class LSP is a special case of a multi-class LSP.

In order to achieve bandwidth reservation for several class types, two approaches can be taken:

- create one multi-class LSP or

- create several single-class LSPs.

Note however that the two approaches have different properties in terms of:

- the number of LSPs established,

- the path that is taken by traffic belonging to different classes and

- the fate sharing between the different classes.

The choice of single-class or multi-class LSP is made based on the requirements of the application and on the network design.

An example scenario for multi-class LSPs is emulating an ATM trunk using a muli-class LSP. In this case, it is preferable to have all the traffic classes following the same path and exhibit the same behavior in case of failure as opposed to using multiple single-class LSPs, each of which might be routed along a separate path.

Another application of multi-class diffserv-TE LSPs is to reduce the number of LSPs in a network by setting up reservations for several classes in one LSP rather than one LSP per class. Assuming a meshed LSP topology, with single class LSPs, the total number of LSPs in the network could be as large as the number of classes times the number of LSPs in the mesh. With multi-class LSPs, the total number of LSPs is equal to the size of the LSP mesh. The reduction in the number of LSPs is important from a scaling and manageability point of view.

# OAM

## Access Link integrity

Access link integrity (liveness) is determined using the native procedures particular to the Layer 2 protocol used for the CNI, between the client and PE.

Alternative mechanisms for determining access link integrity are described in Appendix A.

## LSP OAM

Mechanisms used for LSP OAM, operate client to client, transparent to the network over the established LSP.  Although no specific mechanisms are mandated, possible mechanisms are described in Appendix A.

# Switched LSP Signaling

Signaling procedures are identical to the RSVP-TE [RFC 3209] and GMPLS extensions [RFC3473] except as noted in this section.

## Explicit Routing Object (ERO)

### ERO Sender Processing

If the provider supports the “Transit Network Selection” option, the client may send an ERO object in the Path message. The client equipment shall only insert ASN sub-objects (Type 32) in the ERO object. The client shall insert only those ASN numbers that have been previously agreed upon with the provider.

The client populates the ERO object with only one sub-object containing an Autonomous System Number (ASN) representing a transit network beyond the originating service provider.  The client equipment must set the ASN sub-object ‘L’ bit to 1, indicating a loose route.

In cases where the PE responds to the Path message with a PathErr message containing “Unkown object class” or “No route available towards destination”, the client should notify its management that an LSP cannot be established.  The client may then take action to continue the reservation without the ERO object or via a different explicit route.

### ERO Receive Processing

Support for the ERO object is optional at the PE. If the PE does not support the ERO object and receives a RSVP Path message with an ERO object, it sends a PathErr message with the error code "Unknown object class" toward the sender. This response is the same as specified in section 4.3.7 in [RFC 3209]. This causes the path setup to fail.

When a PE receives a Path message from a client that contains an ERO, it should verify the reachability to the ASN before forwarding the Path message.  If the route is not viable (e.g., according to topology, currently available resources, or local policy), then a PathErr message with an error code 24 “Routing problem” and value 5 "No route available toward destination" is returned.

If the client sends an ASN number in an ERO subobject which does not belong to the list of numbers that have been agreed between the client and the provider, then the PE sends a PathErr message with an error code 24 “Routing problem” and value 3 “Bad Loose Node”.

If the client sends more than one ASN sub-object in the ERO object, or if a PE receives an ERO object from a client with a sub-object other than of type ASN (Type 32), it sends a PathErr with the error code 2 "Policy control failure" toward the sender with value 3 “Bad Loose Node”.

When a PE receives a Path message from a client that contains no ERO indicating transit network selection, then the PE is responsible for progressing the Path message toward the destination.  The progression of the Path message is beyond the scope of this specification.

## Record Routing Object (RRO)

The Record Route Object is not supported on the CNI interface.

The client shall not include RRO in the Path message.  A PE that receives an RRO from a client must remove the RRO from the Path message before forwarding it.

A PE must remove an RRO from the Resv message before forwarding it to the client.

## Notification

The Notification related objects and messages are not applicable to the CNI.  The client shall not send a Notify Request object in any Path or Resv message to the PE.  If the client sends a Notify Request object in a message, the PE shall ignore and silently discard the Notify object.  The client shall ignore and silently discard all Notify Request objects contained in Path or Resv messages received from the PE. Similarly the PE and client shall ignore and silently discard any Notify messages received.

## Connection Deletion with PathErr

[RFC 3473] introduces the Path_State_Removed flag to a PathErr message to indicate that the sender has removed all state associated with the LSP and does not need to see a PathTear message. When a PE next to a client receives a PathErr with Path_State_Removed from the network, it may in turn generate either a ResvTear or PathTear, whichever is applicable, to be sent to the client.

A PE receiving a ResvTear from its downstream neighbor in the network may respond with a PathTear and send a PathErr with Path_State_Removed to the adjacent client.

## Signaling extensions for Multi-class LSPs

### Setup and holding preemption priorities

As per existing TE, routers supporting multi-class LSPs can be configured with a setup and holding priority, each with a value between 0 and 7.  The combination of the setup priority and each of the Class-Types for which the multi-class LSP is set up and of the hold priority and each of the Class-Types for which the multi-class LSP is set up, must be such that together they form one of the (up to) 8 TE-Classes configured in the TE-Class Mapping. This requirement is similar to the requirement spelled out in [RFC 4124] regarding the combination of priority and class-type for single-class LSPs.

### Extended Classtype object

To request LSP setup along a path with bandwidth constraints from more than one Class-Type, a new object is defined, the Extended Classtype object.  This object has a Class_num that ensures that a node that doesn't recognize it will reject it and return an "Unknown Object Num" error. In accordance with the guidelines specified in [RFC 3936], we select the vendor specific Class_Num  of 124 and C-Type of 1 [RFC 3936] which specifies that when including an OBJECT with a vendor specific class number, the implementation must include the MFA Forum SMI enterprise code 353 (decimal) in the first 32 bits of the object in network octet order.

Note: In the case of a bidirectional LSP, the class attribute and bandwidth (BW) attribute in the Path message are used for both directions.

The contents of the Extended Classtype object are a set of sub-objects, each encoded as a TLV.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

Sub-objects

….

….

A TLV of the Extended Classtype sub-object has the following format:

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

| Type | Length | Reserve | CTi |
| --- | --- | --- | --- |
| BW requested for CTi |

Type :	8 bits

The type of the contents of the sub-object. The values are:

1 - bandwidth

Length:	16 bits

The length contains the total length of the sub object in bytes, including the type, length, Reserve, CTi fields. The length MUST be at least 8, and MUST be a multiple of 4.

Reserve:	5 bits

This field is reserved. It must be set to zero on transmission and must be ignored on receipt.

CTi:	3 bits

Indicates the Class-Type. Values allowed are 0, 1, 2, …, 7. Note that this is different from the definition given in [RFC 4124] where the value 0 is not allowed.

BW requested:	32 bits

Indicates the number of bytes (not bits) per second that need to be reserved for the CT indicated.  This is encoded as a 32-bit IEEE floating point number representing a positive, integer value. [IEEE 754]

### RSVP signaling extension

The Extended Classtype object is signaled in the Path message, and saved in the Path State Block (PSB) at every hop. The Extended Classtype object must not be included in a Resv message.

When the Extended Classtype object is present, the values in the TSpec are ignored for admission control purposes and should be 0.  Admission control is performed for the requirements specified in each of the (CT, BW) pairs in the Extended Classtype object. Admission control succeeds only if the requirements for all (CT, BW) pairs are satisfied.

Merging at the CNI must not be performed.

If the Extended Classtype object is not present in the Path message, the LSR associates the LSP with CT0 and performs admission control from the bandwidth/priority values for CT0.

### RSVP error processing

If a PE does not support the Extended Classtype object, the PE returns an "Unknown Object Num' error to the client.

An LSR that recognizes the Extended Classtype object and that receives a Path message which contains the Extended Classtype object but which does not contain a Label Request object or which does not have a session type of LSP_Tunnel_IPv4, must send a PathErr message towards the sender with the error code 'extended-classtype Error' and an error value of 'Unexpected Extended Classtype object'.  These are defined below:

An LSR receiving a Path message with the extended-classtype object, which recognizes the object but does not support the particular Class-Type, must send a PathErr message towards the sender with the error code ' Extended Classtype Error' and an error value of 'Unsupported Class-Type'.

An LSR receiving a Path message with the Extended Classtype object, which:

- recognizes the object,

- supports the particular Class-Type, but

- determines that the tuple formed by (i)this Class-Type and (ii) the holding priority signaled in the same Path message, is not one of the eight TE-classes configured in the TE-class mapping, must send a PathErr towards the sender with an error value of 'CT and holding priority do not form a configured TE-Class'. For setup priority, return 'CT and setup priority do not form a configured TE-class'

The error checking ensures that multi-class LSPs get established only through LSRs that support multi-class diffserv-te LSPs and have consistent TE-mappings with the ingress.

Errors above related to the processing of the Extended Classtype object are reported using the vendor-specific Error-Code "extended-classtype-error" 252. The first four octets following the Error Value are 353(decimal) - the vendor's SMI enterprise code in network octet order (as required by [RFC 3936]).

The error values are the same as defined in [RFC 4124] for the classtype object. The values 3, 6, 7 are not used with multi-class-LSPs.

# A	Appendix A – Alternate OAM Mechanisms for the CNI (informative)

## A.1	Access Link integrity

Technologies currently under development such as Bidirectional Forwarding Detection (BFD) may be used to determine CE-PE access link integrity.  In particular, where the CE is multiple layer 2 hops away from the PE, BFD allows complete CE to PE integrity checking. The native layer 2 integrity mechanism only reports on the adjacent links status, not CE to PE status.

For security reasons, it may also be advantageous to use one of the authentication mechanisms provided in BFD.  See the work in the IETF on BFD for details.

## A.2	LSP OAM

LSP Ping ‎0 and BFD may be used for LSP continutity check.  These mechanisms are used client to client, transparent to the network over the established LSP.

Note: If LSP Ping or BFD are used, the requirements of these specs are assumed to be met by the topology (e.g., return path).  See the work cited above for details.

END OF DOCUMENT

# Footnotes

The intent is to revise this document and recommend the use of the BFD mechanisms in Appendix A, once the RFCs are published by the IETF.

See footnote 1 above.

# Text boxes

MPLS CNI
reference point

Client

Client

Shim LSPs

RSVP-TE

capable access link

MPLS

PSN Connection

client - client connection

MPLS CNI
protocols

PE

PE

IP-MPLS Network