|  | INTERNATIONAL TELECOMMUNICATION UNION | COM 15 – LS 134 – E |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 |  |
|  |  | English only Original: English |
| Question(s): | 12/15 |  |
| LIAISON STATEMENT |
| Source: | ITU-T SG15 |
| Title: | G.8110.1 Amendment 1 |
| LIAISON STATEMENT |
| To: | ITU-T SG13; IETF pwe3 WG, IETF mpls WG, MFA Forum |
| Approval: | Agreed to at SG15 meeting (Geneva, 30 October-10 November 2006) |
| For: | Action |
| Deadline: | 5 January 2007 |
| Contact: | Malcolm Betts Nortel Networks Canada | Tel:+1 613 763 7860 Email: betts01@nortel.com |

Q12/15 met during a SG 15 plenary meeting held in Geneva from the 30th of October to the 10th of November 2006.

Q12/15 has worked on an amendment to G.8110.1 covering the architectural aspects of T-MPLS unidirectional p2mp connections, T-MPLS OAM and T-MPLS survivability.

We have attached for your information and comment the draft Amendment 1 to G.8110.1/Y.1370.1.

We intend to request consent of this Amendment at the next SG 15 plenary meeting planned from 4 to 15 June 2007.

Q12/15 welcomes any comments on the proposed draft and would appreciate a reply if possible by the deadline indicated above.

We will address any comments via correspondence and, if necessary, make adjustments before the consent.

We will keep you advised on our future activities and look forward to further cooperation in this area.

T-MPLS requirements are going to be posted in the Q12 web site. We have updated the requirements for T-MPLS and started working on requirements for T-MPLS control plane.

Below are the updated requirements of T-MPLS and its control plane.

T-MPLS Requirements overview

The scope of Recommendation G.8110.1 provides a concise statement of the role and purpose for T-MPLS.  It states that “transport MPLS network functionality is described from a network level viewpoint, taking into account a T-MPLS network layered structure, client characteristic information, client/server associations, networking topology, and layer network functionality providing T-MPLS signal transmission, multiplexing, supervision, performance and survivability.” and “Transport MPLS is a connection-oriented packet switched transport layer network technology based on MPLS technology modelled in G.8110.

The requirements provided below are not formal requirements, nor are they intended to be comprehensive.  They are provided as an aid in clarifying the role and purpose of T-MPLS for those less familiar with ITU-T transport network technology recommendations.  Two important attributes that T-MPLS (or any transport network technology) should have are (1) independence from both client and server layer networks and (2) compatibility with existing transport network operations and management models.  It is expected that selecting a subset of MPLS functionality necessary and sufficient for transport applications (T-MPLS) will enable both stability for transport recommendations and independence from ongoing extension of MPLS standards used in other application areas.

The requirements are described using ITU-T functional modeling terms, which are defined in Recommendation G.805.  For those more familiar with IETF terminology, RFC 4397 may provide some assistance in understanding the correspondence between ITU-T and IETF terminology.

The purpose of a transport network is to transparently carry client signals between endpoints in the network (typically over several nodes). A key characteristic of transport networks is that they are able to maintain the integrity of the client signal (i.e. the stream of client PDUs or client bits) between ingress and egress ports of the transport network.

A transport network must provide means to commit quality of service objectives to clients. This is achieved by providing mechanism for client service demarcation across the network path and associated resiliency mechanism. A transport network must also provide means for service monitoring in order to guarantee an agreed quality of service. This is achieved by supporting OAM tools.

The transport network uses encapsulation and aggregation to carry client signals: client signals are first encapsulated to allow monitoring.  These encapsulated client signals are then aggregated for transport through the network in order to achieve optimized network management. At every hop the aggregated signals may be further aggregated to cross a physical link. At the edges of aggregation domains encapsulated client signals are extracted and either delivered to client or forwarded to another domain.  In the core of the network only the aggregated signals are monitored, individual client signals are monitored at the network boundary.  This is illustrated in the figure below.

Basic Transport Plane Requirements

1.	T-MPLS shall be based on a connection-oriented packet switched technology. Transport networks can also support circuit switched transport technologies (e.g. SDH, OTH or WDM)

2.	T-MPLS shall operate under a common operation, control and management paradigm with respect to other transport technologies (e.g. SDH, OTN or WDM)

3.	T-MPLS network shall support multiple layer network instances; e.g. a T-MPLS transport network “service layer” instance in which the connections carry the customer’s (individual or bundled) service, a T-MPLS transport network “trunk layer” instance in which the connections carry aggregates of the network “service layer” connections and a transmission media layer instance in which the connections carry the aggregate of network trunk or network service connections.

4.	The identification of each connection within its aggregate shall be based on labels. Connections can be aggregated into trunks by pushing and de-aggregated by popping labels. T-MPLS labels may be swapped within a connection in a layer network instance when the traffic is forwarded from one T-MPLS link connection to another T-MPLS link connection. T-MPLS pop, push, and swap label operations should be performed as defined by the relevant IETF RFCs.

5.	Labelling shall make use of the MPLS label and label stack entry as defined in RFC3032.

6.	A T-MPLS layer network shall support T-MPLS and non T-MPLS client layer networks and shall be able to be carried over T-MPLS and non T-MPLS server layer networks.

7.	The T-MPLS transport plane shall be able to operate without any IP functionality present.

8.	A T-MPLS network shall be able to be operated with a centralized NMS system

9.	A T-MPLS network should be able to be operated by a centralized NMS system with the support of a distributed control plane

10.	T-MPLS shall support both unidirectional and bi-directional point-to-point connections

11.	T-MPLS shall support unidirectional point-to-multipoint connections

12.	The forward and backward directions of a bi-directional connection should follow the same path along the T-MPLS network.

13.	The intermediate nodes should be aware about the binding of the forward and the backward directions belonging to the same bi-directional connection.

14.	T-MPLS shall support traffic-engineering capabilities with traffic- and/or resource-oriented performance objectives.

15.	T-MPLS shall support a method to offer packet loss objectives comparable to those in TDM transport networks (only due to bit errors)

16.	T-MPLS should support transport and QoS mechanisms that can deliver statistical multiplexing gain. Packets exceeding the agreed traffic profile are however not allowed to enter into the T-MPLS network (i.e. they are discarded by the traffic conditioning at the ingress of the network)

17.	The T-MPLS layer network shall operate independently of other layer networks (either T-MPLS or non T-MPLS).

18.	T-MPLS shall support connections through a single domain

19.	T-MPLS should support connections through multiple domains

20.	T-MPLS shall offer as much commonality as possible with the MPLS user plane as defined by IETF. When MPLS offers multiple options in this respect, T-MPLS should select the minimum sub-set (necessary and sufficient subset) applicable to a transport network application.

OAM Requirements

Note – T-MPLS OAM requirements are under definition in Y.17tor draft Recommendation. The requirements below are the main ones and additional requirements will be defined in Y.17tor.

21.	T-MPLS should support transport network connection and performance monitoring mechanisms

22.	T-MPLS OAM shall support fault management, performance management and protection switching mechanisms

23.	The T-MPLS OAM shall be able to operate without any IP functionality present.

Survivability Requirements

24.	T-MPLS should support transport network-style protection switching mechanisms (sub-network connection protection and trail protection)

25.	T-MPLS should support transport network restoration mechanisms

26.	The T-MPLS protection switching shall be able to operate without any IP functionality present.

Additional objectives are provided in G.8131.

T-MPLS Control Pane Requirements Overview

The scope of Recommendation G.8110.1 provides a concise statement of the role and purpose for T-MPLS.  It states that “transport MPLS network functionality is described from a network level viewpoint, taking into account a T-MPLS network layered structure, client characteristic information, client/server associations, networking topology, and layer network functionality providing T-MPLS signal transmission, multiplexing, supervision, performance and survivability.” and “Transport MPLS is a connection-oriented packet switched transport layer network technology based on MPLS technology modelled in G.8110.

The requirements provided below are not formal requirements, nor are they intended to be comprehensive.  They are provided as an aid in clarifying the required attributes of a T-MPLS control plane.  Two important attributes that T-MPLS (or any transport network technology) should have are (1) independence from both client and server layer networks and (2) compatibility with existing transport network operations and management models.  It is expected control plane solutions for T-MPLS will be similar to those employed with other transport technologies (e.g., SDH and OTN).

The requirements are described using ITU-T terms, which are defined in Recommendation G.8080.  For those more familiar with IETF terminology, RFC 4397 may provide some assistance in understanding the correspondence between ITU-T and IETF terminology.

- The transport plane functionality of T-MPLS is independent of the choice of control or management plane solutions.  This provides important separation between the selection of T-MPLS data plane behaviours and the choice of control or management technologies to operate a T-MPLS layer network.  This requirement is supported by D.632 and the Scope statement of Recommendation G.8110.1.

- T-MPLS Control Plane functionality is appropriate to transport applications.  There are many protocols available that might be applied to controlling T-MPLS layer networks.  Some of these have features designed to support applications and network modes other than those provided by T-MPLS.  If a protocol supports more features than are necessary and sufficient for T-MPLS applications, a subset suitable (necessary and sufficient) for use in a T-MPLS control plane should be specified.

- It must be possible to deploy a unified control plane to control the set of transport technologies deployed in a transport network.  To enable a common control and operations regime across the set of transport technologies used in a network, the T-MPLS control plane must be usable for other transport layer networks as well.  This provides the option to use either separate control plane instances or a single control plane instance to control a set of transport layer networks.

- T-MPLS layer network addressing is hidden from clients.  Providing clients of a layer network visibility into the addressing plan of the layer network invariably leads to conflicts between a client’s desire to change its attachment point to the layer network (and retain its endpoint address) and the operator’s desire to manage addressing plans relative to the layer network topology (e.g., to maintain the ability to effectively summarize addresses, to maintain the ability to re-address portions of the network during network rearrangements or merges, etc.).  For this reason it must be possible to operate a T-MPLS layer network without providing internal addresses to clients.

- A T-MPLS control plane must support topology hiding and address independence between domains.

- At the boundary of a domain a T-MPLS control plane must support unique names or addresses identifying boundary points to be interconnected.

- At the boundary of a domain a T-MPLS control plane must support group names or addresses identifying sets of boundary points to be interconnected.

- T-MPLS layer network access points (or connection points that proxy for access points) can be assigned names which are available to clients to identify endpoints in call or connection requests.  To meet the previous requirement, and allow clients to change their attachment points while keeping the same endpoint identifier, it must be possible to provide names to clients for use as endpoint identifiers.

- A T-MPLS control plane supports translation between endpoint names and network addresses.  This is a natural consequence of the previous two requirements.

- A T-MPLS control plane supports pre-provisioned connection protection.  In some situations it is impractical to expect acceptable recovery performance to be achieved using dynamic recalculation of connection routes.  For this reason, it is necessary to allow for pre-planning of protection routes for selected connections.  A T-MPLS control plane must support this capability.

- A T-MPLS control plane scales gracefully to support a large number of connections.  If T-MPLS is used as a common transport layer network, it will be called upon to support a substantial number of connections (equivalent to, or perhaps greater than, existing SDH and PDH layer networks).  Therefore, scalability is an important property of a control plane for T-MPLS.

- A T-MPLS control plane supports constraint-based route calculation.  T-MPLS is a flexible transport network technology.  Control plane route calculation must support the variety of constraints that may be placed on the connections supported by the T-MPLS layer network.  Both routing and signalling protocols must support the necessary variety of constraints for T-MPLS networks.

- A T-MPLS control plane must support provisioning and application of routing constraint policies.

- A T-MPLS control plane supports setup, modification, and release of T-MPLS trails, network connections and subnetwork connections.  The basic function provided by a T-MPLS layer network to clients is a T-MPLS trail, possibly including client adaptation at the trail endpoints as well.  Depending on network domain boundaries, the service provided may be a trail, network connection, or subnetwork connection.

- A T-MPLS control plane supports independent identification of logically distinct control plane elements.  Architecturally distinct elements in a control plane include: nodes and links (in the layer network under control), control plane functional components, protocol controllers, SCN addresses, etc. (see G.8080 section 10 for a more complete list of identifiers).  These elements must be independently identifiable and provisionable to allow for reorganization of control plane components without impacting the data plane services and vice-versa.

- A T-MPLS control plane must clearly distinguish resources belonging to the T-MPLS layer network from those in other layer networks that may also be under control plane control.   If multiple layer networks are operating under control plane control, the resources belonging to each layer network must be distinguishable.  This is important to enable coherent operation of distinct layer networks and provide a reasonable degree of independence in the operation of each layer network.

- A T-MPLS control plane provides a common control mechanism for architecturally similar operations.  To support effective operation of transport networks, it is important to avoid special cases wherever possible.  For example, one control mechanism should be applied to connection setup regardless of the length (number of hops) of the connection.

- A T-MPLS control plane supports mechanisms for partitioning the network under control into separate peer or hierarchical control domains.  Large transport networks often require subdivision, either due to scale, division of operations responsibility, or other reasons.  For these reasons, a T-MPLS control plane must support both peer and hierarchical domain organization.

- The T-MPLS control plane must support the configuration of maintenance functions (MEPs and MIPs) within a T-MPLS connection when the connection is established or modified.

- The T-MPLS control plane must support establishing all the connectivity patterns defined for the T-MPLS transport plane (e.g., P-P, P-MP, protected, etc.) including configuration of protection functions and any associated maintenance functions.

- Are there any auto-discovery requirements (e.g. related to G.7714) specific to the T-MPLS control plane? (For Further Study)

Attachments:

Draft Am.1 to G.8110.1 - TD 345 (WP 3)

_________________