3GPP TSG-RAN2 Meeting #56bis			R2-070434

Sorrento, Italy, January 15 – 19, 2007.

Title:	LS to IETF RoHc (cc RAN) on questions regarding the RoHC Protocol

Work Item:	SAE/LTE, TEI7

Source:	3GPP TSG RAN WG2

To:	IETF ROHC WG (Transport Area)

Cc:	3GPP TSG RAN

Contact Person:

#### Name:	Kim Soeng Hun

Tel. Number:	+82 31 279 5118

E-mail Address:	kimsh23@samsung.com

Attachments:	R2-070137

1. Overall Description

3GPP adopted ROHC as a header compression protocol for the radio link Release 4 onward, and is appreciating the overhead reduction provided by ROHC, which is essential especially for a service like VoIP.

To reduce the overhead further, it has been proposed to RAN WG2 by some companies to consider removing the UDP checksum from the compressed ROHC packets and the detailed information on the proposal can be found in the attachment.

During the discussion in RAN WG2, no decisions were made concerning the proposal itself and some questions were raised, which can only be answered by the ROHC WG.

Question 1:  What is the reason that the UDP checksum is kept in the compressed format?

Question 2: Is the proposed operation transparent and has no impacts on ROHC operation? Does IETF ROHC WG see any problem with the proposed operation from a ROHC protocol point of view?

Question 3:	If this kind of optimization were used then would it better be imbedded in ROHC itself? Does IETF ROHC WG have any plans to address this in the current/future version? If so when will this optimization be available?

Question 4:  If the aforementioned mechanism can be applied to the compressed UDP/IP stream, can it be applied to the uncompressed stream as well? Does IETF ROHC WG see any problem with the proposed operation when applied to the uncompressed UDP/IP stream?

2. Actions:

To IETF ROHC working group.

ACTION: 	RAN2 kindly asks IETF ROHC WG to provide answers to the above questions.

3. Date of Next TSG-RAN2 Meetings:

RAN2 #57			February 12-16, 2007		St. Louis, U.S.A.

RAN2 #57bis			March 27-30, 2007		Malta

# Comments

to be removed before LS is sent