|  | INTERNATIONAL TELECOMMUNICATION UNION | COM 15 – LS 178 – E |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 |  |
|  |  | English only Original: English |
| Question(s): | 12/15 | Geneva, 4-15 June 2007 |
| Source: | ITU-T SG15 |
| Title: | G.8110.1 amendment 1 |
| LIAISON STATEMENT |
| To: | IETF PWE3 and MPLS WG; Copy: ITU-T SG13 Q5/13 |
| Approval: | Agreed to at SG15 meeting June 2007 |
| For: | Information |
| Deadline: | None |
| Contact: | Malcolm Betts Nortel Networks Canada | Tel: + 1 613 763 7860 Fax: +1 613 763 4371 Email: betts01@nortel.com |

Thank you for your liaison statement “Liaison Progress on G.8110.1 Amendment”.  We have taken your comments into account and have now completed our work on this amendment, consequently it has been submitted to the ITU-T approval process.  We provide a response to your comments below.

Section 3.5 Transport MPLS definition

Should be amended to make it clear TMPLS is a true subset of IETF PWE3 over MPLS and that in the case of any differences, the IETF definition is considered the Normative definition.

G.8110.1 describes the behaviour of a T-MPLS network.  Following a discussion of your liaison statement it was agreed to clarify that T-MPLS uses a subset of the MPLS forwarding plane behaviour.  For OAM only label 14 is used and hence only “ITU” mechanisms are supported.  It is also assumed that MPLS and T-MPLS are deployed as disjoint networks.  An LSP initiated from an IP/MPLS network element is encapsulated in Ethernet before it transits a T-MPLS network.  Similarly if IP/MPLS is used as a server layer for T-MPLS then an LSP initiated from a T-MPLS network element is encapsulated in Ethernet before it transits an IP/MPLS network.  This enforces the independence of the control planes for T-MPLS and IP/MPLS.  Further as is customary with ITU-T Recommendations, equipment designed before the approval of the Recommendations is not expected to meet all the requirements of the new Recommendation.

Section 4.7.2 and A.3

The PWE3 WG is concerned that the OAM is not based on VCCV. Any true subset of the IETF PWE3/MPLS design should allow the use of the IETF preferred OAM mechanism. This does not preclude the ITU specifying an additional mechanism as an optional extension to enhance VCCV, although it would be preferable for the ITU to work with the IETF to enhance VCCV to provide the additional OAM mechanisms that are needed.

At a previous meeting SG 15 decided to base T-MPLS OAM on Y.1711 and requested Q5/13 to enhance the OAM mechanisms based on Y.1711.  Based on this request Q5/13 developed Y.1373/G.8114, the amendment to G.8110.1 adds a reference to Y.1373/G.8114.  As described above, we expect T-MPLS and MPLS to be deployed as disjoint networks and as is customary with ITU-T Recommendations, equipment designed before the approval of the Recommendations is not expected to meet all the requirements of the new Recommendation.  We do not anticipate any compatibility issues.

The PWE3 WG is not clear how you determine that the client signal is not present when the client is a packet service.

This text has been updated.

Section 4.10

"- Minimize the rerouting distance (to avoid physical layer impairments on the signals)."

We do not understand why in a well engineered network the distance in the virtual layer providing reroute has impact results in physical layer impairments

This text has been removed.

Appendix V

The introductory material to Appendix V states that it will be re-written at some time in the future to align with the IETF work on p2mp LSPs. We would therefore request that you liaise the final text to us when it is completed.

We will continue keeping you advised of our progress on T-MPLS topics.

As it stands the text of Appendix V looks correct, however we do have two proposals that we would ask you consider

1. We recommend that Upstream Assigned Labels be used over P2MP connections, or at least that you note in the text that generally administration of labels is simplified by using upstream assignment in this scenario.

The text has been updated.

2. That you include a reference to RFC 4875 (RSVP-P2MP) as this discusses many issues pertaining to P2MP MPLS connections.

A reference has been included.

A copy of the G.8110.1 amendment that has been submitted to the ITU-T approval process is attached for your information.  (TD377R1/P)

An electronic copy of this liaison statement is available at:

http://ties.itu.ch/ftp/public/itu-t/tsg15opticaltransport/COMMUNICATIONS/

___________________