# Liaison Statement

| Title: | LS From TISPAN to IETF MMUSIC WG regarding SIP/RTSP |
| --- | --- |
| From Organisation: | TISPAN WG3 |
| Technical Contact: | Raymond Forbes (Ericsson), |
| Reply to: | Raymond.forbes@ericsson.com, TISPANsupport@etsi.org |
| Reply by (date): |  |

| To Organisation: | IETF – MMUSIC WG |
| --- | --- |
| Contact Person: | Jean-Francois Mule |
| e-mail: | jf.mule@cablelabs.com |

| For: |
| --- |
| Action: |  |
| Information: | X |

ETSI TISPAN WG3 wishes to inform IETF MMUSIC WG of the standardization of IPTV services over IMS in draft ETSI TS 183 064 and its extensions and modifications to RTSP [RFC 2326].

In the draft ETSI TS 183 064, there are two methods for supporting IPTV services delivered over IMS with different combinations of SIP and RTSP. While one method uses regular RTSP version 1.0, there is also a second method which describes a tightly coupled SIP/RTSP model that uses an extended and modified version of RTSP 1.0. The main modification is to use SIP for RTSP session establishment and teardown. A SIP Invite with SDP offer/answer is used to setup the media flows and a TCP connection for RTSP requests and responses, removing the need for the RTSP SETUP and TEARDOWN methods. The usage of SIP and tighter coupling of SIP/RTSP enables closer integration with IMS and its functions, such as QoS, user identification and charging functions.

ETSI TISPAN WG3 would encourage IETF MMUSIC WG to consider defining support for the above described functionality. If such specification would become available TISPAN will consider adopting the use of it.

To find the ETSI TISPAN latest drafts see: http://portal.etsi.org/docbox/tispan/open/NGN_LATEST_DRAFTS/