Title:	On RTCP Bandwidth Negotiation

Source:	3GPP TSG SA WG4 (SA4)

To:	IETF MMUSIC WG

Contact Person:

#### Name: Nikolai Leung

Tel. Number: +1 (703) 346-8351

E-mail Address:	nleung@qualcomm.com

Attachments: None

3GPP SA4 uses the RTCP bandwidth modifiers (b=RS and b=RR) to control the amount of RTCP bandwidth used in point-to-point VoIP and video telephony sessions.  As these parameters were primarily designed for multicast sessions, the calculations in section 2 of RFC 3556 apply to the total RTCP bandwidth for the session, i.e., total bandwidth for all clients sending/receiving RTCP traffic. However, there are no SDP Offer/Answer models defined that use these parameters for the negotiation of the total RTCP bandwidth for point-to-point sessions.

To clarify this, SA4 is planning to make the following recommendations in our specifications:

- The RS and RR values included in the SDP offer should be treated as proposed values for the session and may be modified by the answerer during session negotiation.

- When generating the SDP answer, the answerer should include the RR and RS values proposed in the SDP offer. The answerer may instead choose to include RR and RS values lower than those proposed in the SDP Offer.

- The RS and RR values included in the SDP answer should be treated as the negotiated values for the session and should be used to calculate the total RTCP bandwidth for all terminals in the session.

2. Actions:

To IETF MMUSIC WG

ACTION: 	SA4 asks MMUSIC WG to review the above recommendations and identify if there are any discrepancies with the practices or understanding in the IETF.

3. Date of Next TSG-SA WG4 Meetings:

SA4#70	13 – 17 Aug 2012		Chicago, USA

SA4#71	5 – 9 Nov 2012   	 	Bratislava, Slovakia