|  | INTERNATIONAL TELECOMMUNICATION UNION | COM 15 – LS 392 – E |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2009-2012 |  |
|  |  | English only Original: English |
| Question(s): | 3, 9, 10, 12, 14/15 |  |
| LIAISON STATEMENT |
| Source: | ITU-T Study Group 15 |
| Title: | Request advance work on the p2mp framework in MPLS-TP |
| LIAISON STATEMENT |
| For action to: | - |
| For comment to: | IETF MPLS WG |
| For information to: | IETF PWE3 WG |
| Approval: | Q3, 9, 10, 12, 14 Joint interim meeting (Seoul, 11-15 June 2012) |
| Deadline: | 10 August 2012 |
| Contact: | Yoshinori Koike (Q3/15) NTT Japan | Tel: +81 422596723 Email: koike.yoshinori@lab.ntt.co.jp |
| Contact: | Ghani Abbas (Q9/15) Ericsson UK | Tel: +44 7710 370 367 Email: Ghani.Abbas@ericsson.com |
| Contact: | Huub van Helvoort (Q10/15) Huawei Technologies Co. Ltd. PRC | Tel: +31 36 531 5076 Email: huub.van.helvoort@huawei.com |
| Contact: | Malcolm Betts (Q12/15) ZTE PRC | Tel: +1 678 534-2542 Email: malcolm.betts@zte.com.cn |
| Contact: | Hing-Kam Lam (Q14/15) Alcatel-Lucent USA | Tel: +1 908 582 0672 Email: kam.lam@alcatel-lucent.com |

At the Seoul interim meeting, we discussed a future work on P2MP in MPLS-TP.  P2MP framework draft was originally planned to be an RFC between IETF and ITU-T in Feb 2011. However, the Internet-draft (draft-fbb-mpls-tp-p2mp-framework-03) was expired and has not been updated since July 8, 2011.

However, it was noted that the demand for P2MP traffic is expected to increase due to the increase in new services such as IP-TV and video distribution services. It was also noted that considering the global trend to improve energy efficiency, a P2MP transport function in MPLS-TP could be one of the solutions to achieve this goal from the perspective of efficient use of network resources. As a result, it is anticipated that the demand for P2MP in MPLS-TP transport network is also growing.

During the discussion, the following comments were raised.

- According to the requirements in RFC5860, four OAM functions (CV, RT, DT and LI) are supported in P2MP LSPs only when a return path exists. However, even if a return path does not exist, those OAM functions should be supported when the EMS/NMS can retrieve information.

- It should be clarified if the return path can be provided by notifications or messages to EMS/NMS. In this case, there will be no impact on traffic of data-plane and other management functions of EMS/NMS.

Therefore we encourage the development of P2MP framework including the clarification of the above comments in the Internet-draft “A Framework for Point-to-Multipoint MPLS in Transport Networks”.  Mr Yoshinori Koike (koike.yoshinori@lab.ntt.co.jp ) has indicated that he is willing to assist in progressing this draft in the IETF. We look forward to working with the IETF to advance this work.

_______________