## Slide 1: 6LoWPAN Selective Fragment Recovery
IETF 102
Montréal
P.Thubert
draft-thubert-6lo-fragment-recovery-01

## Slide 2: Features
New formats for the fragment header
Selective Fragments Recovery
  Expects but does not depend on IOD
Window-based Flow Control
  ACK at the end of the window
Explicit Congestion Notification
  ECN flag echoed to the source
Explicit Signaling to both set up and clean up
  Including Abort and Fin

## Slide 3: Status
Draft -01
  Replaces draft-thubert-6lo-forwarding-fragments
  Removed the virtual Recovery Buffer operation
    Now in draft-Watteyne-6lo-minimal-fragment
  Specify that the slack for variation of 6LoWPAN HC overhead must be in the first buffer
    This is not “needed” by VRB, but here we ack and retry fragments end to end

## Slide 4: Past IETF presentation
IETF
Prague
P.Thubert

## Slide 5: History
Presented 6lo Fragmentation issues in Chicago
  In appendix of this slideware
  Mostly issues for route-over
  Summarized in next slide
Work on fragmentation at LPWAN
  As part of the SCHC IP/UDP draft
  Optional: Windowing/individual retry of fragments
  Does not need to support multihop

## Slide 6: Context
TCP rarely used,
  Pro is MSS to avoid fragmentation
6LoWPAN applications handle their reliability
  UDP
  to get exactly what they need
  They also expect very long round trips.
Time gained by streamlining fragments is available for retries without a change in the application behavior.
Notes: > TCP is almost inexistant but when it is present, this is mostly to avoid the legacy fragmentation and rely on 100 bytes MSS instead; boils down to: we do not need to support the new model or fragmentation at all for TCP.
>
> Still Doing this right may require a bit more of cross layer coordination so that whatever happens over CoAP (e.g. Cocoa) is aware of the latency that can be expected.
>
> 6LoWPAN applications usually handle most of the reliability to get exactly what they need. They also expect very long round trips.
>
> Currently, packets are reassembled at each hop of the mesh; the new work enables to forward fragments, which can reduce latency and bloat dramatically. One rule of a thumb is that the time we gain by streamlining is available for retries without a change in the application behavior.
>
> Another rule is that applications are really conservative and some I am aware of are adapting their retransmission timers based on IETF recommendations so as to be good internet citizens.

## Slide 7: 6lo Route-Over fragmentation issues
Recomposition at every L3 hop
  Cause latency and buffer overutilization
Uncontrolled sending of multiple fragments
  Interferences in single frequency meshes
Fragment flows interfere with one another
  Buffer bloat / congestion loss
Loss locks buffers on receiver till time out
  Readily observable, led to RFC 7388

## Slide 8: 6lo Fragmentation reqs
Provide Fragment Forwarding
  There are pitfalls, better specify one method
  E.g. datagram tag switching ala MPLS
  Stateful => state maintenance protocol
Provide pacing/windowing capabilities
  Mesh awareness? (propagation delay, nb hops)
Provide fragment reliability
  individual ack/retry/reset, e.g. ala SCHC
Provide congestion control for multihop
  E.g. ECN

## Slide 9: Path Forward
Solutions exist (as shown by draft-thubert..):
Produce a problem statement at 6lo
  - Based on this slideware
Form a design team
  Need TSV skills to solve the problem
  Also MPLS and radio skill, CoAP, CoCoA
Find a host WG and produce a std track
  at TSVWG?
Also recommendations for application design

## Slide 10: Appendix

## Slide 11: Backup slides The problem with fragments in 6lo mesh networks
IETF 99
Prague
P.Thubert
draft-thubert-6lo-forwarding-fragments-04

## Slide 12: Recomposition at every hop
Basic implementation of RFC 4944 would cause reassembly at every L3 hop
In a RPL / 6TiSCH network that’s every radio hop
In certain cases, this blocks most (all?) of the buffers
  Buffer bloat
And augments latency dramatically
Research was conducted to forward fragments at L3.

## Slide 13: Early fragment forwarding issues #1
Debugging issues due to Fragments led to RFC 7388
Only one full packet buffer
Blocked while timing out lost fragments
Dropping all packets in the meantime
Arguably there could be implementation tradeoffs
  but there is no good solution with RFC4944,
  either you have short time outs and clean up too early,
  or you lose small packets in meantime

## Slide 14: Early fragment forwarding issues #1 c’d
Need either to abandon fragmented packet
or discover loss and retry quickly, both need signaling
Solution is well-know:
  selective acknowledgement
  reset
Requires new signaling
=> Implementation recommendations are not sufficient

## Slide 15: Early fragment forwarding issues #2
On a single channel multihop network (not 6TiSCH):
Next Fragment interferes with previous fragment
No end-to-end feedback loop
Blind throttling can help
New signaling can be better
2
1
A
B
C

## Slide 16: Deeper fragment forwarding issues #3
More Fragments pending than hops causes bloat
No end-to-end feedback loop for pacing
Best can do is (again) blind throttling
Solution is well-known, called dynamic windowing
Need new signaling
=> Implementation recommendations are not sufficient

## Slide 17: Deeper fragment forwarding issues #4
Multiple flows through intermediate router cause congestions
No end-to-end feedback for Congestion Notification.
Blind throttling doesn’t even help there
Fragments are destroyed, end points time out, packets are retried, throughput plummets
Solution is well-known, called ECN
Need new signaling
=> Implementation recommendations are not sufficient

## Slide 18: Deeper fragment forwarding issues #5
Route over => Reassembly at every hop creates a moving blob per packet
Changes the statistics of congestion in the network
Augments the latency by preventing streamlining
More in next slides
=> Need to forward fragments even in route over case

## Slide 19: Current behaviour
 | Sender | Router 1 | Router 2 | Receiver
T=0 | III |  |  | 
T=1 | II(I) | I |  | 
T=2 | I(I) | II |  | 
T=3 | (I) | III |  | 
T=4 |  | II(I) | I | 
T=5 |  | I(I) | II | 
T=6 |  | (I) | III | 
T=7 |  |  | II(I) | I
T=8 |  |  | I(I) | II
T=9 |  |  | (I) | III

## Slide 20: Window of 1 fragment
 | Sender | Router 1 | Router 2 | Receiver
T=0 | III |  |  | 
T=1 | II(I) | I |  | 
T=2 | II | (I) | I | 
T=3 | II |  | (I) | I
T=4 | I(I) | I |  | I
T=5 | I | (I) | I | I
T=6 | I |  | (I) | II
T=7 | (I) | I |  | II
T=8 |  | (I) | I | II
T=9 |  |  | (I) | III

## Slide 21: Streamlining with larger window
 | Sender | Router 1 | Router 2 | Receiver
T=0 | III |  |  | 
T=1 | II(I) | I |  | 
T=2 | II | (I) | I | 
T=3 | I(I) | I | (I) | I
T=4 | I | (I) | I | I
T=5 | (I) | I | (I) | II
T=6 |  | (I) | I | II
T=7 |  |  | (I) | III
T=8 |  |  |  | 
T=9 |  |  |  | 

## Slide 22: Even Deeper fragment forwarding issues #6
Original datagram tag is misleading
Tag is unique to the 6LoWPAN end point
Not the IP source, not the MAC source
2 different flows may have the same datagram tag
Implementations storing FF state can be confused
Solution is well known, called label swapping
An easy trap to fall in, need IETF recommendations

## Slide 23: Datagram Tag Confusion
Fragmentation
Also pick
Datagram tag 5
Pick
Datagram tag 5
Confused

## Slide 24: Even Deeper fragment forwarding issues #6
Forwarding Fragments requires state in intermediate nodes
This state has the same time out / cleanup issues as in the receiver end node
Solution is well known: Proper cleanup requires
  signaling that the flow is completely received
  or reset

## Slide 25: Conclusion
People are experiencing trouble that was predictable from the art of Internet and Switching technologies
The worst of it (collapse under load and hard-to-debug misdirected fragments) was not even seen yet but is predictable
Some issues can be alleviated by Informational recommendations
Some require a more appropriate signaling
Recommendation is rethink 6LoWPAN fragmentation

## Slide 26: draft-thubert-6lo-forwarding-fragments
Provides Label Switching
Selective Ack
Pacing and windowing + ECN
Flow termination indication and reset
Yes it is transport within transport (usually UDP)
Yes that is architecturally correct because fragment re-composition is an endpoint function
And No splitting the draft is not appropriate, because the above functionalities depend on one another.

## Slide 27: RFC 4944: 6LoWPAN Fragmentation
1
0
0
Datagram Tag
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
1
0
Next fragments
1
0
Datagram Offset
1
0
0
Datagram Tag
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
1
0
1st fragment
1
0
Datagram Size
Datagram Size
Size and offset from uncompressed form
1-hop technology

## Slide 28: draft-thubert-6lo-forwarding-fragments
Datagram Tag
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
1
0
ACK
Y <= ECN
Ack bitmap
Ack bitmap
1
0
Y
1
1
1
0
1
1
0
X
Datagram Tag
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
1
0
fragment
X <= ack request
1
1
Datagram Offset
Sequence 0..31
Datagram Size
0
0
1
…
Size and offset from compressed form
…
…
multi-hop technology

## Slide 30: Current behaviour
 | Sender | Router 1 | Router 2 | Receiver
T=0 | III |  |  | 
T=1 | II(I) | I |  | 
T=2 | I(I) | II |  | 
T=3 | (I) | III |  | 
T=4 |  | II(I) | I | 
T=5 |  | I(I) | II | 
T=6 |  | (I) | III | 
T=7 |  |  | II(I) | I
T=8 |  |  | I(I) | II
T=9 |  |  | (I) | III

## Slide 31: Single fragment
 | Sender | Router 1 | Router 2 | Receiver
T=0 | III |  |  | 
T=1 | II(I) | I |  | 
T=2 | II | (I) | I | 
T=3 | II |  | (I) | I
T=4 | I(I) | I |  | I
T=5 | I | (I) | I | I
T=6 | I |  | (I) | II
T=7 | (I) | I |  | II
T=8 |  | (I) | I | II
T=9 |  |  | (I) | III

## Slide 32: Streamlining
 | Sender | Router 1 | Router 2 | Receiver
T=0 | III |  |  | 
T=1 | II(I) | I |  | 
T=2 | II | (I) | I | 
T=3 | I(I) | I | (I) | I
T=4 | I | (I) | I | I
T=5 | (I) | I | (I) | II
T=6 |  | (I) | I | II
T=7 |  |  | (I) | III
T=8 |  |  |  | 
T=9 |  |  |  |