## Slide 1: IPv6 Mesh over Bluetooth(R) Low Energy using IPSP draft-ietf-6lo-blemesh-03
Carles Gomez, S. M. Darroudi
Universitat Politècnica de Catalunya
Teemu Savolainen
DarkMatter
Michael Spörk
Graz University of Technology
IETF 102 – Montreal, July 2018

## Slide 2: Status (I)
  draft-ietf-6lo-blemesh-03
  Last revision, July 2018
  Not updated between Sept 2017 – July 2018
  -02 was considered stable
  Need to validate the draft by means of running code before requesting WGLC
  Slow progress since then
    Several reasons

## Slide 3: Status (II)
  Two paths for implementing the draft
    1. Using Raspberry PIs, BlueZ (Linux BLE stack) as basis
      RFC 7668: One master (6LBR), single slave (6LN) running
      RFC 7668: One master (6LBR), several slaves (6LNs) not working
        BlueZ issue
    2. Using BLEach as basis
    RFC 7668 open source implementation for Contiki
    One master (6LBR) and several slaves (6LNs) running!

## Slide 4: Status (III)
  BLEach RFC 7668 scenario
    CC2650 devices, Contiki OS
    Basis for our implementation work
6LBR
6LN
6LN

## Slide 5: Updates in -03 (I/VIII)
New author
  Michael Spörk, Graz University of Technology (Austria)
  Main author of BLEach
New contributor
  Carlo Alberto Boano, Graz University of Technology (Austria)
In -02, we assumed already established BLE connections
In -03, we detail relationship between 6LoWPAN roles and IPSP roles for connection establishment
  Added text in 3.3.2 (Neighbor Discovery)
  Added Appendix
    Example of 3.3.2

## Slide 6: Updates in -03 (II/VIII)
3.3.2. Neighbor Discovery, item 3.b)
  Section 6.2 of RFC 6775, for dynamic config. scenarios
    6LR comes up as a non-router
    6LR waits for an RA to configure its own interface address first, and turns to a router
  In order to support the same operation:
    6LR starts by using the IPSP Node role only
    A previously existing IPSP Router establishes a BLE connection with the 6LR, which receives an RA from that router
    The 6LR configures its interface address, it turns into a router, and runs as an IPSP Router
    6LBR runs as an IPSP Router from the beginning

## Slide 7: Updates in -03 (III/VIII)
Appendix: example
  Step 1

## Slide 8: Updates in -03 (IV/VIII)
Appendix: example
  Step 2

## Slide 9: Updates in -03 (V/VIII)
Appendix: example
  Step 3

## Slide 10: Updates in -03 (VI/VIII)
Appendix: example
  Step 4

## Slide 11: Updates in -03 (VII/VIII)
Appendix: example
  Step 5

## Slide 12: Updates in -03 (VIII/VIII)
Appendix: example
  Step 6

## Slide 13: Related work: Bluetooth SIG
“Bluetooth Mesh” specification
  Published in July 2017
  BLE Mesh networking
  (Controlled) Flooding over advertising channels
    Note: RFC 7668 assumes link-layer connections over data channels for IPv6 over BLE