## Slide 1: Transmission of IPv6 Packets over PLC Networks draft-hou-6lo-plc-04
Jianqiang Hou (Huawei)
Bing Liu (Huawei)
Yong-Geun Hong (ETRI)
Xiaojun Tang (State Grid EPRI)
Charles Perkins (Futurewei)
IETF 102 – Montreal, July 2018

## Slide 2: Status
draft-hou-6lo-plc-04
  Updated Parts
    Formally include IEEE 1901.1 into the scope
    Address autoconfiguration and mapping designed for IEEE 1901.1
    Add RFC 6775-update features to Neighbor Discovery
Charlie Perkins and Bing Liu become co-authors

## Slide 3: Recently published IEEE 1901.1 Standard
IEEE 1901.1: IEEE Standard for Medium Frequency (less than 12 MHz) Power Line Communications for Smart Grid Application
  Published in May 2018
  https://standards.ieee.org/findstds/standard/1901.1-2018.html
Technical Characteristics
  TDMA and CSMA/CA support
  OFDM
  Fragmentation and reassembly, improving the transmission efficiency
  Data retransmission
  AES/3DES/DES data encryption
  Incident processing with four levels of priorities for differentiated QoS
  Data rate up to 2Mbps

## Slide 4: Stateless Address Autoconfiguration
64-bit IID derived from long address
  Based on the EUI-64 ID or EUI 48 MAC (extended to 64-bit by inserting 0xFFFE)
  Set the U/L (7th bit of the first byte) to 1 and G/I (8th bit of the first byte) to 0
64-bit IID derived from short address:
YYYY:YYFF:FE00:0XXX
24-bit NID (Network Identifier)
12-bit TEI (Terminal Equipment Identifier)
  U/L bit and G/I bit set to 0.
  To avoid any ambiguity in the derived Interface ID, these two bits MUST NOT be used to generate the NID (for IEEE 1901.1) or PAN ID (IEEE 1901.2, ITU-T G.9903).
MMMM:00FF:FE00:NNNN
16-bit Short address
16-bit PAN ID
IEEE 1901.1
IEEE 1901.2 and
ITU-T G.9903

## Slide 5: Unicast Address Mapping
IEEE 1901.1
IEEE 1901.2 and
ITU-T G.9903
Link layer address option can be used in Neighbor Discovery to resolve Link layer address and to suppress the broadcast in RA/RS and NA/NS.

## Slide 6: Using RFC 6775-update for Neighbor discovery
RFC6775-update PLC devices include the EARO with the 'R' flag set when sending Router Solicitations, and process Router Advertisements that include EARO to extract status information.
Duplicate Address Detection is in this case proxied by a routing registrar, which MAY operate according to Optimistic DAD (ODAD) [RFC4429].
For networks with mixed RFC6775-only and RFC6775-update devices, the RFC6775-update PLC devices MUST use a 64-bit ROVR for backward compatibility.

## Slide 7: Future Work
Next Steps
  WG Adoption?
Welcome feedback!