## Slide 1: RFC 6775 Extension
IETF 102
Montreal
P.Thubert, E. Nordmark, S. Chakrabarti, C. Perkins

## Slide 2: Unmet expectations
Solicited node multicast requires highly scalable L2 multicast
  IEEE does not provide it => turns everything into broadcast
  IPv6 ND appears to work with broadcast on 802.1 fabrics up to some scale ~10K nodes
IPv6 ND requires reliable and cheap broadcast
  Radios do not provide that => conserving 802.1 properties over wireless is illusory
  RFC 4862 cannot operate as designed on wireless
  Address uniqueness is an unguaranteed side effect of entropy
802.11 expects proxy operation and broadcast domain separation
  802.11 provides a registration and proxy bridging at L2
  Requires the same at L3, which does not exist
  Implementations provide proprietary techniques based on snooping => widely imperfect
  RFC 6775 solves the problem for DAD in one LL
  This update enable establishing proxy services directly (ND for now), over a LLN, across multiple LLNs

## Slide 3: What are the 6LoWPAN ND extensions?
  Provide for draft-thubert-6lo-rfc6775-update-reqs
  draft-ietf-6lo-rfc6775-update
        Simplifies the protocol (no DAR/DAC for LL, no secondary NC)
        Enables proxy registration
  draft-ietf-6lo-ap-nd
        Protects addresses against theft (Crypto ID in registration)
  draft-ietf-6lo-backbone-router
        Federates 6lo meshes over a high speed backbone
        ND proxy that mimics 802.11 association but at Layer 3

## Slide 4: RFC 6775 Update
P.Thubert, E. Nordmark, S. Chakrabarti, C. Perkins

## Slide 5
6LR
6LBR
6BBR
Router/Server
LP Node
Radio Mesh
Ethernet
RA (unicast)
RA (u|mcast)
Router/Server
Router/Server
Ethernet
Radio 1 Hop
SLLA
6CIO
PIO
MTU
SLLA
CONTEXT
6CIO
PIO
MTU
SLLA
CONTEXT
ABRO
6CIO
PIO
MTU
RA (u|mcast)
RS (mcast)
RA (u|mcast)
PIO
MTU
SLLA
Classical ND
RFC 6775 update
RFC 6775 update
RFC 6775 update

## Slide 6
6LR
6LBR
6BBR
Router/Server
LP Node
Radio Mesh
Ethernet
NS DAD (ARO)
NS (EARO)
NS (ARO)
EDAR
Router/Server
Router/Server
Ethernet
Radio 1 Hop
SRC = UNSPEC
DST = SNMA
TGT = LPN
UID = LPN
TID included
SRC = 6LR *
DST = 6LBR
REG = LPN
UID = LPN
TID included
SRC = LPN_LL *
DST = 6LR_LL *
TGT = LPN **
SLLA = LPN
UID = LPN
TID included
opt: AP-ND
SRC = 6LBR
DST = 6BBR *
TGT = LPN
SLLA = 6LBR
UID = LPN
TID included
* Global / ULA
* Can be Anycast
Create binding state
Create proxy state
* link local unique EUI-64
** ULA or GUA
6LR
6LBR
6BBR
Router/Server
LP Node
Router/Server
Router/Server
Classical ND
RFC 6775 update
RFC 6775 update
RFC 6775 update

## Slide 7
6LR
6LBR
6BBR
Router/Server
LP Node
Radio Mesh
Ethernet
NA (O) *
NA (EARO)
NA (ARO)
EDAC
Router/Server
Router/Server
Ethernet
Radio 1 Hop
SRC = 6LR
DST = 6LBR
REG = LPN
UID = LPN
TID included
SRC = 6LR_ll
DST = LPN_ll
TGT = LPN
TLLA = LPN
UID = LPN
TID included
SRC = 6BBR
DST = 6LBR
TGT = LPN
TLLA = L6BR
UID = LPN
TID included
* Omitted in general
** link local
DAD time out
SRC = 6BBR_ll **
DST = NS SRC
TLLA = L6BR
TGT = LPN
6LR
6LBR
6BBR
Router/Server
LP Node
Router/Server
Router/Server
Classical ND
RFC 6775 update
RFC 6775 update
RFC 6775 update

## Slide 8: IESG Review (cont.)
RFC 6775 Update
Draft-…-17 to - 18

## Slide 9: Need to vs. MUST on operator behaviour
From Dave Thaler (added in 17)
  “ In order to deploy this, network administrators MUST ensure that 6LR/6LBRs
  in their network support the number and type of devices that can register to
  them, based on the number of IPv6 addresses that those devices require and
  their address renewal rate and behavior. “
Final text (since 18, with help from Warren Kumari and Ben Campbell)
  “ Network
  administrators need to ensure that 6LR/6LBRs in their network support
  the number and type of devices that can register to them, based on
  the number of IPv6 addresses that those devices require and their
  address renewal rate and behavior.
  “

## Slide 10: Mirja Kühlewind (in -18)
TID Should be zero if the T flag is not set => text added
Draft reads better if section 6 moves up
-21 -17

## Slide 11: Benjamin Kaduk (in -18)
« In general the Security and Privacy Considerations seem well thought-out « ^ ^
Non Zero status: an error?
  RFC 6775 section 8.2.5 has "In the case where the DAC indicates an error (the Status is non-zero)
ROVER definition (ended up with text below, later split in the document)
Enables the correlation between multiple attempts to register a same
IPv6 Address. The ROVR is stored in the 6LR and the 6LBR in the state
associated to the registration.
This can be a unique ID of the Registering Node, such as the EUI-64
address of an interface. This can also be a token obtained with
cryptographic methods which can be used in additional protocol exchanges
to associate a cryptographic identity (key) with this registration
to ensure that only the owner can modify it later.
The scope of a ROVR is the registration of a particular
IPv6 Address and it cannot be used to correlate registrations of
different addresses.

## Slide 12: Eric Rescorla (in -18)
« I found this document quite challenging to read. It would be very helpful if it started with a description of the failings of 6775 and a brief overview of how it solves those. »
  Text below was proposed, applied in 18. Upon Charlie’s later review, some migrated to Annex with reqs.
  Missing Eric’s validation. What should we do, put back back in intro or leave in annex?
This specification updates 6LoWPAN ND to simplify the registration
operation in 6LoWPAN routers and to extend the protocol as a more
generic registration technique. The specified updates enable other
specifications to define new services such as Source Address
Validation (SAVI) with [I-D.ietf-6lo-ap-nd], participation as an
unaware leaf to an abstract routing protocol such as the "Routing
Protocol for Low Power and Lossy Networks" [RFC6550] (RPL) with
[I-D.thubert-roll-unaware-leaves], and registration to a backbone
routers performing proxy Neighbor Discovery in a Low-Power and Lossy
Network (LLN) with [I-D.ietf-6lo-backbone-router].

## Slide 13: Eric Rescorla (in -18)
« Can you describe here the problem that ARO has that this solves?»
  Text below was proposed, applied in 18. Upon Charlie’s later review, somewhat reworded later
  Missing Eric’s validation.
The Address Registration Option (ARO) is defined in section 4.1 of
[RFC6775]. This specification introduces the Extended Address
Registration Option (EARO) based on the ARO for use in NS and NA
messages. The EARO conveys additional information such as a sequence
counter called Transaction ID (TID) that is used to determine the
latest location of a registering mobile device. A 'T' flag is added
to indicate that the TID field is populated.
The EARO also signals whether the 6LN expects routing or proxy
services from the 6LR using a new 'R' flag.
The EUI-64 field is overloaded and renamed ROVR in order to carry
different types of information, e.g., cryptographic information of
variable size. A larger ROVR size may be used if and only if
backward compatibility is not an issue in the particular deployment.

## Slide 14: Eric Rescorla (in -18)
Cross check with AP ND, fixed mismatch in Leftmost vs. Rightmost bits
Misc. Clarifications
More comments / fixes on the ROVR field, e.g., be very specific on the length

## Slide 15: Ben Campbell (in -18)
Down references added during IESG review in terminology section
  Not really solved to date. Created a separate reference section
  11.2. Terminology Related References
  [RFC4919] Kushalnagar, N., Montenegro, G., and C. Schumacher, "IPv6
  over Low-Power Wireless Personal Area Networks (6LoWPANs):
  Overview, Assumptions, Problem Statement, and Goals",
  RFC 4919, DOI 10.17487/RFC4919, August 2007,
  <https://www.rfc-editor.org/info/rfc4919>.
  [RFC6606] Kim, E., Kaspar, D., Gomez, C., and C. Bormann, "Problem
  Statement and Requirements for IPv6 over Low-Power
  Wireless Personal Area Network (6LoWPAN) Routing",
  RFC 6606, DOI 10.17487/RFC6606, May 2012,
  <https://www.rfc-editor.org/info/rfc6606>.

## Slide 16: Final fixes
RFC 6775 Update
Draft-…-19 to - 21

## Slide 17: Charlie Perkins
As an author and native speaker, Charlie made a final pass on the language and the organization
Found that text was repeated, other was scattered
Fixed the language, regrouped items
E.g., took functional text out of the definition, to appropriate section
Also removed extraneous references
Work happened over draft 19-21

## Slide 18: Issue 1: EDAR / EDAC extensibility
The size of the ROVR was inferred from the size of the message
Did not leave a possibility to insert options
This might be desirable in the future, e.g., MAC Address option for a MAP server
Long discussion, tried multiple possibilities
Ended up with split ICMP Code, similar to what we discussed with Adrian Farrell
Added in draft -20

## Slide 19: RFC 6775 update new features: ICMP code split
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type |CodePfx|CodeSfx| Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Status | TID | Registration Lifetime |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
... Registration Ownership Verifier (ROVR) ...
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+ Registered Address +
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Code: The ICMP Code [RFC4443] for Duplicate Address
Messages is split in two 4-bit fields, the Code
Prefix and the Code Suffix.

## Slide 20: RFC 6775 update new features: ICMP code split
Code:
The ICMP Code [RFC4443] for Duplicate Address
Messages is split in two 4-bit fields, the Code
Prefix and the Code Suffix. The Code Prefix MUST be
set to zero by the sender and MUST be ignored by the
receiver. A non-null value of the Code Suffix
indicates support for this specification. It MUST be
set to 1 when operating in a backward-compatible
mode, indicating a ROVR size of 64 bits. It MAY be
2, 3 or 4, denoting a ROVR size of 128, 192, and 256
bits, respectively.

## Slide 21: Issue 2: Enabling Other Routing Registrars
6BBR is only one possible routing registrar. Others include
  RPL [I-D.thubert-roll-unaware-leaves] and
  RIFT [I-D.ietf-rift-rift]
Resolution to use a generic term as opposed to mention 6BBR specifically
Also allow an opaque field. RPL uses it for instance ID.
Added in draft -19
Generalization to the term « routing registrars » in -21

## Slide 22: RFC 6775 update new features: the Opaque field
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Status | Opaque |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Rsvd | I |R|T| TID | Registration Lifetime |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
... Registration Ownership Verifier (ROVR) ...
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Opaque:
An octet opaque to ND; the 6LN MAY pass it
transparently to another process. It MUST be set to
zero when not used.

## Slide 23: RFC 6775 update new features: the I field
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Status | Opaque |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Rsvd | I |R|T| TID | Registration Lifetime |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
... Registration Ownership Verifier (ROVR) ...
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
I: Two-bit Integer: A value of zero indicates that the
Opaque field carries an abstract index that is used
to decide in which routing topology the address is
expected to be injected.

## Slide 24: IESG Review (past)
RFC 6775 Update
Draft-…-12 to -16, presented at IETF 101

## Slide 25: INT-DIR (Tim Chown) => v-12
Use of EUI-64, should it be deprecated (for privacy reasons) ?
Clarifications on privacy addresses
Added a matrix matching specs and requirements in appendix
Added a glossary
Suggestion to ask 6MAN about the need for a LRU algorithm

## Slide 26: OPS-DIR (Jürgen Schönwälder) + SEC-DIR (Chris Lonvick) => v-13
Moved terminology up for readability
Changed “legacy” to “RFC6775-only” referering to RFC 6775
Changed OUI field to RUID
Added Appendix B.7.
  “Requirements Related to Operations and Management”

## Slide 27: IOT-DIR (Dave Thaler) => v-14
Reworded Intro (and many other things)
Introduced the ‘R’ flag based on parallel discussion with ROLL
Reworded RUID description
Limiting the number of addresses => What is the minimum?
Clarification on address duplication over backbone

## Slide 28: RTG-DIR (Adrian Farrel) => v-15
RUID => ROVR Registration Ownership Verifier ; new text on ROVR functionality and collision scope and consequences
6CIO now the only way to discover 6LR capabilities. New flag for 6LBR capability to support extended DA messages
Use of ICMP code: non-NULL code => Extended DA message
EARO Length extended due to side discussion on AP-ND

## Slide 29: GEN-ART (Peter Yee) => v-16
Clarifications, e.g., RECOMMENDED for implementations
How properties are discovered (completing Adrian’s review)
Review of the requirements and security section
Clarified / fixed IEEE references
A lot of editorials, syntax corrections

## Slide 30: draft-ietf-6lo-ap-nd
P.Thubert, B. Sarikaya, M Sethi, (and expecting R. Struik but not there yet)

## Slide 31: Unmet expectations
First come first Serve address registration
  First registration for an address owns that address till it releases it
  The network prevents hijacking
Source address validation
  Address must be topologically correct
  Source of the packet owns the source address
First Hop Security only?
  Proxy ownership and routing advertisements not protected yet

## Slide 32: Recent changes
Simplified the computation of the Crypto-ID
  Digital signature (SHA-256 then either NIST P-256 or EdDSA) is executed on the concatenation of short modifier and public key
  Modifier not used to make computation complex as opposed to CGA. This simplifies the operation of a constrained node
  But 64 bits ROVR might not suffice for adequate protection => Longer ROVR
Reuse options defined in RFC 3971 for SEND
  Crypto-ID Parameters Option, a variation of the CGA Option
  Nonce Option
  NDP Signature Option, a variation of the RSA Signature Option
  the option is extended for non-RSA Signatures
  this specification defines an alias to avoid the confusion.

## Slide 33: Security properties
We made the size of the ROVR tunable so we can get high security
At the moment a joining 6LN is challenge from the 6LR
  The 6LBR MUST trust the 6LR
  A rogue 6LR may pretend that it represents a 6LN that passed the challenge
  Should we challenge all the way from the 6LBR?
  Can the Crypto-ID be used in routing protocols, how?

## Slide 34: AP-ND Status, talks with Eric Rescorla
Quite Stable, not republished since IETF 101
Fixed inconsistency with RFC 6775 update in RFC 6775 update (Eric Rescorla)
Multiple talks to sync with Eric, but then no change done yet.
Need to clarify key encoding
  Draft uses DER. Behcet recommended lihter like Jason Web Key.
  Eric: “Aren't you using EC keys? If so, why do you need *either* encoding.” ?
Remove text on 64-bits identifiers since ROVR is up to 256 bits
256 bits solves many concerns about security that Eric had.

## Slide 35
6LR
LP Node
NS (EARO, CIPO*, Nonce and NDPSO**)
Radio 1 Hop
6LR
6LN
AP-ND
NA (EARO(status=0))
NS (EARO(ROVR=Crypto-ID))
NA (EARO(status=Validation Requested), Nonce)
* Crypto-ID Parameters Option
** NDP Signature Option
6LBR
Radio Mesh
EDAR
6LBR
RFC 6775 update

## Slide 36: draft-ietf-6lo-backbone-router
P.Thubert

## Slide 37: Unmet expectations
Scale an IOT subnet to the tens of thousands
  With device mobility (no renumbering)
  Controlled Latency and higher Reliability using a backbone
Deterministic Address presence
  Route towards the latest location of an address
  Remove stale addresses

## Slide 38: Recent changes
Uses of the ‘R’ flag
  Indicates the need for proxy operation
Clarifications
TBD : RPL Root / 6LBR separation

## Slide 39
6LR
6LBR
6BBR
Router/Server
LP Node
RPL
Ethernet
NA (~O)
NS (EARO)
Proxy NS (EARO)
RPL DAO
Router/Server
Router/Server
Ethernet / Wi-Fi
Radio 1 Hop
Classical ND
RFC 6550
RFC 6775 update
RFC 6775 update
NA (EARO)
DAO-ACK
NA (EARO)
6LR
RPL Root
6BBR
Router/Server
LP Node
Router/Server
Router/Server
NS lookup
Packet

## Slide 40
6LR
6LBR
6BBR
Router/Server
LP Node
RPL
Ethernet
NA (~O)
NS (ARO)
NS (ARO)
RPL DAO
Router/Server
Router/Server
Ethernet
Radio 1 Hop
SRC = 6BBR
DST = NS SRC
TGT = LPN
TLLA = 6LBR
SRC = 6LR
DST = Parent *
or Root
TGT = LPN
ROVR missing : (
TID included
SRC = LPN_ll
DST = 6LR_ll
TGT = LPN
SLLA = LPN
UID = LPN
TID included
SRC = 6LBR
DST = 6BBR
TGT = LPN
SLLA = L6BR
UID = LPN *
TID included
* Parent in storing mode
* From binding state
NS lookup
RPL
cannot DAD
for lack
of ROVR
6LR
6LBR
6BBR
Router/Server
LP Node
Router/Server
Router/Server

## Slide 41: 6BBR Status
Quite Stable, not republished since IETF 101
WGLC?