## Slide 1: BIER Multicast Overlay for HTTP Response https://tools.ietf.org/html/draft-purkayastha-bier-multicast-http-response-00
Debashish Purkayastha, Dirk Trossen, Akbar Rahman,
Toerless Eckert
IETF-102, BIER WG, July 2018

## Slide 2: Recap : Multicast HTTP using BIER
Draft “Multicast HTTP using BIER” (https://tools.ietf.org/html/draft-purkayastha-bier-multicast-http-00.html) describes:
  Example realization of the use case (https://tools.ietf.org/html/draft-ietf-bier-use-cases-06#section-3.10 )
  A Few requirements
Operational details were described
  Required Functional elements
    PCE
    Service Router
  Suggested Protocols
    Between Service Routers and PCE, Registration with PCE
2
102 IETF, Montreal

## Slide 3: Reference Architecture over BIER
The multicast overlay is formed by the BFIR and BFER of the BIER layer and the additional SR (Service Handler) and PCE (Path Computation Element) elements
3
102 IETF, Montreal

## Slide 4: Realization over IPMC
“HTTP Response Multicast” maybe realized over IP Multicast (IPMC)
  Require support for group formation, maintain group state and IGMP signaling to join a group
For fewer receivers
  Many of the bitrates may not be required and dropped by the CNAP
  Extremely high and undesirable amount of IP multicast signaling protocol activity (PIM/IGMP)
4
102 IETF, Montreal

## Slide 5: Realization over BIER
Components
  SR : terminates application level protocols, extracts the URI to determine the PATH ID via PCE request
  PCE : keeps track of all service execution end points and how to reach them. (can be part of BIER-TE)
  Interface functions to BFIR where the PATH ID is mapped to BIER header
Achieving Multicast
  SNAP simply coalesces the forwarded HTTP requests from the CNAP, and determines for every requested block the set of CNAPs requesting it
  A set of CNAPs corresponds to a set of bits in the BIER-bitstring, one bit per CNAP
  The SNAP then sends the block into BIER with the appropriate bitstring set
5
102 IETF, Montreal

## Slide 6: Advantages of Realization over BIER
Eliminates any dynamic multicast signaling between CNAP and SNAP
Avoid sending of any unnecessary data block, which in the IP multicast solution is pretty much unavoidable
SNAP can also easily control how long to delay sending of blocks
  For example, it may wait for some percentage of the time of a block (e.g, 50% = 1 second), ensuring that it is coalescing as many requests into one BIER multicast answer as possible
6
102 IETF, Montreal

## Slide 7: Next steps
We suggest to include an additional Applicability Statement documenting “How BIER can be applied to aggregate HTTP responses over a BIER infrastructure”
  The draft will elaborate on the solution to support the applicability statement
7
102 IETF, Montreal