## Slide 1: draft-ietf-bier-mld-01 BIER Ingress Multicast Flow Overlay using Multicast Listener Discovery Protocols
Pierre Pfister, pierre.pfister@darou.fr
IJsbrand Wijnands, ice@cisco.com
Markus Stenberg, markus.stenberg@iki.fi
Stig Venaas, stig@cisco.com
Cui (Linda) Wang, lindawangjoy@gmail.com
Zheng (Sandy) Zhang, zhang.zheng@zte.com.cn

## Slide 2: BIER MLD/IGMP
MLDv2/IGMPv3 overlay is used to inform ingress BIER routers which egress BIER routers should receive which flows
Added text about MTU
  IGMPv3 reports can get big by including a large number of groups
  Need to make sure report is not too big to reach all potential ingress routers
  One can use a safe configurable value, or rely on MTU discovery
  Prefer to minimize the number of messages by using the maximum size possible
No other changes
Uses configurable multicast groups for all BMLD queriers/nodes
  Prefer not to make use of existing groups for all-nodes and all MLDv2 routers as it is domain-wide rather than link-local
    Depends whether we regard BIER as one hop, as a single link.
  Allow multiple instances, e.g. multiple sub-domains, by using different group addresses
    Most deployments probably need only 1 instance.
  Should we request new well-known groups from IANA to simplify configuration?
  IGMP overlay requires no configuration if we do this.