## Slide 1: draft-venaas-bier-mtud-01
Stig Venaas, stig@cisco.com
Mahesh Sivakumar
IJsbrand Wijnands, ice@cisco.com
Les Ginsberg, ginsberg@cisco.com

## Slide 2: BIER MTU discovery
MTU basics
MTU discovery
What discovery options do we have?
draft-ietf-bier-path-mtu-discovery provides MTU discovery
  But probe based and only gives MTU for current receiver set and paths
  If anything changes, need new probe to find new MTU
Idea is to find an MTU value that is mostly stable and can be used for all BIER packets in a sub-domain, rather than finding the optimal MTU per receiver set and path

## Slide 3: MTU basics
For an IP packet to reach its destination it must be small enough to traverse all the links to the destination.
  The size must not exceed the IP MTU of any of the links on the path
Fragmentation by routers (in-flight fragmentation)
  An IPv4 packet without DF (Don’t Fragment) set is fragmented as needed
  If a router determines it is too big for the out-going interface, it fragments the packet
Fragmentation by hosts (and routers when originating packets)
  IPv6 packets and IPv4 packet with DF are not fragmented when being forwarded
    Link layer may provide fragmentation though (including tunneling)
  Originator needs to ensure packet is small enough
For IPv6 and IPv4 DF, originator can ensure the datagram is small enough
  Applications can be configured with a safe size, or use e.g., a socket option
  TCP can also adjust, but we are interested in multicast here.
What size is small enough?
  Use a safe minimum? 1500, 1280, or less? Use MTU recommended by network admin?
  Use MTU of the host interfaces, assuming no link on the path has a smaller MTU?
  MTU discovery?

## Slide 4: MTU discovery and BIER
MTU discovery allows originator to send packets at an optimal size
  Application/TCP can send packets at the optimal size, no fragmentation
  Fragmented packets can be split in the fewest possible number of fragments
  Optimal size means less packets originated and forwarded
  With BIER pim/igmp overlays we want to maximize pim J/P and igmp reports (many groups in each)
IP Path MTU discovery
  IPv6 usually performs PMTUD (unless assuming max 1280), optional for IPv4 (use of DF)
  When a router determines packet too big for the outgoing interface, it sends an ICMP message to the IP source address with the max allowed value
  This might happen multiple times along the path, and when the path changes.
  Host stack starts with a default MTU for a destination and adjusts it based on ICMP responses
BIER In-flight fragmentation a bad idea
  With BIER it would require decap, IP fragmentation, reencap etc, or BIER fragments
MTU discovery and BIER
  Can do IP PMTUD where BFR sends ICMP response to the source.
    Requires decapsulation and reachability to the source. Possibly relay message via BFIR
  If BFIR knows what MTU is safe across the BIER domain for the specified receiver set, it can send ICMP to the source
  If BFIR/BFER knows the BIER MTU, it can use it for pim/IGMP overlay (j/p report size)

## Slide 5: BIER MTUD solutions
How can a BFIR know/learn the MTU that can be used?
  For a given flow the exact BIER path MTU depends on the path/tree, which depends on the receiver set and entropy
Configuration of safe value, all BIER links have same MTU?
PMTUD similar to IP (no current proposal)
  A BFR signals BFIR (source) when data packet is too big for an OIF
    New BIER message, BIER encapsulated ICMP message?
PMTUD based on probing
  draft-ietf-bier-path-mtu-discovery
  Relies on probes following same path as the data
  Potentially slower recovery than the above when topology changes
Sub-domain MTUD (this draft)
  A compromise. Not optimal. “Weakest link” (the link with the smallest MTU) in the sub-domain determines the MTU.

## Slide 6: BIER Sub-domain MTUD
“Weakest link” (thinnest) in the sub-domain determines the MTU
MTU will often not be optimal, but better than a safe default
  An admin could potentially configure the same with full knowledge of the topology, but would also need to reconfigure all routers if the weakest link MTU changes.
No probing or data triggered signaling
No new message types, instead a new IGP sub-TLV
Independent of which BIER links a flow traverses
  Robust, not impacted by receiver set changes or most routing/topology changes*
  Less per flow state
Only possible topology change impact is if the “weakest link” goes down
  This may cause the sub-domain MTU to increase
  Draft proposes dampening, it is not urgent to learn the bigger MTU
    Avoids MTU updates if the link is flapping
May be combined with BIER PMTUD solutions
  One may use this MTU as an initial value, but for selected flows increase the MTU based on PMTUD

## Slide 7: BIER MTUD issue 1
What MTU should be advertised?
  It appears the text in the draft may be ambiguous
Draft tries to say that routers advertise BIER payload MTU (option 1)
  That is, how big an IP packet can be encapsulated
Should it be the largest possible BIER packet? (option 2)
  Size of IP packet plus BIER encapsulation, size after encapsulation.
We need BFIR to learn the BIER payload MTU
  With option 1, BFIR uses the smallest advertised value. Each BFR considers which encapsulations are used on the different links (or to different neighbors) to determine what to announce
  With option 2, BFIR can subtract the max encapsulation overhead for all BIER encapsulations (all defined, or all known to be deployed in the domain)
  Option 2 likely simpler. But it may depend on how multiple encapsulations may be used. Can we have multiple encapsulations in a BIER domain, in an IGP area, on a single link? Can the encapsulation change as a packet is forwarded?
Encapsulation needs to be considered by all MTU discovery mechanism

## Slide 8: BIER MTUD issue 2
How to handle tunneling or repair-paths that require additional encap?
Have not given this much thought yet. Also applies to other discovery mechanisms.
If a neighbor is known to be reachable only via tunneling, then that affects what is the biggest BIER payload that can be sent to that neighbor, so this is already taken care of in the draft.
Not sure how to handle a dynamic event such as a repair path
  Could potentially announce a new smaller MTU when repair is in place, but the goal is to have a fairly static MTU value. Hence a router supporting use of repair paths should probably announce an MTU that allows for reaching the neighbors via a repair path.