## Slide 1: BIER Penultimate Hop Popping draft-zzhang-bier-php-00
102th IETF, Montreal
Zhaohui (Jeffrey) Zhang

## Slide 2: Use Case
An MVPN/EVPN deployment with enough P/PE routers capable of BIER to benefit from using BIER as provider tunnel
We know how to deal with BIER incapable P routers
What if some PE routers are not BIER capable?

## Slide 3: BIER Incapable Egress PE
A BIER capable Ingress PE would have to send traffic via BIER to BIER PEs and via traditional tunnels to incapable PEs
  Complicated & inefficient
What if an incapable egress PE pretends it supports BIER, but requests the upstream BFR to pop the BIER header?
  Transparent to other PEs

## Slide 4: BIER PHP
A BIER incapable router signals BIER information but requests other BFRs to pop the BIER header and send traffic “natively”
  Those BFRs do not have to be directly connected
    There could be incapable P routers in between – traffic could be tunneled
PHP requested via
  PHP sub-sub-TLV in BIER sub-TLV
    MPLS and non-MPLS encapsulation
  Implicit Null Label as label range base
    In MPLS Encapsulation sub-sub-TLV

## Slide 5: Conditions for PHP
Egress PE must be able to demultiplex the payload w/o the BIER header
  IP payload: must be in the address space for the BIER routing underlay
  MPLS payload: top of the label stack must be “downstream assigned” by the egress PE
    DCB labels considered as “downstream assigned”
      Draft-ietf-bess-mvpn-evpn-aggregation-label
  VXLAN/NVGRE: should be fine
  Others: For further study

## Slide 6: BIER Incapable Ingress PE
Have BIER capable PEs relay traffic from incapable Ingress PEs
  MVPN: Virtual Hub & Spoke (RFC 7024)
  EVPN-mpls: Virtual Hub & Spoke
    draft-keyupate-bess-evpn-virtual-hub
  EVPN-overlay: Assisted Replication
    draft-ietf-bess-evpn-optimized-ir

## Slide 7: Next Steps
Seek WG comments
Seek WG adoption