## Slide 1: BIER Brownfield Migration Frameworks draft-przygienda-bier-migration-options
BIER WG
IETF102# Montreal
Tony Przygienda
Jeffrey Zhang
Juniper

## Slide 2: Why
BIER moved from “will it happen?” to “how do I brownfield BIER”
We don’t have the luxury of greenfield deployments but that should not be a surprise
Customers have different technology mixes in their networks and different comfort levels, timelines to introduce new ones
This draft allows a “guided” framework what “brownfield” options are available and their properties

## Slide 3: What
Draft holding possible frameworks to brownfield BIER layer with
  IGP underlay
  Controller “underlay”
Different solutions to get “around” or “through” non-BFRs
BIER overlay is not in scope of this draft

## Slide 4: Frameworks
IGP Multi-Topology Only
IGP RFC 8279 Section 6.9
BIER Specific Algorithm (BAR)
Controller

## Slide 5: Multi Topology Only Solution
Confine BFRs in own on multi-topology
Properties
  Needs MT deployed
    MT has been around for different purposes since many years
  MT can be connected by any tunnel that looks like L3
  Allows for unicast and multicast path to BFER to deviate
  “Partial” BFR routers are possible where only some interfaces support BIER
  Standard IGP computation and protection in IGP used
  Links can be in multiple MTs at the same time and used as 2ndary backup for each other since IGP metric is per MT
  tunnel & IGP link metrics may end up doing ECMP
  Any change necessitates “touching” the link configuration on both sides

## Slide 6: Section 6.9 Solution, Modified Step 2)
”Re-parenting” solution RFC 8279 section 6.9 mod’ed step 2)
Properties:
  When dynamic tunnel technologies (like SR) are deployed and used
    Can “tunnel through” any non-BFR without additional configuration
    Provide immediate full node protection coverage
    Tunnels do not show up in IGP as Fas
    Each change in tunnel signaling may lead to BIFT recomputation
    They normally lack OAM available with static tunnels
  BIER multicast traffic path to BFER is same as unicast

## Slide 7: BIER Specific Algorithm
Use a signaled BAR to compute paths that guarantee black-hole-free BIER in a distributed fashion
Properties
  Tunnels necessary if no direct BFR-only path available
  Can take into account things like fan-out-degree or subdomain inter-dependencies or partial BFR support (with more BIER TLVs)
  Unicast and multicast path to BFER can diverge
  Computation of all IGP protections is possible

## Slide 8: Controller Based Solutions
Controllers are “omnipotent” and see whole topology
  Quis custodiet ipsos custodes?
Controller downloads computed BIRTs and/or BIFTs (that’s the r/w object in Yang model discussion)
Properties:
  Anything can be taken into account on computation
  Signaling that a node is using controller based BIER tables is desirable operationally
  Failure re-convergence slower than IGP
    Backup tables/next-hops for a single failure scenario could be also controller computed