## Slide 1
Use of BIER Entropy for Data Center CLOS Networks
draft-xie-mboned-bier-entropy-staged-dc-clos-00
Jingrong Xie, Mike McBride, Gang Yan
@Huawei
Xiaohu Xu
@Alibaba Inc
Notes: 26/7/28
<number>

## Slide 2: Problem Statement
Describes how BIER Entropy can be useful in DC CLOS networks.
Large, long lived elephant flows may affect performance of smaller short lived flows and reduce efficiency of per flow load sharing.
Due to ECMP hash function inefficiencies it is possible to have frequent flow collisions. More flows get placed on one path over the others.
Isolating faults in the network with multiple parallel paths and ECMP based routing is non trivial due to lack of determinism.
When BIER is deployed in a multi-tenant data center network for efficient delivery of BUM, an operator may want a deterministic path.
A deterministic path for a multicast path in the DC, with multiple staged equal cost paths, is comparable to a traffic-engineering path defined in ietf-mpls-spring-entropy-label with multiple hop equal cost paths.
A deterministic path can be found by part of the 20 bit entropy field. Bit 0 to bit 2 of entropy label can represent a value of 0 to 7, and can be used to select a deterministic path from 8 equal cost paths.

## Slide 3: Problem Statement
DC-CLOS network: 3 layers, 5 stages, Northwards Stages (stage 1 & 2) have rich ECMP.
Problem 1: Steering for elephant flows (A1->C1->S1-->A2)
Problem 2: Path Division for Tenant flows to different SIs (A1->C1->S1-->A2, A1->D1->S4-->A3)
C1
D1
A1
B1
S1
S2
S4
S5
C2
D2
A2
B2
S3
S6
stage1
stage2
stage3
stage4
stage5
POD2
bfr-id 11-12
POD1
bfr-id 1-2
C3
D3
A3
B3
POD30
bfr-id 301-302

## Slide 4: Solution by using BIER Entropy
Stage 1: use bit[0] of the 20-bit Entropy to represent RED and BLUE path.
Stage 2: use bit[1~2] of the 20-bit Entropy to represent 3 paths to each RED/BLUE cluster.
Similar to the [ietf-mpls-spring-entropy-label] for multi-stage ECMPs along a path by breaking the 20-bit BIER Entropy.
C1
D1
A1
B1
S1
S2
S4
S5
C2
D2
A2
B2
S3
S6
stage1
stage2
POD2
POD1
C3
D3
A3
B3
POD3

## Slide 5: Local convergence and global optimization
For a flow from A1, originally using Entropy[0]=0, and Entropy[2~1]=00, then
  upwards path(s): A1->C1->S1
  downwards path(s): C1->B1(intra-POD), S1->C2->A2/B2(inter-POD).
When Link between C1 and B1 fail, then A1 can do local convergence
  upwards path(s): A1->C1->S1, A1->D1. //the BIFT-0 on A1 can converge for BFER<B1> locally.
  downwards path(s): D1->B1(intra-POD), S1->C2->A2/B2(inter-POD).
A1 can also do a global optimization by using Entropy[0]=1 and Entropy[2~1]=01 or 02.
C1
D1
A1
B1
S1
S2
S4
S5
C2
D2
A2
B2
S3
S6
stage1
stage2
POD2
POD1
C3
D3
A3
B3
POD3

## Slide 6: Forwarding Procedure
The use of BIER entropy label to select a path between some equal cost paths is a local configuration matter.
This draft defines a method to use part of the 20-bit entropy label in each router, and this needs a data-plane to do some bit operation function.
It is expected to be easier than hashing function.
Page <number>

## Slide 7
Thank You
Thank you !
Notes: 26/7/28
<number>