## Slide 1: CBOR Manifest Serialisation

## Slide 2: Open issues
Should the primary object be an array or a map?
Should the graph described in draft-moran-suit-manifest-02 be replaced with trees?
  How are they overridden?
  How are they represented?
  Are there any use cases that break?
Should one digest be used for the whole manifest, or is there a good reason to support more than one?
Should more sections be severable?
  Should it be possible to encrypt severable sections?
COSE has no algorithm identifiers for digests, so they cannot be reused
  May need another SUIT draft for COSE

## Slide 3: Open Issues (Cont’d)
Should encryption of the manifest be addressed explicitly, or should that be handled one level higher?
Encoding of Processing Step
Encoding of Directive
Encoding of Conditions
Extension encoding
IANA implications for use of enums throughout the manifest

## Slide 4: Primary structure array vs map
Most fields are mandatory
  Version
  digestInfo*
  Nonce
  Sequence
  Preconditions
  Resources
  Targets
Those that aren’t used cost 1 byte (nil or 0-length object)
Out of 12 fields, 7 are mandatory

## Slide 5: Tree-based process description proposal
Things that are installed (assets) get their own section
  Digest
  Size
  Component identifier
Description of how to obtain an asset:
  Component identifier
  List of processing steps
  Resources are a processing step with URIs or a ComponentIdentifier instead of inputs

## Slide 6: Tree-based process description (cont’d)
Asset = [
component: ComponentIdentifier, ; where to store the asset
encoding: bstr / nil, ; the format of the asset
parameters: bstr / nil, ; any specialized arguments for installing the asset
size: uint / nil, ; size of the resource
digest: Digest ; digest of the processed resource
]
ComponentIdentifier = [* bstr ]
Digest = [
digestAlgorithm : DigestIdentifiers / nint, ; Digest identifier
rawDigest : bstr ; Raw bytes of the digest
? digestParameters : bstr ; optional extra arguments to the algorithm
]

## Slide 7: Tree-based process description (cont’d)
AssetInstallationInfo = [
component : ComponentIdentifier
processors : [ * Processor ],
? allowOverride : bool,
? extensions : { * int => bstr }
]
Processor = [
type: &( resource: 1, decrypt: 2, decompress: 3,
undiff: 4, relocate: 5, unrelocate: 6) / nint,
inputs: UriList / ComponentIdentifier / {int => int},
parameters: bstr ; Note: this needs to have more detail instead of bstr
]

## Slide 8: Description of installation process in manifest
Why not leave container information in the payload(s)?
  Reject early if unsupported
  Important for low-bandwidth
Why not enums for aggregate formats?
  Lots of specialized parameters.
  Many possible configurations.
  Registration space of accepted enums becomes large

## Slide 9: Description of installation process in manifest
Example:
  Raw binary payload: no arguments
  Encrypted binary payload:
    key identifier
    algorithm identifier
  Encrypted, compressed binary payload:
    key identifier
    encryption algorithm identifier
    compression algorithm identifier
  Encrypted, compressed, delta payload
    key identifier
    encryption algorithm identifier
    compression algorithm identifier
    precursor digest
    precursor component ID, storage location
    delta algorithm identifier

## Slide 10: Description of installation process in manifest
Each enum would need its own parameter structure
Easy to miss a reasonable combination of supported steps
Describe each step instead
  Each step can have a defined structure
  All steps can be represented in the same way
  How is flow described?
Flow of data between steps is a tree, not a linear sequence
  Delta makes it clear that flow is at least a tree
  A resource shared between two steps makes it clear that flow is a graph
  Graphs make constrained processing hard
  Use multiple trees instead of a graph

## Slide 11: Description of installation process in manifest
For each asset, a tree defines the installation process
To reduce nesting depth in the parser, the tree is encoded as a list, where
  output identifiers are the index of the processor in the processor list
  inputs are a map of indices into the processor list.
Resources are encoded as a processor with no inputs
Assets designate a single input node
Output nodes can be marked as non-overridable
Dependent manifests can override any installation tree not marked as non-overridable

## Slide 12: Examples:
Raw Binary payload
  Installation Information:
    Component Identifier: [ bstr(0) ]
    Resource:
      Parameters: List of URIs
  Asset Information
    Component Identifier: [ bstr(0) ]
    Encoding: raw-binary

## Slide 13: Examples:
Delta payload
  Installation Information:
    Component Identifier: [ bstr(1) ]
    Processors:
      Delta: {1 => 1, 2 => 2}
      Resource: URIs
      Resource: [ bstr(1) ]
  Asset Information
    Component Identifier: [ bstr(1) ]
    Encoding: raw-binary
    inode: bstr(2)

## Slide 14: Current changes

## Slide 15: Highlights of changes
Primary structure is array (not map)
Text is severable
Multiple payloads allowed
Resources (before installation) separated from assets (after installation)
Description of installation process in the manifest
Conditions divided into preconditions and postconditions
Added component identifier (replaces storage identifier)
Timestamp removed, added sequence number

## Slide 16: WIP status
This serialization is still in development
There is ongoing discussion on the mailing list
See Open Issues for more information

## Slide 17: Severable Text
Text is for humans
Text is not used by devices to make decisions
Devices don’t need to receive text
Text is still needed in management systems

## Slide 18: Severable Text (cont’d)
Text lives outside the authenticated container
AuthenticatedManifest = [
authenticatedManifest: COSE_Mac / COSE_Sign,
text: bstr .cbor TextMap
]
TextKeys = &(
uninitialised: 0
manifestDescription: 1
payloadDescription: 2
vendorName: 3
modelName: 4
payloadVersion: 5
) / nint
TextMap = { * TextKeys => tstr }

## Slide 19: Severable Text (cont’d)
Inside the authenticated container, text is authenticated with a digest

## Slide 20: Multiple payloads
Payloads had three components:
  A resource identifier
  Installation instructions (cryptographic info)
  An asset description
Required extension for advanced uses (e.g. Delta)
Aliases, Dependencies, Payloads are now all resource references
Assets are now separate from their resource identifier
Installation instructions are now separate (examples below)

## Slide 21: Resources separated from assets
All resource references are effectively the same
No need to distinguish between alias, dependency, payload
Resources define a local or remote input
  URI
  Digest
Assets define an installed image:
  Size
  Digest
  Location

## Slide 22: Conditions divided into preconditions and postconditions
Some conditions need to be checked before installation
  Identifiers, time, precursors, custom
Some conditions need to be checked after installation
  Content not identified by an asset digest, custom
Two choices:
  Two lists
    makes it easier for devices to know what to do in each step of the process
    typically costs 1 byte
  Duplicate condition identifiers
    typically smaller serialization
    duplication of identifiers may increase integer encoding size
    more registration and maintenance with duplicate identifiers

## Slide 23: Component Identifier
Storage Identifier may not be adequate for all use cases
Devices can be aggregates of one or more processors with two or more different storage systems
Component Identifier allows designating the storage system
Storage systems and hardware components can be nested
Component Identifier needs to be a list to handle this.
Storage Identifier can be merged into this list as the last element.