## Slide 1: A Firmware Update Architecture for Internet of Things Devices
draft-ietf-suit-architecture-01

## Slide 2: Changes between -00* and -01
New terminology for entities
Updated operating modes
Device Firmware Update Examples
Added David Brown as co-author
Many editorial changes
New figures
*: draft-ietf-suit-architecture-00 was discussed at the virtual interim meeting

## Slide 3: Entities

## Slide 4: Author & Device
Author: The author is the entity that creates the firmware image and a manifest.
  There can be multiple authors in a system ( firmware consisting of multiple software components, or device running multiple MCUs)
  There are also other parties that can create a manifest even though they do not create new firmware
Device: Definition updated to point out that the device may need multiple firmware images.

## Slide 5: Communicator
The communicator component of the device interacts with the firmware update server.
It receives firmware images and triggers an update, if needed.
The communicator either polls a firmware update server for the most recent manifest/firmware or manifests/firmware images are pushed to it.
Note that the firmware update process may involve multiple stages since one or multiple manifests may need to be downloaded before the communicator can fetch one or multiple firmware images/software components.

## Slide 6: Status Tracker
The status tracker offers device management functionality that includes keeping track of the firmware update process. (It typically knows what firmware / software is run on the devices.)
This includes fine-grained monitoring of changes at the device, for example, what state of the firmware update cycle the device is currently in.

## Slide 7: Firmware Server
Entity that stores firmware images and manifests. Some deployments may require storage of the firmware images/manifests on more than one entities before they reach the device.

## Slide 8: Device & Network Operator
Device Operator: The actor responsible for the day-to-day operation of a fleet of IoT devices.
Network Operator: The actor responsible for the operation of a network to which IoT devices connect.
Both may also create manifests (for already existing firmware)
In https://www.ietf.org/mail-archive/web/suit/current/msg00587.html Frank suggests to also introduce the OEM Operator:
  OEM Operator: Actor responsible for the day-to-day operation of OEM units in IoT devices connected to an IoT network

## Slide 9: Trust Provisioning Authority (TPA)
The TPA distributes trust anchors and authorization permissions to various entities in the system.
The TPA may also delegate rights to install, update, enhance, or delete trust anchors and authorization permissions to other parties in the system.
This infrastructure overlaps the communication architecture and different deployments may empower certain entities while other deployments may not.

## Slide 10: Operating Modes

## Slide 11: Operating modes
Client-initiated Update: Client-initiated updates take the form of a communicator on a device proactively checking for new firmware imagines provided by firmware servers.
Server-initiated Update: The status tracker determines what devices qualify for a firmware update. Once those devices have been selected the firmware server, in cooperation with the status tracker, distributes updates to those devices.
Hybrid Update: The status tracker pushes notifications of availability of an update to the device, and the communicator then downloads the image from the firmware server when it wants.

## Slide 12: Communication Architecture

## Slide 13: Communication Architecture
Firmware + +----------+ Firmware + +-----------+
Manifest | |-+ Manifest | |-+
+--------->| Firmware | |<---------------| | |
| | Server | | | Author | |
| | | | | | |
| +----------+ | +-----------+ |
| +----------+ +-----------+
|
|
|
-+-- ------
---- | ---- ---- ----
// | \\ // \\
/ | \ / \
/ | \ / \
/ | \ / \
/ | \ / \
| v | | |
| +------------+ |
| |Communicator| | | |
| +--------+---+ | Device | +--------+ |
| | | | Management| | | |
| | Device |<----------------------------->| Status | |
| | | | | | Tracker| |
| +--------+ | || | | |
| | || +--------+ |
| | | |
| | \ /
\ / \ /
\ / \ Device /
\ Network / \ Operator /
\ Operator / \\ //
\\ // ---- ----
---- ---- ------
-----

## Slide 14: Device Firmware Update Examples

## Slide 15: Single CPU SoC
The simplest, and currently most common, architecture consists of a single MCU along with its own peripherals.
These SoCs generally contain some amount of flash memory for code and fixed data, as well as RAM for working storage.
These systems either have a single firmware image, or an immutable bootloader that runs a single image.
A notable characteristic of these SoCs is that the primary code is generally execute in place (XIP).
Combined with the non-relocatable nature of the code, firmware updates need to be done in place.

## Slide 16: Single CPU with Secure - Normal Mode Partitioning
Another configuration consists of a similar architecture to the previous, with a single CPU.
However, this CPU supports a security partitioning scheme that allows memory (in addition to other things) to be divided into secure and normal mode.
There will generally be two images, one for secure mode, and one for normal mode. In this configuration, firmware upgrades will generally be done by the CPU in secure mode, which is able to write to both areas of the flash device.
In addition, there are requirements to be able to update either image independently, as well as to update them together atomically, as specified in the associated manifests.

## Slide 17: Dual CPU, shared memory
This configuration has two or more CPUs in a single SoC that share memory (flash and RAM). Generally, they will be a protection mechanism to prevent one CPU from accessing the other's memory. Upgrades in this case will typically be done by one of the CPUs, and is similar to the single CPU with secure mode.

## Slide 18: Dual CPU, other bus
This configuration has two or more CPUs, each having their own memory.
There will be a communication channel between them, but it will be used as a peripheral, not via shared memory. In this case, each CPU will have to be responsible for its own firmware upgrade.
It is likely that one of the CPUs will be considered a master, and will direct the other CPU to do the upgrade.
This configuration is commonly used to offload specific work to other CPUs.
Firmware dependencies are similar to the other solutions above, sometimes allowing only one image to be upgraded, other times requiring several to be upgraded atomically. Because the updates are happening on multiple CPUs, upgrading the two images atomically is challenging.

## Slide 19: Encryption of Manifest
In the “Human Rights” review in https://www.ietf.org/mail-archive/web/suit/current/msg00580.html Gurshabad Grover recommends to offer encryption of manifests.
Currently, only the encryption of the firmware is supported (as an optional to use feature).

## Slide 20: Next Steps

## Slide 21: Random Thoughts
More editorial clean-up
Incorporate feedback from this meeting
More text about device interactions and bootloader design
Better alignment with information model