## Slide 1: BFR Tethering
IETF 103
Jeffrey Zhang, Juniper
Nils Warnke, DT
Ice Wijnands, Cisco

## Slide 2: Brownfield Deployment
Get around them and/or tunnel through them
  X in the below diagram does not support BIER
How to handle BIER incapable routers?
Source: Arial 12pt.
BFR1
X
BFR2
BFR3
BFR4
BFR5
BFR6
5
1
1
5
BFR1
X
BFR2
BFR3
BFR4
BFR5
BFR6
5
1
1
5

## Slide 3: Tunnel Through Incapable Routers
Section 6.9 of BIER Architecture spec
  At the end of SPF, examine each immediate child node on the SPF tree
  If it’s not BIER capable, replace it with its immediate children
  If a new child (that just replaced its parent) itself is incapable, replace it with its immediate children
  The process is repeated until all immediate children are BIER capable
  If a child is not directly connected, then a tunnel must be used to send BIER traffic to the child
Any tunnel to the child can be used
  Static or dynamic (e.g. LDP/SR/GRE)
  No need to announce the tunnels
And follow unicast topology

## Slide 4: Tunneling Alone May Not Be Good Enough
If the number of BFRs that X connects to is large, then BFR1 needs to tunnel many copies through that BFR1-X link
  Not good if the BFR1-X connection is long distance and/or BW constrained
A solution is to tether a BFRx to X with a fat local pipe
  BFR1 tunnels a single copy to BFRx, who in turn tunnels to other BFRs
BFR1
X
BFR3
BFR4
BFR5
BFR6
BFIR1
BFER3
BFER4
BFER5
BFER6
BFRx

## Slide 5: Making Tethering Easier
Tunnels would need to be announced in IGP to make tethering work
  Otherwise the Section 6.9 method would never put BRFx onto its SPF tree
  They would need to be announced a BIER specific MT or use FlexAlgo
    Don’t want to send unicast traffic through BFRx
Unless with the following trick:
  X advertises that it supports BIER so it will receive BIER packets natively
    The BIER packets come with a BIER label that normally directs to BIER forwarding
  X label switches (based on the BIER label) the BIER packets to BFRx
  BFRx uses the Section 6.9 method to tunnel incoming BIER packets from X to other BFRs through X
    BFRx knows that X does not really support BIER
      Through provisioning or additional signaling from X
    X could also have other connections as long as the X-BFRx metric is 1

## Slide 6: Additional Signaling
X signals “BFRx is my helper”
  BFRx will know X is actually not capable
  Other BFRs may use Section 6.9 method to tunnel over X
    Instead of relying on X to use BIER labels to switch to BIER packets to its helper
Alternatively, BFRx signals “I am X’s helper”

## Slide 7: Summary
Tethering a BFR helper reduces the copies of tunneled packets over
Two options to make tethering easier
  X pretends it supports BIER but label switches incoming BIER packets to its helper BFRx
    Requires software upgrade on X and its helper only
    Only works for MPLS
  BFRx advertises it is X’s helper and others will tunnel over X
    Upgrade needed on BFRs but not on X
Next Steps
  Seek comments
  Request adoption after polishing