## Slide 1: IETF 103 Bangkok
IJsbrand Wijnands Cisco ice@cisco.com
Xiaohu Xu Huawei xuxiaohu@huawei.com
Hooman Bidgoli Nokia hooman.bidgoli@nokia.com
An Optional Encoding of the BIFT-id Field in the non-MPLS BIER Encapsulation
draft-ietf-bier-non-mpls-bift-encoding-01
1

## Slide 2: Status/History
Informational document.
Draft has been accepted by WG.
New encoding added
  (based on discussion on the mailing list with Eric).

## Slide 3: 1. The Non-MPLS Static BSL-SD-SI BIFT Encoding
The BIFT-id is 20 bits.
We overload this BIFT-id field and carve out space for:
  BSL (4 bits), SD (8 bits) and SI (8 bits).
For the data-pane, this remains a 20 bit value!!!
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| BSL | SD | SI | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|-------- 20 bit BIFT-id Field ---------|

## Slide 4: 2. The Non-MPLS Static IBU-SI BIFT Encoding
The BIFT-id is 20 bits.
We overload this BIFT-id field and carve out space for:
  IBU (12 bits) and SI (8 bits).
For the data-pane, this remains a 20 bit value!!!
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IBU | SI | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|-------- 20 bit BIFT-id Field ---------|

## Slide 5: 2. The Non-MPLS Static IBU-SI BIFT Encoding
Encoding 1 does not allow adding new dimensions, like (draft-zzhang-bier-multicast-as-a-service-00)
The IBU is similar to the (global) MPLS Label.
But this encoding already has space carved out for SI.
With MPLS we allocated a range of labels (typically 256), but this comes down to the same thing.
Any combination of {IBU, SI} can be associated with a specific SD, BSL and/or RD.
It is more obvious now that the data-plane MUST never parse the 20bit field.

## Slide 6
Questions?