## Slide 1: draft-venaas-bier-pfm-sd-00 PIM Flooding Mechanism and Source Discovery for BIER
Stig Venaas, stig@cisco.com
IJsbrand Wijnands, ice@cisco.com
Mankamana Mishra, mankamis@cisco.com
Mahesh Sivakumar, sivakumar.mahesh@gmail.com

## Slide 2: RFC 8364 PFM-SD
SRC
Rcv
Initial data packet detected and dropped by first hop router
FHR sends triggered PFP-SA message containing (S,G) for the source (but no data)
PFP-SA forwarded hop by hop throughout the domain
All routers know about the (S,G)
LHR can join towards source
No RPs, no shared trees.
PFM-SD message
Data
FHR
LHR

## Slide 3: BIER PFM-SD overview
FHR send message with its originator address and a list of its active sources and their holdtime.
BIER ingress routers add their BIER prefix, SD and BFR-ID, and metrics for the sources. Replicates to all BIER routers in SD
BIER egress caches the info, removes BIER info and forwards just the pim info.
SRC
FHR
Rcv
PIM
BIER
PIM
Origin
(S,G,H)
Origin
BIER prefix,SD,ID
(S,G,H, metric)
Origin
(S,G,H)

## Slide 4: BIER PFM-SD PIM joins
When BFER receives (S,G) join, it looks in cache and sends join over BIER to BFIR with smallest metric; here BFIR1
SRC
PIM (S,G) join
BFER Cache
Origin, BFIR1 (S,G,H, metric1)
Origin BFIR2
(S,G,H, metric2)
BFIR2
BFER
BFIR1
PIM (S,G) join
PIM (S,G) join over BIER
Rcv

## Slide 5: PFM BIER Ingress TLV
New TLV added by a BIER ingress router (BFIR)
Contains info needed to signal BFIR. E.g., pim join over BIER
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0| Type = TBD | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sub-domain-id | Reserved | BFR-id |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| BFR-prefix (4 or 16 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 6: PFM Group, Source, Holdtime, Metric TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0| Type = TBD | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Group Address (Encoded-Group format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Src Count | Src Holdtime |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Src Address 1 (Encoded-Unicast format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Metric Preference 1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Metric 1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Src Address 2 (Encoded-Unicast format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Metric Preference 2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Metric 2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . |
| . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Src Address m (Encoded-Unicast format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Metric Preference m |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Metric m |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+