## Slide 1: BIER Prefix Redistribute draft-zwzw-bier-prefix-redistribute-01
BIER WG
IETF103# Bangkok
Sandy Zhang
Bo Wu
Jeffrey Zhang
IJsbrand Wijnands

## Slide 2
Problem Statement
    Different routing protocols/areas run in different regions.
    Hybrid Network
    There are tens of routers in some regions. There is only one hop forwarding in some other regions.
    Multicast services are provided in this hybrid network by using protocol independent feature of PIM currently.
    If we deploy BIER in this network:
    BIER is deployed in each IGP region.
    Border router needs to maintain overlay state.
    Border router must convert BIER encapsulation.
    Multiple BIER encap/decap functions lead to inefficient forwarding.
R1
R2
R3
R4
ISIS/OSPF
OSPF
Rm
Rn
Bier domain 1
Bier domain 2
……
OSPF
Rx
Ry
Bier domain 3
……

## Slide 3
In order to improve forwarding efficiency:
Merge several regions into one BIER domain.
Remove overlay state in border router.
Decrease the times of BIER encap/ decap.
Problem Statement
BIER domain
But how to build BIER forwarding across multiple routing regions?
R1
R2
R3
R4
ISIS/OSPF
OSPF
Rm
Rn
……
OSPF
Rx
Ry
……

## Slide 4
BIER info advertisement associates with prefix redistribution in border router.
BIER node information spreads in the whole BIER domain across multiple regions.
The advertisement is aligned with the existed IGP/BGP definition.
MPLS encapsulation has local significance. We need not, but MAY, advertise it to next routing area.
Every node in the domain can build BIER forwarding plane.
Solution

## Slide 5
Because some prefixes in one region may be hidden when border router does prefix distribution function. Such as summarized / aggregated route, default route.
A new extension is added for summarized/ aggregated prefix advertisement.
Solution
The BFR-ids associated with the summarized prefix can be advertised individually in the BIER range sub-TLV.
BIER proxy range sub-TLV can be used to improve advertisement efficiency if the BFR-ids are continuous.
Multiple BIER proxy range sub-TLVs may be used if the BFR-ids covered by the prefix are allocated from different ranges. Necessary policy should be provided to guide the range generation of BFR-ids.

## Slide 6
Any comment is welcomed 
WG adoption?
Thanks!