## Slide 1: BIER-TE-ARCH IETF103 Bangkok
draft-ietf-bier-te-arch-01
Toerless Eckert (tte@cs.fau.de)
Gregory Cauchie (GCAUCHIE@bouyguestelecom.fr)
Wolfgang Braun (wolfgang.braun@uni-tuebingen.de)
Michael Menth (menth@uni-tuebingen.de)

## Slide 2: Since IETF101
draft-ietf-bier-te-arch-00.txt – 01.txt
Reworked details about forwarding plane, comparison thereof with BIER
  Goal is make it clear what if any differences there are to BIER to encourage HW forwarding support for BIER-TE.
    Differences hopefully so small that all BIER capable HW can also do BIER-TE
  Document still intends to target experimental because BIER-TE requires control plane
    Explicit, non-standardized establishment of TE BIFT entries fine for experiments but likely insufficient for standard deployments
Emphasized that RFC8926 can be used unchanged (from feedback in IEF101)
  Just requires configuration, e.g.: per subdomain whether BIFT is operating BIER or BIER-TE
  Additional drafts for encap (not currently refreshed) should be considered as optional enhancements to be vetted independently (not required by BIER-TE)
    Indicate in header (bit) whether BIER/BIER-TE is expected (diagnostics)
    Add packet sequence number field for DetNet and similar. Independent of BIER/BIER-TE

## Slide 3: 3.6 Requirements
New section with MUST/SHOULD against forwarding plane to comply
  Similarily to BIER architecture where ECMP is optional, mandate with MUST the most core BIER-TE forwarding functions, SHOULD/MAY the others
MUST
  Configure subdomain for BIER-TE forwarding
  Bits indicating no or one adjacency: forward connected, forward routed or local_decap
    Forward_routed could be degraded, but for scalability we think its very important
    Aka: adjacency is encap into another label to send to remote BIER-TE router
SHOULD
  DNR (Do Not Reset) flag on adjacencies. To support L3 rings with just one bit per direction.
MAY
  ECMP adjacencies.
    Only MAY (less important than in BIER), because feeling is that with TE you want to manage amount of traffic on paths more explicit, and doing that with ECMP is more difficult than explicit, non-ECMP paths.
  More than one adjacency on a bit. Flood from hub to multiple spoke adjacencies. Good for broadcast TV style traffic, also sounds like on the bottom of the priority list.

## Slide 4: 3.6 Pseudocode
Same pseudocode than BIER
  Just commented out [1]
Doing [1] and [2] together in BIER-TE does not work
You want to reset the bit B you are forwarding on in [2], so
  F-BM = ~ (2 << B)
But then [1] would reset all the bits.
Simple solution: Just do not do [1] when BIFT uses BIER-TE mode
BIER pseudocode adopted to BIER-TE:
void ForwardBitMaskPacket_withTE (Packet)
{
SI=GetPacketSI(Packet);
Offset=SI*BitStringLength;
for (Index = GetFirstBitPosition(Packet->BitString); Index ;
Index = GetNextBitPosition(Packet->BitString, Index)) {
F-BM = BIFT[Index+Offset]->F-BM;
if (!F-BM) continue;
BFR-NBR = BIFT[Index+Offset]->BFR-NBR;
PacketCopy = Copy(Packet);
PacketCopy->BitString &= F-BM; [2]
PacketSend(PacketCopy, BFR-NBR);
// The following must not be done for BIER-TE:
// Packet->BitString &= ~F-BM; [1]
}
}

## Slide 5: 3.6 Pseudocode
Simplified original pseudocode from -00 version
Removes use of FBM
  Implementations do not need to provide FBM for BIER-TE, that’s just a choice if commin HW for BIER/BIER-TE makes that beneficial
  Only need to reset bit of adjacency itself (unless DNR set) [1]
Also shows handling of the different adjacency types
  No equivalent level of detail in BIER arch RFC pseudocode, but hopefully useful.
void ForwardBitMaskPacket_withTE (Packet) {
SI=GetPacketSI(Packet);
Offset=SI*BitStringLength;
AdjacentBitstring = Packet->BitString &= ~AdjacentBits[SI];
Packet->BitString &= AdjacentBits[SI];
for (Index = GetFirstBitPosition(AdjacentBits); Index ;
Index = GetNextBitPosition(AdjacentBits, Index)) {
foreach adjacency BIFT[Index+Offset] {
if(adjacency == ECMP(ListOfAdjacencies, seed) ) {
I = ECMP_hash(sizeof(ListOfAdjacencies),
Packet->Entropy, seed);
adjacency = ListOfAdjacencies[I]; }
PacketCopy = Copy(Packet);
switch(adjacency) {
case forward_connected(interface,neighbor,DNR):
if(DNR)
PacketCopy->BitString |= 2<<(Index-1); [1]
SendToL2Unicast(PacketCopy,interface,neighbor);
case forward_routed([VRF],neighbor):
SendToL3(PacketCopy,[VRF,]l3-neighbor);
case local_decap([VRF],neighbor):
DecapBierHeader(PacketCopy);
PassTo(PacketCopy,[VRF,]Packet->NextProto); }
} } }

## Slide 6: What else ?
Added node how BIER/BIER-TE might best be understood by someone coming from SR
  BIER are 1 bit equivalent of destination/Node SIDs
  BIER-TE could be seen as doing for multicast what an SR SID-stack would do to do explicit routing. Every hop SID is just a bit.
Purely opportunistic text
  Hope it is helpfull for people coming from SR looking at BIER
  If not, will just remove (1 paragraph).

## Slide 7: THE END
Credit rolls…
Oh wait, one more thing...
And now for something completely different

## Slide 8: While trying to figure out BIFT for BIER-TE
Independent of BIER-TE, but BIER thought
Do BIER BIFT implementations have to accept arbitrary F-BM values ?
Not currently ? There is no API from IETF (YANG,..) that allows to program BIFT/F-BM directly ?!
BIFT/F-BM only programmed internally from BIRT ?!
Arbitrary F-BM (not derived from BIRT) might not be possible/desirable to support in optimized BIFT
Could easily create “funny” FBM that stretch platforms
  E.g.: BIRT derived BIFT can be parallelized
  Egres linecards would only need to look/examine bits with NBRs on the interface
  Funny F-BMs would not allow to do this. ”Last” linecard may need to still evaluate impact of all preceding bits.
Define in any BIER rev constraints on required F-BM to ensure platform optimizations can be done without running into future surprises ?
  When BIFT ae exposed directly to programming
BFER1
BFER2
BFER3
BFR1
GEEKOMETER
buzzwords
inch2
linecard1
linecard2
BFR2
BFR3
BFER1,2,3 are bit 1,2,3.
On BFR1:
BIFT[1]->F-BM = 011 BIFT[1]->BFR-NBR = 2
BIFT[2]->F-BM = 110 BIFT[2]->BFR-NBR = 3
BIFT[3]->F-BM = 100 BIFT[3]->BFR-NBR = 3