## Slide 1: Multicast/BIER As A Service
IETF 103, Bangkok
Zhaohui (Jeffrey) Zhang, Juniper
Eric Rosen, Juniper
Liang Geng, China Mobile

## Slide 2: Current Multicast Use Cases
Enterprise Applications
  FSI Financial Data Distribution
Service Provider
  Live TV/video distribution inside a provider itself
  Customer Multicast/BUM for VPN/EVPN
  Internet Multicast is minimum
    Mbone is mostly in Internet2, w/o much real usage

## Slide 3: Multicast As A Service?
Only in the form of MVPN or EVPN BUM
Other multicast transport by SPs virtually non-existent
  E.g., can an SP provide multicast transport for a non-VPN 3rd party?
    E.g. for a content provider who does not have its own all-reach network?
  Lack of confidence/interest on service provider side
    Complexity and scalability concerns – signaling and per-flow state
    Profitability concerns
      Lots of multicast flows are low volume
      For high volume (e.g. video) traffic, how to bill?
  Lack of interest on customer side
    Lack of provider support
    Content providers resorted to p2p/p2sp (peer to peer or peer to server/peer)
  Chicken & Egg problem

## Slide 4: BIER Enables MaaS
BIER removes per-flow state
  Significantly simplifies multicast control plane
  Significantly improves scalabilities
BIER can help break the chicken & egg vicious circle
  It can encourage service providers to provide multicast transport services
    In addition to using BIER for its own MVPN/EVPN services
  It can encourage content providers to use multicast for delivery
Potential use cases for MaaS
  CDN (large scale high definition live broadcast or content pushing)
  Any large scale high rate data distribution

## Slide 5: Current Common BIER Use Cases
Current use cases have entire BIER sub-domain (BFERs and BFRs) under the same operator
  BIER as provider/underlay tunnels for MVPN/EVPN-BUM
    End-to-end multicast flow in overlay
  BIER sub-domain as part of end-to-end multicast tree
    E.g. PIM signaling as “BIER Multicast Flow Overlay”
    Similar to “mLDP Inband Signaling”
    An end-to-end multicast tree could have multiple unrelated BIER sub-domains
Most likely IGP is the BIER signaling protocol

## Slide 6: BIER Enabled MaaS
BFERs/BFRs may be under separate operators
  BFERs owned by a customer
  Service providers don’t have to worry about per-flow state at all
    BFRs do need to know how to route to customer BFERs
An operator may provide BIER based transport for many customers
  Independently for each customer
Mainly BGP signaling
  OTT tunneling very common
  IGP signaling may be used in an area/AS where most devices support BIER

## Slide 7: A Simple Example
Single Operator (e.g. a content provider’s own all-reach network)
BFERs all over the places
  Starting w/o BFRs
    Essentially Ingress Replication
  Gradually add BFRs at strategic points
    E.g. Turn on BIER on ASBR23 & ASBR24
BGP based BIER signaling
  draft-ietf-bier-idr-extensions
Multi-AS but (initially) no segmentation
  Either have fewer than 256 BFERs or multiple sets are used
BFER11
BFER42
BFER52
BFER51
BFER32
BFER31
BFER13
BFER12
ASBR24
ASBR3
ASBR21
ASBR1
BFER41
ASBR23
ASBR5
ASBR4
AS100
AS400
AS200
AS300
AS500
BFER22
BFER21

## Slide 8: A Couple of Details
In the previous slide, BFER11’s shortest path to BFER21 is through ASBR21, which does not support BIER, while BFER23 does
  For AS100 to send BIER traffic to ASBR23:
    Only ASBR23 should re-advertise BFER21’s BIER info
      Incongruent unicast/multicast path
Preventing tunneling to BFERs directly
  Tunnel Encap Attribute: attached by an BFER, updated by each BFR that changes BGP Next Hop, and used as the BIER neighbor to replicate traffic to
    BFER42 uses its own BIER prefix as tunnel destination address
    ASBR24 changes it to its own BIER prefix; ASBR23 changes again
    For BFER11 to reach BFER42, it tunnels to ASBR23, who then tunnels to ASBR24, who then tunnels to BFER42

## Slide 9: Turn on BIER inside an AS/Area
In the previous slide, BIER traffic are tunneled between a few strategically placed BFRs
  BFER11 tunnels (Ingress Replicates) to BFER12/BFER13/ASBR1
If enough routers in AS100 supports BIER, AS100 can run BIER internally
  The entire network (across ASes) is still a single sub-domain
  With mixed IGP and BGP signaling for BIER
    https://tools.ietf.org/html/draft-zwzw-bier-prefix-redistribute used to redistribute BIER info between IGP and BGP
      BFER11/BFER12/BFER13’s BIER Prefixes and BFR-IDs are re-advertised into BGP by ASBR1
      Other BFERs’ BIER prefixes and BFR-IDs are re-advertised into IGP by ASBR1
  This does require redistribute BFER prefixes into IGP

## Slide 10: Segmentation
If the number of BFERs is very large, segmentation can be used
  E.g. each AS/area is an independent BIER sub-domain
  A segmentation point maintains xPMSI (or PIM) state, decapsulate BIER header in the upstream sub-domain and forward to a downstream sub-domain (label switch or PIM based forwarding) with a new BIER header
  Use Route Targets or policy to restrict BIER info to each sub-domain
This is reasonable for this single operator case
If a deployment started with fewer PEs w/o segmentation, segmentation can be introduced incrementally
  Add a BFR as or convert an existing BFR to a segmentation point
  Make sure it does not re-advertise BIER information between two sub-domains
  Make sure BFRs/BFERs in a sub-domain only exchange BIER information among themselves (including the segmentation points)

## Slide 11: Multi-Operator Case
What if AS200 in the earlier simpler example does not belong to the content provider that owns the BFERs?
With BGP based signaling, it still works
AS200 is now providing MaaS
  BIER as a Service (BaaS) to be more accurate

## Slide 12: BIER as a Service
Provided by AS200
BIER level; no BFER, hence no customer (s,g) state
  What if segmentation is needed?
    xPMSI state maintained on segmentation points
      Inclusive or some (s/*,g) Selective PMSI
    Optionally, a customer equipment (physical or virtual) can be tethered as segmentation point
What if different customers have conflicts in subdomain-id and BFR-id?
  Use per-customer RD with BIER Prefix
    BIFT is now per <RD, subdomain-id, bsl, set>; or a sub-domain is now per <RD, subdomain-id>
    What if we need to redistribute BIER info between BGP and IGP?
      In IGP signaling, use a BIER Domain sub-TLV to encode the RD and BIER Info
A BFR needs to scale on number of BIFTs
  E.g., 256 BIFTs, each with 256 entries (64k routes in total)

## Slide 13: MaaS Control & Billing
A provider can have policies to control:
  Whether/how it re-advertises certain BIER prefixes, e.g. to certain peers only
  Whether it advertises its own BIER prefixes (with a certain RD)
    i.e. whether it becomes a BFR for a particular customer
      This controls the number of BIFTs that it instantiates
A provider can count traffic and bill accordingly:
  At an entry point: incoming BIER packets for each BIER label that it advertises
  At an exit point: outgoing packets for each BIER label that it imposes

## Slide 14: Summary
Scalable MaaS enabled by BIER
“BIER Transport Service” to be more accurate
  Leave BFER (and customer specific state) to customers
  Existing MVPN/EVPN with BIER can provide traditional multicast service
Incrementally expandable
With policy control and billing