## Slide 1: BFD for BIER
IETF BIER, November 2018, Bangkok
Fangwei Hu (ZTE)
Quan Xiong(ZTE)
Greg Mirsky(ZTE)
Chang Liu(Cina Unicom)
draft-hu-bier-bfd-02.txt

## Slide 2: Changes from version 00 &01
Removes the definition of BIER OAM packet format, and refers it from <draft-ietf-bier-ping>
  for the BIER OAM packet format has been defined in <draft-ietf-bier-ping>.
Removes the one-hop bootstrap part ,and keeps multi-hop bootstrap only:
  The multi-hop bootstrap is more suitable: Because BIER is overlay technology, and it is more likely that BFRs are connected by tunnels.
Corrects some references: because some draft had been published.
Riches the security and Acknowledgments parts.

## Slide 3: BIER BFD
BIER BFD is based on draft-ietf-bfd-multipoint
  Uses Demand mode( defined in RFC 5880) – no three-way handshake
BFERs use source address and My discriminator to demultiplex BFD sessions
  Source address:
    BFIR-id and BIER MPLS Label(MPLS network)
    BFIR-id and BIFT-id(Non-MPLS network)

## Slide 4: BIER BFD Encapsulation
BIER BFD encapsulation uses the BIER OAM packet format defined in [I-D.ietf-bier-ping].
Msg Type field MUST be set to BIER BFD (TBD by IANA)
BFD Control packet[RFC5880] immediately follows the BIER OAM header

## Slide 5: Bootstrapping BIER BFD session
Multi-hop Bootstrapping
  Use BIER OAM ping [I-D.ietf-bier-ping]

## Slide 6: Next Step
We will add active tail solution in the next version
  Base on the comments received
More comments?

## Slide 7
Thank you