## Slide 1
LSR extensions for advertising BIER-ETHER encapsulation capability & parameters
draft-dhanaraj-bier-lsr-ethernet-extensions-00
IETF104 2019-03-25 Prague
Senthil Dhanaraj
IJsbrand Wijnands
Peter Psenak
Zhaohui(Jeffrey) Zhang
Jingrong Xie
Gang Yan
Notes: 26/7/30
<number>

## Slide 2: Draft purpose
BIER ETHERNET (BIER-ETH) is one of the encapsulation type to deploy BIER in Non-MPLS networks.
Like BIER-MPLS, processing and forwarding of BIER-ETH packets requires new software / hardware.
BFRs supporting BIER-ETH encapsulation must advertise this capability (along with the other required parameters) to the other BFRs in BIER domain (to aid building BIER Routing table).
This draft defines the required extensions to ISIS and OSPF protocols to advertise the BIER-ETH encapsulation capability and parameters.
Page <number>
Eth Header
(EthTYpe=0xAB37)
BIER Header
Data

## Slide 3
Add new sub-sub-TLV for BIER-ETH
ISIS/OSPF TLV
Bier sub-domain Sub TLV
MPLS Encap sub-sub-TLV
BIER-Eth Encap sub-sub-TLV
Existing TLV
New TLV
Add a new BIER-ETH sub-sub-TLV under BIER sub-domain sub-TLV to advertise the BIER-ETH capability and other associated parameters of the encapsulation.
A BIER sub-domain MAY support more than one BIER encapsulation type.
  The different encapsulation types supported in a sub-domain shares the same BFR-id.
  The selection of encapsulation type to be used by a BFIR or BFR for a sub-domain could be a matter of local policy and is outside the scope of this work.
How to advertise ?

## Slide 4
bit-string-length supported (same as BS Len in BIER-MPLS)
  Number of SETS supported for the bit-string-length (same as Max SI in BIER-MPLS)
  BIFT-id for each SET (BIFT-id, not MPLS Base Label)
What to advertise ?
Refer BIER-MPLS Encap sub-sub-TLV
What to advertise in BIER-ETH Encap sub-sub-TLV ?

## Slide 5
More about BIFT-Id
  [RFC8296] specifies that the BIFT-id in Non-MPLS networks is a "domain-wide-unique-value“ and is not expected to change at each hops as the BFR forwards the BIER packet. Then why advertise BIFT-id ?
  [I-D.ietf-bier-non-mpls-bift-encoding] describes two possible methods for assigning and encoding the BIFT-id in Non-MPLS BIER Header.
  Though BIFT-id is expected to be unique per BIER Sub-domain across all the BFRs, considering that there
  are multiple possible options to generate/assign BIFT-id, it is advisable to advertise the BIFT-id to detect
  any bad provisioning and thereby avoiding traffic black holing.
  Contrary to [RFC8296], BIER architecture [RFC8279] does NOT require domain-wide-unique BIFT-ids to be used (even for non-MPLS encapsulation) and is possible that a locally assigned non-unique value can be used as BIFT-id.
  This can be seen as other reason why we need to advertise BIFT-id along with the previous reasoning.

## Slide 6
More about BIFT-Id
  In BIER MPLS world, for an [SD, BSL] pair, contiguous labels are allocated and we advertise only the base label and the label-range-size (a.k.a Max SI).
  This way, signaling of individual labels per SET is avoided and signaling is simplified.
  Should BIFT-id in Non-MPLS networks, be contiguous, similar to MPLS Labels ? Not necessarily !
  But to make the IGP signaling simpler, we suggest to follow similar approach as BIER-MPLS.
      Allocate contiguous range of BIFT-Ids !
      Advertise only the Base BIFT-id and the BIFT-id range (a.k.a Max SI)

## Slide 7
It is advertised within the BIER Info sub-TLV defined in [RFC8401] which in-turn is carried within the TLVs 235, 237 [RFC5120] or TLVs 135 [RFC5305], or TLV 236 [RFC5308].
Type: 2 (TBD – IANA)
Length: 4
Max SI: 1 octet. Maximum Set Identifier (Section 1 of [RFC8279]) used in the encapsulation for this BIER subdomain for this BitString length. The first BIFT-id is for SI=0, the second BIFT-id is for SI=1, etc. If the BIFT-id associated with the Maximum Set Identifier exceeds the 20-bit range, the sub-sub-TLV MUST be ignored.
Local BitString Length (BS Len): 4 bits. Encoded bitstring length as per [RFC8296].
BIFT-id: 20 bits. First BIFT-id of the BIFT-id range. The usage of BIFT-id value for non-MPLS networks is as defined in [RFC8296].
ISIS – Add new BIER-ETH encap sub-sub-TLV

## Slide 8
It is advertised within the BIER sub-TLV defined in [RFC8444] which in-turn is carried within the OSPFv2 Extended Prefix TLV defined in [RFC7684].
Type: 11 (TBD – IANA)
Length: 8
Max SI: 1 octet. Maximum Set Identifier (Section 1 of [RFC8279]) used in the encapsulation for this BIER subdomain for this BitString length. The first BIFT-id is for SI=0, the second BIFT-id is for SI=1, etc. If the BIFT-id associated with the Maximum Set Identifier exceeds the 20-bit range, the sub-sub-TLV MUST be ignored.
BIFT-id: 20 bits. First BIFT-id of the BIFT-id range. The usage of BIFT-id value for non-MPLS networks is as defined in [RFC8296].
Local BitString Length (BS Len): 4 bits. Encoded bitstring length as per [RFC8296].
OSPF – Add new BIER-ETH encap sub-TLV

## Slide 9: Request to the WG
Comments / Inputs
Adoption Request

## Slide 10: Appendix (BIFT-id range)
As an example, suppose a particular BIER domain contains a SD (SD 0), supports two BSLs (256 and 512), and contains 512 BFRs. A BFR that is provisioned for above SD, and that supports both BSLs, would have to advertise the following set of BIFT-id's: BIFT-id 1: corresponding to SD 0, BSL 256, SI 0. BIFT-id 2: corresponding to SD 0, BSL 256, SI 1. BIFT-id 3: corresponding to SD 0, BSL 256, SI 2. BIFT-id 4: corresponding to SD 0, BSL 256, SI 3. BIFT-id 5: corresponding to SD 0, BSL 512, SI 0. BIFT-id 6: corresponding to SD 0, BSL 512, SI 1. In such case, a BFR MUST assign a contiguous range of BIFT-ids as, BIFT-id range [1 to 4] correspond to <SD 0, BSL 256>. BIFT-id range [5 to 6] correspond to <SD 0, BSL 512>.
The first BIFT-id in the range correspond to SI=0, the second correspond to SI=1, and so on.