## Slide 1
BIER P2MP mLDP Signaling
H.Bidgoli (Nokia)
J.Kotalwar (Nokia)
Andrew Dolganow (Nokia)
July 2018
Notes: NOKIA

## Slide 2
The background
Extending draft-bier-ietf-pim-signaling to mLDP
Problem:
  introduce BIER to a desired segment of the network with “minimal or no disruption and operational impact” to the mLDP domains.
  Simplify operation by eliminating legacy multicast control plane protocols in BIER domain. With SR and BIER no more MPLS control plane.
  Gradual upgrade to BIER starting with desired segment and eventually upgrading the entire network to BIER aware hardware.
Identifying and stitching a P2MP LSP through a BIER core.
  This draft is not proposing LDP neighboring through a BIER core
  Much like PIM Signaling through BIER
Notes: NOKIA

## Slide 3
Signaling BGP
P1
100.0.0.21
PE3
100.0.0.14
PE1
100.0.0.8
P2
100.0.0.2
Source C(S1,G1)
Host IPv4
C(S1,G1)
PE4
P4
100.0.0.4
P3
P5
mLDP Fec (root, opaque<lspID1>,label1)
mLDP Fec (root, opaque<lspID2>, label2)
After receiving the FEC assign a local label
And signal the label mapping toward PE1
mLDP Fec (root, opaque<lspID1>, label3)
mLDP Fec (root, opaque<lspID2>, label4)
hb
BIER Domain
LDP Domain
LDP Domain
Egress BIER Boundary Router(EBBR)
Signaling Extended
Ingress BIER Boundary Router(BBR)
IGP-111A
IGP
IGP
On EBBR assign a BIER Tree Label (BTL) from <EBBR, SD> Pool for this FEC to uniquely present the P2MP LSP in BIER domain
1
2
signal mLDP FEC and to EBBR
mLDP Fec (root, opaque<lspID1>)
mLDP Fec (root, opaque<lspID2>)
3
4
5
4
EBBR will signal BTL to IBBRs (via BGP) tunnel attribute and correct NLRI (TBD) the <EBBR,SD>(BTL)> mapping
BGP
4
Notes: NOKIA

## Slide 4
Control Plane
Control plane
  LDP signaling is terminated at BIER Boundary Routers (BBRs)
  BBRs will maintain LDP adjacency toward the mLDP domain
  On a arriving label mapping/withdraw from LDP domain, if IBBR determines the Root of the FEC resides on the other side of BIER Domain, it will signal the FEC and the FEC action to the EBBR, as an example <FEC, label mapping> or <FEC, label withdraw>
  The EBBR can be found with using the outer root of the FEC and the procedure explained in ietf-draft-bier-pim-signaling
  The EBBR will receive the bier signaling packet including the <FEC, label action>
    The EBBR will assign a BIER Domain TREE Label (BTL) to identify the P2MP LSP uniquely in the BIER domain, as an example if there is no BTL assigned to this label yet.
    For scaling considerations this BTL can be assigned per <EBBR PrefixID,SD> label pool.
    The EBBR will have a MP-BGP adjacency to IBBR(s) and will signal the <<EBBR,SD> (BTL)> with correct (New) PTA and NLRI
  The Egress BBR keeps track of all IBBRs that are interested in this specific FEC. It creates a tree with OIF all the IBBRs signaling this FEC
  The Egress BBR will also generate a new mLDP label for the FEC and forward the label mapping/withdraw toward the Root in LDP domain.
Notes: NOKIA

## Slide 5
MPLS table
P1
100.0.0.21
PE3
100.0.0.14
PE1
100.0.0.8
P2
100.0.0.2
Source C(S1,G1)
Host IPv4
C(S1,G1)
PE4
P4
100.0.0.4
P3
P5
hb
BIER Domain
LDP Domain
LDP Domain
Egress BIER Boundary Router(EBBR)
Ingress BIER Boundary Router(BBR)
IGP-111A
IGP
IGP
SDN
6
ILM Table (EBBR)
Label3(stitch) BTL-1 NHLFE (all IBBRs interested into this FEC)
Label4(stitch) BTL-2 NHLFE (all IBBRs interested into this FEC)
7
ILM Table (IBBR)
<EBBR, SD> (BTL-1) (stitch) label 1 NHLFE (all OIFs)
<EBBR, SD> (BTL-2) (stitch) label 2 NHLFE (all OIFs)
Notes: NOKIA

## Slide 6
The solution mLDP signaling over a BIER Core
On EBBR there will be a ILM entry of
  Incoming label stitch to BTL with out going interface all the IBBRs interested in this FEC
On IBBR there will be a ILM entry of
  Incoming BTL from a specific EBBR label pool stitch to outgoing label with out going interfaces all mLDP OIFs
Notes: NOKIA

## Slide 7
FIGURE 1
P1
100.0.0.21
PE3
100.0.0.14
PE1
100.0.0.8
P2
100.0.0.2
Source C(S1,G1)
Host IPv4
C(S1,G1)
PE4
P4
100.0.0.4
P3
P5
hb
BIER Domain
LDP Domain
LDP Domain
Datapath
BFIR
BFER
MPLS packet (label3)
BIER DATAPATH
IPoFECoBIER
MPLS packet (label1)
IGP-111S
OR
IGP-111A
IGP
IGP
Stitch Label3
to BDT1
PUSH BIER for all IBBR(s)
Check BIER header
Find EBBR PrifixID
Stitch EBBRs BDT1
to label1
ILM Table (EBBR)
Label3(stitch) BTL-1 NHLFE (all IBBRs interested into this FEC)
Label4(stitch) BTL-2 NHLFE (all IBBRs interested into this FEC)
ILM Table (IBBR)
EBBR-POOL (BTL-1) (stitch) label 1 NHLFE (all OIFs)
EBBR-POOL (BTL-2) (stitch) label 2 NHLFE (all OIFs)
Notes: NOKIA

## Slide 8
Data Plane
Data plane
  Single BIER domain label to represent a P2MP LSP in BIER domain
  Mpls packets arrive on BFIR from LDP domain, will be stitched to BIER domain Tree label (BTL) on BFIR
  BFIR has a list of all BFERs interested in the P2MP LSP and use it to build the BIER header.
  BFIR will use bier forwarding to forward the P2MP LSP to all BFERs interested.
  BFERs will swap the BIER domain Tree label to the corresponding P2MP LSP label and forward to the mLDP domain toward the leafs
Notes: NOKIA

## Slide 9
Thoughts/Questions?
Notes: NOKIA