## Slide 1: Deploying Hybrid Access Networks with MPTCP IETF104, March 2019
O. Bonaventure (Tessares)

## Slide 2: Motivation

## Slide 3: Using Multipath TCP to build Hybrid Access Networks
DSL
4G/LTE
Multipath TCP
Regular TCP
Hybrid Access
Gateway
TCP
TCP
See BBF's WT-378 and draft-ietf-tcpm-converters discussed within the tcpm working group

## Slide 4: Deploying Hybrid CPEs
Includes a transparent TCP<->MPTCP proxy
Three main types of deployments
  Proxy added to an existing xDSL CPE that is attached to an LTE CPE
    Allows to reuse existing CPEs, but performance issues
  Proxy in hybrid CPE that combines xDSL and LTE
    Requires replacing existing CPEs
  xDSL CPE modified to redirect IP packets to LTE CPE that includes Proxy
    Reuses existing CPEs and leverages performance of LTE CPE

## Slide 5: Running the proxy on an hybrid CPE
Hybrid CPE
HAG
DSL
LTE
SYN
SYN+MP-CAPABLE
SYN
SYN+ACK
SYN+ACK+MP-CAPABLE
SYN+ACK
@H
ADD_ADDR(@H)
SYN+MP-JOIN
TCP
TCP
MPTCP

## Slide 6: Running the proxy on an LTE CPE
DSL CPE
HAG
DSL
LTE
SYN
SYN+MP-CAPABLE
SYN
SYN+ACK
@H
LTE CPE
SYN
SYN+MP-CAPABLE

## Slide 7: Performance of Hybrid CPEs
Mainly depends on their CPU
  Example with Linksys WRT1200 AC using an Armada 385 @1.33 Ghz
DSL : X Mbps, 20 msec
LTE : X Mbps, 20, 50 or 80 msec

## Slide 9: The Hybrid Access Gateway
Deployment models depend on how the xDSL and LTE networks are organised
  Centralised HAG if they only converge in backbone
  Distributed HAGs located where both networks interconnect
    HAG can run on physical servers or inside virtual machines

## Slide 11: Conclusion
Multipath TCP enables Hybrid Access Networks that boost Internet access
Several deployment models for CPEs
  Hybrid CPE and two boxes solutions
Several deployment models for HAGs
  Centralised HAG and Distributed HAG
3GPP has recently selected Multipath TCP with the 0-rtt convert protocol for Access Traffic Steering Switch and Splitting (ATSSS) in 5G
  See discussion on draft-ietf-tcpm-converters in tcpm