## Slide 1: BIER-TE-ARCH IETF105 Prague
draft-ietf-bier-te-arch-03
Toerless Eckert (tte@cs.fau.de)
Gregory Cauchie (GCAUCHIE@bouyguestelecom.fr)
Michael Menth (menth@uni-tuebingen.de)

## Slide 2: Since IETF104
Entered WGLC after IETF104
Authors reviewed text.
  No technical changes
  But hard to understand document because of circular dependencies
  And missing explanation of relationship between traffic engineering and
    Native and/or overlay topologies
  Solution: Add more introductory text to resolve those issues
Rev’ed to draft-ietf-bier-te-arch-03

## Slide 3: Overview
Abstract improved
  This memo introduces per-packet stateless strict and loose path engineered replication and forwarding for Bit Index Explicit Replication packets ([RFC8279]). This is called BIER-TE.
  …(more improvements)... pls. Re-read
1.1 New section: Basic Examples
  One topology, full set of bits, explaining different packets
  “native” – adjacencies are L2 (forward_connected)
  “overlay” – adjacencies are remote (forward_routed)
2. Layering
  Add topology and explains in 3 sentences how topology comes into play.
8. Comparison with Segment Routing
  Extended: if you want to think of bits as segments, what does it mean ?
  Hopefully instructive to users of SR

## Slide 4: “Native” BIER-TE example
p5 p6
--- BFR3 ---
p3/ p13 \p7
BFR1 ---- BFR2 BFR5 ----- BFR6
p1 p2 p4\ p14 /p10 p11 p12
--- BFR4 ---
p8 p9
(simplified)
BIER-TE Bit Index Forwarding Tables (BIFT):
BFR1: p1 -> local_decap
p2 -> forward_connected to BFR2
BFR2: p1 -> forward_connected to BFR1
p5 -> forward_connected to BFR3
p8 -> forward_connected to BFR4
BFR3: p3 -> forward_connected to BFR2
p7 -> forward_connected to BFR5
p13 -> local_decap
BFR4: p4 -> forward_connected to BFR2
p10 -> forward_connected to BFR5
p14 -> local_decap
BFR5: p6 -> forward_connected to BFR3
p9 -> forward_connected to BFR4
p12 -> forward_connected to BFR6
BFR6: p11 -> forward_connected to BFR5
p12 -> local_decap

## Slide 5: “Overlay” BIER-TE example
p1 p3 p7
....> BFR3 <.... p5
........ ........>
BFR1 (Rtr2) (Rtr5) BFR6
........ ........>
....> BFR4 <.... p6
p2 p4 p8
(simplified)
BIER-TE Bit Index Forwarding Tables (BIFT):
BFR1: p1 -> forward_routed to BFR3
p2 -> forward_routed to BFR4
BFR3: p3 -> local_decap
p5 -> forward_routed to BFR6
BFR4: p4 -> local_decap
p6 -> forward_routed to BFR6
BFR6: p5 -> local_decap
p6 -> local_decap
p7 -> forward_routed to BFR3
p8 -> forward_routed to BFR4
Rtr2/Rtr5 do not speak BIER-TE

## Slide 6: BIER-TE Topology in the architecture
<------BGP/PIM----->
|<-IGMP/PIM-> multicast flow <-PIM/IGMP->|
overlay
[BIER-TE Controller Host] <=> [BIER-TE Topology]
^ ^ ^
/ | \ BIER-TE control protocol
| | | eg.: Netconf/Restconf/Yang
v v v
Src -> Rtr1 -> BFIR-----BFR-----BFER -> Rtr2 -> Rcvr
|--------------------->|
BIER-TE forwarding layer
|<- BIER-TE domain-->|
|<--------------------->|
Routing underlay
During bring-up or modifications of the network topology, the controller discovers the network topology and creates the BIER-TE topology from it: determine which adjacencies are required/desired and assign BitPositions to them. Then it signals the resulting of BitPositions and their adjacencies to each BFR to set up their BIER- TE BIFTs.

## Slide 7: BIER-TE Topology in the architecture
BIER-TE BitPosition (BP) can be understood as the BIER-TE equivalent of "forwarding segments" in SR, but they have a different scope than SR forwarding segments. Whereas forwarding segments in SR are global or local, BPs in BIER-TE have a scope that is the group of BFR(s) that have adjacencies for this BP in their BIFT. This can be called "adjacency" scoped forwarding segments.
Adjacency scope could be global, but then every BFR would need an adjacency for this BP, for example a forward_routed adjacency with encapsulation to the global SR SID of the destination. Such a BP would always result in ingres replication though. The first BFR encountering this BP would directly replicate to it. Only by using non-global adjacency scope for BPs can traffic be steered and replicated on non-ingres BFR.
SR can naturally be combined with BIER-TE and help to optimize it. For example, instead of defining BitPositions for non-replicating hops, it is equally possible to use segment routing encapsulations (eg: MPLS label stacks) for the encapsulation of "forward_routed" adjacencies.
Note that BIER itself can also be seen to be similar to SR. BIER BPs act as global destination Node-SIDs and the BIER bitstring is simply a highly optimized mechanism to indicate multiple such SIDS and let the network take care of effectively replicating the packet hop-by- hop to each destination Node-SID. What BIER does not allow is to indicate intermediate hops, or terms of SR the ability to indicate a sequence of SID to reach the destination. This is what BIER-TE and its adjacency scoped BP enables.

## Slide 8: THE END