## Slide 1
Inter-domain Multicast
using BIERv6
draft-geng-bier-ipv6-inter-domain-00
Presenter: Jingrong Xie
IETF105 2019-07-24 Montreal
Notes: 26/7/28
<number>

## Slide 2: Scenario: Hierarchial Multicast

## Slide 3: Solution: Static-bift for BIERv6
bier sub-domain 6 ipv6-underlay ##configuration for BR1
bfr-prefix 2001:DB8::B1:AB37
bfr-id 0
encapsulation ipv6 bsl 256 max-si 2
static-bift
nexthop 2001:DB8::B2:AB37 bfr-id 1 to 256 ##Note1
nexthop 2001:DB8::B3:AB37 bfr-id 257 to 512 ##Note1
bier sub-domain 6 ipv6-underlay ##configuration for PE1x
bfr-prefix 2001:DB8::E1:AB37
bfr-id 0
encapsulation ipv6 bsl 256 max-si 2
static-bift
nexthop 2001:DB8::B1:AB37 bfr-id 1 to 512 ##Note1
Note1: Use the BSL-SD-SI BIFT-id encoding method described in [I-D.ietf-bier-non-mpls-bift-encoding] as auto-generation method.

## Slide 4: Scenario: Peering Multicast

## Slide 5: Solution: auto-IR to each domain
# PE1x routing underlay layer configuration
bier sub-domain 6 ipv6-underlay
bfr-prefix 2001:DB8::E1:AB37
bfr-id 1
encapsulation ipv6 bsl 256 max-si 1
color 1 protocol isis
color 2 static-bift
next-hop 2001:DB8::B2:AB37 bfr-id 1 to 512
color 3 static-bift
next-hop 2001:DB8::B3:AB37 bfr-id 1 to 256
The following lists the BIFTs that will be constructed on PE1x:
BIFT corresponding to SD<6>/BSL<256>/SI<0> for color 1 ;;Ref1
BIFT corresponding to SD<6>/BSL<256>/SI<0> for color 2 ;;Ref2
BIFT corresponding to SD<6>/BSL<256>/SI<1> for color 2 ;;Ref3
BIFT corresponding to SD<6>/BSL<256>/SI<0> for color 3 ;;Ref4

## Slide 6: Solution: auto-IR to each domain
Overlay Multicast Flow steering to (Color, SD/BSL/SI, BitString) tuple on Ingress PE
(VRF<X>, S<S1>, G<G1>)
(Color<1>, SD<6>, BSL<256>, SI<0>, BitString<0001>) ;;Ref1
(Color<2>, SD<6>, BSL<256>, SI<0>, BitString<0001>) ;;Ref2
(Color<2>, SD<6>, BSL<256>, SI<1>, BitString<0001>) ;;Ref3
(Color<3>, SD<6>, BSL<256>, SI<0>, BitString<0001>) ;;Ref4
Color Extended Community carried in Leaf-AD route from Egress PE.
Leaf A-D route:
NLRI: RD, S, G, OrigIP, LeafIP
PMSI: Sub-domain, bfr-prefix, bfr-id
Color Extended Community: Color=1/2/3 (PE1y/PE2x/PE3x carry Color 1/2/3 resp.)

## Slide 7: Comments on the list (1)
For the “peering multicast”, how many BIER sub-domain do you have?
  haven't evaluate that so far.
  I initiate this idea when I found a recent rfc8313 and thought of the tenant spanning multiple DCs.
  Also I assume the multicast as a service draft for this case.
  The document assume a single BIER sub-domain (through multiple AS) for multicast deployment.

## Slide 8: Comments on the list (2)
What’s the real difference between “hierarchical multicast” and “peering multicast”, once you take away the color and MVPN aspects that I believe are orthogonal here?
  the hierarchical one is a P2MP case like IPTV in service provider.
  The peering one is an MP2MP case where the multicast source may be more unpredictable.
  From BIER point of view, there is still some difference.
  In current BIER Architecture, BIFT is constructed per the tuple of <SD/BSL/SI>.
  In the above Color case, BIFT is constructed per the tuple of <Color/SD/BSL/SI>.
  There may be some consideration of supporting multiple encapsulation in one <SD/BSL>, then the BIFT may be constructed per the tuple of <SD/BSL/Encap/SI>.
  Note the multicast overlay need to steering a flow to <Color/SD/BSL/SI> instead of <SD/BSL/SI>.

## Slide 9: Comments on the list (3)
What’s the significance of “inter-domain” here, that requires this new draft?
  static-configuration is not desired in intra-domain case since there is so automated IGP deployment.
  For Inter-domain case (mainly about inter-AS case as this document examples), static-configuration can be used, and I am used to understand things clearly by using static-configuration first.
  I will try to learn and understand how the dynamic protocol as proposed on the WG can be used for inter-domain.

## Slide 10: Comments on the list
What’s the uniqueness of IPv6 here?
  I found it difficult to construct the inter-domain BIFTs since the BIER-MPLS label is dynamic.
  SRGB is a thing I could thought of to use for static-configuration.
  Use of a static SRGB label as BIER-MPLS of a BR(border router) is wasteful, while use the SRGB for the entire domain seems not welcome in ietf102.
  This document assume the 'SD-BSL-SI' auto-generation of BIFT-ID is used consistently in all BFRs, makes inter-domain BIERv6 deployment easy.
  (1) inter-domain BIERv6 configuration is easy
  (2) inter-domain BIERv6 can skip non-BFRs completely.
  (3) inter-domain BFRs use only the BIERv6 encapsulation without any addition.

## Slide 11
Thank You
Thank you !
Request for
Comments/questions/discussions
Notes: 26/7/28
<number>