## Slide 1: draft-moran-suit-manifest-05
Brendan Moran

## Slide 2: Overview of manifest problem statement

## Slide 3: Problem Statement (1/6)
IoT devices need to be updated
  Security patches
  Functional bugs
  Feature deployment
  Time to market

## Slide 4: Problem Statement (2/6)
IoT updates should be easy:
  An author has firmware
  A device needs firmware
  Put the firmware on the device
IoT updates are not easy because:
  Many possible actors
  Diversity of update model
  Diversity of memory model
  Multiple functional units
  Security concerns

## Slide 5: Problem Statement (3/6)
Diversity of update model
  Active Partition (discard on update)
  Active Partition (swap)
  Multi-partition (execute in-place)
Diversity of memory model
  XIP
  Run-from-RAM
  OS + single application
  OS + multiple applications

## Slide 6: Problem Statement (4/6)
Update may have many actors with varying concerns and privileges
  Device OEMs
  Firmware/Software vendors
  Device operators
  Network operators
  Device Owners
  Users

## Slide 7: Problem Statement (5/6)
Devices may be composed of multiple functional units:
  One or more host processors
  Intelligent I/O
    Radio modules
    I/O controllers
  Intelligent peripherals
    Sensors with dedicated controllers
    Actuators with dedicated controllers

## Slide 8: Problem Statement (6/6)
Security Considerations
  Devices need to make decisions based on trust
  Trust must be established for any code or configuration either
    At time of installation
    At time of use
    Or, both
  Multiple actors adds complexity
    Different trust levels
    Trust for different operations
  Multiple functional units adds complexity
    Actors x Functional units x Operations

## Slide 9: Behavioural Manifest Summary

## Slide 10: Observations about updates
We can’t have many similar formats, there needs to be just one.
Simple parsers need few unique structures and low nesting levels.
Update use cases all use the same operations in varying orders.
An update consumer does not care what an update is, just what it should do.
Maybe a sequence of update-relevant commands?

## Slide 11: Behavioural manifests
Composed of several parts:
External information:
  Structure Version
  Sequence number
Common information
  Dependencies
  Components identifiers
  Common sequence
Command Sequences
  6 sequences
Text / text reference
Layout of the structure:
{
1 : version
2 : sequence number
3 : common
7 : dependency resolution
8 : payload fetch
9 : install
10 : validate
11 : load
12 : run
13 : text
}

## Slide 12: Summary of changes from 04 (1/?)
Common elements moved into nested in bstr
  Reduce parsing complexity
  Improve consistency in format
Changed encoding of command sequences:
  Was: [ + { SUIT_Command } ]
  Now: [ + SUIT_Command ]
    SUIT_Command is pairs of integer, argument

## Slide 13: Summary of changes from 04 (2/?)
Changed handling of optional sequences:
  Was: conditional sequences, no explicit structure
  Now: “try-each” list of conditional sequences. One must pass.
Added encrypted manifest support
  Cose Encrypt and detached payload added in outer wrapper as:
    3 : COSE_Encrypt
    4 : Manifest Ciphertext
Added “swap” directive
Defined SUIT-specific digest identifiers
Editorial changes