## Slide 1: draft-friel-anima-brski-cloud
Friel Cisco
Shekh-Yusef Avaya
Richardson Sandelman Software Works

## Slide 2: TL;DR
draft-ietf-anima-bootstrapping-keyinfra does not fully specify Default Cloud Registrar operation
draft-friel-anima-brski-cloud does
Use cases:
  A pledge bootstrapping from a location remote from the domain, and having no Join Proxy needs to discover the location of it's home Registrar.
  Use case: A pledge bootstrapping in a location in which there is not (yet?) a Registrar may need to use a Manufacturer provided service for onboarding

## Slide 3: Architecture
Pledge connects to Cloud Registrar on bootstrap and requests Voucher
  Mutual TLS enforced using IDevID and implicit TA
  Assumption is that Pledge has internet access
Choices, choices, choices
  Does Cloud Registrar issue Voucher or 3xx to Home Registrar?
  If Cloud Registrar issues Voucher, does it also issue suitably namespaced LDevID, or does it redirect to EST requests to home Registrar?
  If Cloud Registrar issues LDevID, how does it tell the Pledge about its home domain?
Cloud
Registrar
Pledge
Home
Registrar
MASA
Home
CA
Home
Services
Cloud
CA
Home Domain
Cloud
Lost
Multiple
Possible
signalling permutations

## Slide 4: Home Domain Mutual Authentication
Pledge must be imprinted with trust anchor for home Registrar
  Pledge may need to be imprinted with realm/domain name of home domain if trust anchor is a Public CA
  Details on realm/domain identity mapping and verification TBD
Home Registrar must either
  Have visibility to and verify Voucher issued by MASA that is bound to Pledge
  Verify locally significant LDevID that Pledge presents

## Slide 5: Cloud Registrar Redirects
Cloud Registrar replies with a 3xx to the Voucher Request
Pledge completes full BRSKI flow against Home Network
Cloud
Registrar
Pledge
Home
Registrar
MASA
Home
CA
Home
Services
Cloud
CA
Cloud
1. Voucher Request
-> 3xx
2. Voucher
Request
-> 200 OK
2. Voucher
Request
-> 200 OK
3. Enroll
-> 200 OK
3. Enroll
-> 200 OK
Home Domain

## Slide 6: Cloud Registrar Issues Voucher Home CA issues LDevID
Cloud Register issues Voucher
Cloud registrar replies with a 3xx to EST enrol / CSR Attributes requests
  A suboption is that Voucher includes EST domain
The Voucher issued by the Cloud must include the home network trust anchors
There is a problem here: The Home Network does not see the Voucher so how does it know to trust the Pledge i.e. the IDevID serial number?
  Could the Voucher be included as a Bearer?
  Does the Home Registrar need to fetch the Voucher from the Cloud?
  Does the Pledge need to be explicitly configured on both Home Doman and Cloud?
Cloud
Registrar
Pledge
Home
Registrar
MASA
Home
CA
Home
Services
Cloud
CA
Cloud
1. Voucher Request
-> 200 OK
3. Enroll
-> 200 OK
3. Enroll
-> 200 OK
2. Enroll
-> 3xx
+ Authorization:
Bearer Voucher??
Home Domain

## Slide 7: Cloud Registrar Issues Voucher Cloud CA issues LDevID
Two problems here:
How does the Cloud Registrar inform the Pledge about its home network for service access?
  Include a domain in the Voucher?
How is the LDevID suitably namespaces so that the home network can enforce policy?
  E.g. is the SAN off a home network subdomain:
    serial-number.pledges.home-network.com?
  RFC 5280 Name Constraints not suitable as the Cloud CA will be issuing LDevIDs for multiple home service domains
Cloud
Registrar
Pledge
Home
Registrar
MASA
Home
CA
Home
Services
Cloud
CA
Cloud
1. Voucher Request
-> 200 OK
3. Service Access
-> 200 OK
2. Enroll
-> 200xx
How is Pledge redirected Home ??
Home Domain

## Slide 8
Option 1
Cloud Registrar redirects
Option 2
Cloud Registrar Issues Voucher
Home CA issues LDevID
Option 3
Cloud Registrar Issues Voucher
Cloud CA issues LDevID
Could Voucher include Home Registrar / EST Domain?
How is Voucher given to Home Registrar?
How does Pledge discover Home Service Domain?
How is Cloud CA issued LDevID namespaced?
If the pinned-domain-cert is a Public CA, does the Voucher also include a home registrar domain / realm?
How many options should be supported?
Discussion / Next Steps?