## Slide 1: BGP-LS Filters A Framework for Network Slicing and Enhanced VPNs
draft-drake-bess-enhanced vpn-02
Adrian Farrel (adrian@olddog.co.uk) John Drake (jdrake@juniper.net) Luay Jalil (luay.jalil@verizon.com) Avinash Lingala (ar977m@att.com)
BESS Working Group – IETF 106 – Singapore, November 2019

## Slide 2: Network Slicing/Enhanced VPN
Described in draft-ietf-teas-enhanced-vpn
A set of VPN overlay networks over a common underlay network
  Different performance and scaling properties
  Each requires a subset, either dedicated or shared, of the underlay network resources
  First proposed for 5G mobile networks (network slicing)
Requires a mechanism to inform each VPN of the underlay network resources (links and nodes) it can use
Each VPN uses only those resources
  Segment routing or RSVP-TE
Approach is a generalization of SR TE policy
  Supports MP2MP, P2MP, and P2P bi-directional topologies
  Integrates BGP-VPN support (L3VPN, EVPN)
  DSCP and Color based forwarding

## Slide 3: Approach
Network Controller performs global optimization across all enhanced VPNs
  [Source, Destination] traffic matrix for each VPN
  Performance and scaling properties for each VPN
  Underlay network topology (BGP-LS northbound)
Network controller assigns P router link bandwidth to DSCP or adjacency SID
Each enhanced VPN gets a subset of the underlay network resources
  BGP-LS Filter
  PEs have a complete view of underlay network resources, BGP-LS Filter acts as a filter
  Encoded w/ BGP-LS (southbound)
Granularity
  All PEs in a VPN
  Set of PEs in a VPN
  Individual PE in a VPN
Distribute BGP-LS Filter to PEs using standard VPN tools
  Route targets (RTs), route reflectors, RT constraints

## Slide 4: Approach – Continued
BGP-LS
  Integrates easily /w VPNs
  Supports segment routing and RSVP-TE
  Supports inter-AS
  Supports both IS-IS and OSPF
  No new invention required
Follows VPN scaling model
  Per-VPN information restricted to its PEs
  P-routers have no per-VPN information
Non-enhanced VPN PEs don’t receive BGP-LS Filters
  Network controller ensures underlay network resources for enhanced VPNs have higher IGP and TE metric
  Enhanced VPNs may use non-enhanced VPN underlay network resources

## Slide 5: BGP-LS Filter
Provides connectivity between the PEs in a VPN or set of VPNs
Should provide multiple paths between a given ingress/egress PE pair
Tagged with the RTs of the VPNs whose PEs are to import it
When sending a packet an ingress PE
  Selects a path to the egress PE using the BGP-LS Filters for the packet’s VPN
  Adds a segment routing header to the packet *OR*
  Places the packet in an RSVP-TE LSP using that path
  Can use any path computation it wishes as long as path is constrained
An underlay network link or node may appear in multiple BGP-LS Filters
  Requires AFI (BGP-LS) and SAFI (BGP-LS-VPN) w/ a different RD for each BGP-LS Filter
Requires a new attribute for a BGP-LS UPDATE

## Slide 6: BGP-LS Filter example
PE1
PE2
PE3
PE4
PE1
PE2
PE3
PE4
PE1
PE2
PE3
Base Network Topology
BGP-LS from Controller:
  Filter filter1:
  Nodes, Links, Color
  Community X, Y
BGP-LS from Controller:
  Filter filter2:
  Nodes, Links, Color
  Community Z

## Slide 7: BGP-LS Filter Attribute
Assumptions:
  A PE may import more than one BGP-LS Filter
  A BGP-LS Filter may change over time
  A given BGP-LS Filter may contain multiple BGP-LS UPDATEs
  The BGP-LS UPDATEs for a given BGP-LS Filter may arrive in any order
  The BGP-LS UPDATEs for multiple BGP-LS Filters may be interleaved
This requires:
  A Filter identifier
  A version number
  A Filter type (MP2MP, P2MP, P2P (uni- or bi-directional) )
  Total # of fragments
  Fragment # of the current fragment
Also may contain a DSCP and/or a Color List
  If present, indicates which DSCPs and/or Colors may use it

## Slide 8: Details
Cannot use a BGP-LS Filter until it is completely assembled
Underlay network resource can only be used if active
Underlay network topology is the union of all imported BGL-LS Filters
Filter precedence: P2P, P2MP, MP2MP
New version of BGP-LS Filters when
  The PE membership of a given VPN changes
    Network controller must track PE membership
  The underlay network topology changes
    Not required if connectivity still exists
Enhanced VPNs may use non-enhanced VPN underlay network resources when:
  A new PE is activated
  No connectivity to an egress PE
Should be corrected when new BGP-LS Filters are received

## Slide 9: Plans
Check back with draft-ietf-teas-enhanced-vpn
Work with authors of related drafts…
  draft-dong-spring-sr-for-enhanced-vpn
  draft-dong-teas-enhanced-vpn-control-plane
  draft-dong-idr-bgpls-sr-enhanced-vpn
  … We believe that the concepts are similar and that our draft is a functional superset
Iterate the draft
Discuss with implementers