## Slide 1
BIER IPv6 Encapsulation
draft-xie-bier-ipv6-encapsulation-03
IETF106 BIER WG, 2019-11 Singapore
Jingrong Xie (Huawei)
Liang Geng (China Mobile)
Mike McBride (Futurewei)
Rajiv Asati (Cisco)
Senthil Dhanaraj (Huawei)
Speaker: Liang Geng
Notes: 26/7/30
<number>

## Slide 2
IPv6 network
CE1
A
D
bfrid=3
CE3
IPv4/6 Hdr:
SA: X, DA: mcX
Payload
B
Outer IPv6 Header &
BIER Header in DOH
IPv6 Hdr(Outer):
SA: A::1, DA: B::2
Dest Opt Hdr (BIER Hdr in):
BIFTid: xxx, BitString: 0110
IPv4/6 Hdr(inner):
SA: X, DA: mcX
Payload
C
bfrid=2
Inner IPv4/IPv6
multicast packet
CE2
IPv6 Hdr(Outer):
SA: A::1, DA: D::4
Dest Opt Hdr (BIER Hdr in):
BIFTid: xxx, BitString: 0100
IPv4/6 Hdr(inner):
SA: X, DA: mcX
Payload
IPv4/6 Hdr:
SA: X, DA: mcX
Payload
IPv4/6 Hdr:
SA: X, DA: mcX
Payload
E
non-bier
Standard BIER Header in IPv6 Destination Options Header.
Unicast Address of BFIR in IPv6 Source Address field.
Unicast Address of Neighbor BFR in IPv6 Destination Address field.
BFR gets an End.BIER indication by FIB lookup, and process the BIER header in DOH.
The proposed BIER IPv6 encapsulation

## Slide 3: Comply with the BIERv6 requirements (1)
Req 4.7. BIER architecture support ----Yes/Comply
  Multiple Sub-domains
  Multiple Sets for scalability
  Multiple BSLs (64,128,256,…,4096)
  Multiple BIFTs for ECMP
  Bypassing non-BIER routers or bypassing Layer-2 switches
  BIER architecture support comes from the fact that
    Standard BIER Header encoding does not change (per the past IETF 102-105 meetings).
    Standard BIER Header encapsulated in existing IPv6 EH (Dest Options Header).

## Slide 4: Comply with the BIERv6 requirements (2)
Req 4.3. L4 Inspection not required ----Yes/Comply
Req 4.11. Support Fragmentation ----Yes/Comply
Req 4.12. Support IPv6 Security ----Yes/Comply
  BIER forwarding and BitString modifying by Layer-3 headers.
  No Conflict with other Layer-3 functions:
    Fragmentation and Assembly on BFIR and BFERs only.
    IPSEC Confidentiality or Integrity on BFIR and BFERs only.

## Slide 5: Comply with the BIERv6 requirements (3)
Req 4.2 Hop by hop SA or DA modification ----Yes/Comply
  DA modification by each BFR to its NBR-BFR
    Using unicast DA for many benefits (per the past IETF 102-105 meetings)
      Bypassing Layer-3 Non-BFR router(s) or Layer-2 switch(es).
      One encapsulation/forwarding method for one-hop and multi-hop cases.
  No SA modification by each BFR to its NBR-BFR
    Once the IPv6 Source Address is set by BFIR.
      Receiving notices on the BFIR for functions of PING, TRACE and MTU
      For better SA filtering and data origin authentication.
      No SA change helps reducing cost when forwarding packet.

## Slide 6: Comply with the BIERv6 requirements (4)
Req 4.1. L2 Agnostic ----Yes/Comply
  Based on IPv6 unicast, and can run on various link types.
Req 4.4. Multicast address in SA field not allowed ----Yes/Comply
  Multicast address in SA field not used or required.
Req 4.5. Incorrect bits handling ---Yes/Comply
  BitString update per 8279 prevents duplication.
Req 4.6. SA filtering ----Yes/Comply
  Unchanged IPv6 address of BFIR as SA helps SA filtering.
Req 4.8. Simple Encapsulation ----Yes/Comply
  One encapsulation for one-hop and multi-hop replication.
Req 4.9. Hardware fast path ----Yes/Comply
  Forwarding based on IPv6 DA lookup and BIER Header
Req 4.10. Conform to existing IPv6 Spec ----Yes/Comply
  Existing IPv6 Extension Header with option TLV extension.

## Slide 7: Next Step
First revision post in April 2018, based on a lot of earlier work before.
  Based on earlier V6 drafts and requirements since 2016 (ietf97 to ietf100).
  Based on working group charter V2 in early 2018 (ietf101).
Has been stable since rev-03, based on a lot of improvements before.
  Based on discussions since its first post (ietf102 to ietf103).
  Based on discussions on the requirements draft (ietf104 to ietf105).
It’s mature, and we’d like to ask for working group adoption.
Thank you !