## Slide 1: DetNet Data Plane Drafts IP, MPLS and Sub-Nets (IP, MPLS)
Balázs Varga, Don Fedyk, Lou Berger, Andrew Malis, Stewart Bryant, János Farkas, Jouni Korhonen
DetNet WG
Singapore, 21st November, 2019

## Slide 2: Data plane documents Status
Building block approach
DetNet Data plane drafts
draft-ietf-detnet-data-plane-framework-03
draft-ietf-detnet-ip-03
draft-ietf-detnet-mpls-03
draft-ietf-detnet-ip-over-mpls-03
draft-ietf-detnet-mpls-over-udp-ip-03
draft-ietf-detnet-ip-over-tsn-01
draft-ietf-detnet-mpls-over-tsn-01
draft-ietf-detnet-tsn-vpn-over-mpls-01
TSN VPN over DetNet
DetNet over sub-net
DetNet IP|MPLS
Data plane framework

## Slide 3: DetNet Data Plane: IP draft-ietf-detnet-ip-03
Content
  specifies the Deterministic Networking data plane when operating in an IP packet switched network.
DetNet IP Data Plane
  DetNet forwarding sub-layer only
DetNet IP Data Plane Procedures
  Flow identification: 6-tuple (5-tuple + DSCP)
Management and Control Information Summary
Note: the DetNet IP data plane does not perform additional encapsulations but operates on the IP header fields already in place.

## Slide 4: DetNet Data Plane: IP Management and Control Information Summary
Set of information that is needed to identify individual and aggregated DetNet flows:
IPv4 and IPv6 source address field.
IPv4 and IPv6 source prefix length.
IPv4 and IPv6 destination address field.
IPv4 and IPv6 destination prefix length.
IPv4 protocol field.
IPv6 next header field.
DSCP field in IPv4 Type of Service and IPv6 Traffic Class.
DSCP list in IPv4 Type of Service and IPv6 Traffic Class.
IPv6 flow label field.
TCP and UDP Source Port. Exact and wildcard matching. Port ranges optional.
TCP and UDP Destination Port. Exact and wildcard matching. Port ranges optional.
IPsec Header SPI field. Exact matching is required.
ECN omitted
In order to maximize reuse of 5-tuple based mechanisms, DetNet aware applications and end systems SHOULD NOT mix DetNet and non-DetNet traffic within a single 5-tuple.

## Slide 5: DetNet Data Plane: MPLS draft-ietf-detnet-mpls-03
Content
  specifies the Deterministic Networking data plane when operating over an MPLS Packet Switched Networks.
DetNet MPLS Data Plane
  DetNet service sub-layer
  DetNet forwarding sub-layer
DetNet MPLS Data Plane Procedures
  Flow identification: Labels
  Sequence number: d-CW
Management and Control Information Summary
Note: zero or more F-labels

## Slide 6: DetNet Data Plane: MPLS Management and Control Information Summary
Service Sub-Layer Information
App-Flow identification information
Sequence number length
S-Label for the service
PRF used or not
Associated forwarding sub-layer information
Service sub-layer (for received traffic)
Associated forwarding sub-layer information
S-Label for the received service
PEF or POF is to be provided
Sequence number length
Service Aggregation
S-Labels or F-Labels that are to be carried over each aggregated service
A-Label associated with each aggregated service
Other S-Label information summarized above
Forwarding Sub-Layer Information
Outgoing F-Label stack
Traffic parameters associated with a specific label in the stack
Outgoing interface and next hop (for unicast traffic)
Sub-network specific parameters
Forwarding sub-layer (for received)
Incoming interface
Incoming F-Label stack to be popped
Incoming forwarding sub-layer flow
Note: Required information depends on the DetNet node type and the DetNet functions being provided.
ONLY some editorial changes.

## Slide 7: DetNet Data Plane: IP over MPLS draft-ietf-detnet-ip-over-mpls-03
Content
  specifies the Deterministic Networking data plane when operating in an IP over MPLS packet network.
IP over DetNet MPLS
  Data plane scenarios
  Encapsulation
IP over DetNet MPLS Procedures
  Flow identification
  Traffic treatment
Management and Control Information Summary

## Slide 8: DetNet Data Plane: IP over MPLS Management and Control Information Summary
At the MPLS ingress node:
Each MPLS App-Flow is identified using the IP flow identification information as defined in [I-D.ietf-detnet-ip]. Includes all wildcards, port ranges and ability to ignore specific IP fields.
The DetNet MPLS service that is to be used to send the matching IP traffic. Includes both service and traffic delivery information.
At the MPLS egress node:
S-Label values that are carrying MPLS over IP encapsulated traffic.
For each S-Label, how the received traffic is to be handled.
ONLY some editorial changes.

## Slide 9: DetNet Data Plane: MPLS over UDP/IP draft-ietf-detnet-mpls-over-udp-ip-03
Content
  specifies the MPLS Deterministic Networking data plane operation and encapsulation over an IP network.
DetNet MPLS over DetNet IP
IP over DetNet MPLS Procedures
Management and Control Information Summary

## Slide 10: DetNet Data Plane: MPLS over UDP/IP Management and Control Information Summary
Set of information that is needed to configure DetNet MPLS over UDP/IP
Label information (S-label or F-label) to be mapped to UDP/IP flow.
IPv4 and IPv6 source address field.
IPv4 and IPv6 destination address field.
IPv4 Type of Service and IPv6 Traffic Class Fields.
UDP Source Port.
UDP Destination Port.
ONLY some editorial changes.

## Slide 11: Summary – Next Steps
Shepherd review: DONE
WG last call: FINISHED
  Started: 28th October
  Ended: 11th November
Ready for submission to the IESG …
Draft: | WG last call
draft-ietf-detnet-ip-03 | 
draft-ietf-detnet-ip-over-mpls-03 | 
draft-ietf-detnet-mpls-03 | 
draft-ietf-detnet-mpls-over-udp-ip-03 | 

## Slide 12
Thanks …