## Slide 1: TCP ACK Pull draft-gomez-tcpm-ack-pull-01
Carles Gomez
Universitat Politècnica de Catalunya
Jon Crowcroft
University of Cambridge
IETF 106 – Singapore, November 2019

## Slide 2: Status
  Initial version presented in IETF 105
  Updated version is -01
  Incorporate feedback from the room

## Slide 3: Motivation
  Delayed ACKs may be detrimental
  Segment carrying a message of up to 1 MSS, no app-layer response, 2nd data segment not sent earlier than Delayed ACK timer
  Unnecessary delay
  Consequences
  Using Nagle, the sender may be prevented from sending more data while awaiting the ACK
    High underperformance in high bit rate environments (e.g. DNS stateful operations, RFC 8490)
  IoT devices
    Memory resources cannot be released until ACK arrival
    Increased energy consumption
    Delay might be exacerbated (in some L2 mechanisms)

## Slide 4: ACK Pull mechanism
  Use of a TCP header reserved bit: AKP flag
  A sender sets the AKP flag to request an immediate ACK for a data segment
  Upon reception of a data segment with AKP flag set, a receiver (conforming to this spec) MUST send the ACK immediately
13th and 14th bytes of the TCP header

## Slide 5: Updates in -01
  Introduction
  Delayed ACK timer value of ~50 ms
  Presented problem: low performance, solution avoiding (header, packet) overhead
  Annex. Alternative approaches
  AckCC [RFC 5690]
    Sender tells the receiver the ACK ratio “R” to be used
    “TCP ACK Congestion Control Permitted” option (2 bytes)
    “TCP ACK Ratio” option (3 bytes)
  TLP
    Additional ACKs at the receiver by sending probe segment
  Workarounds
    Sending an old byte
    “Split hack” (Contiki OS): splitting a message into two segments

## Slide 6: Further motivation and approaches
  Delayed ACK suppression during slow start
  Getting up to speed fast without inducing much queue
    draft-kuehlewind-tcpm-accurate-ecn-03
    Discussions in the context of QUIC
  Active Detection of Classic ECN AQMs
  “Rather niche”
  Trigger quick ACKs
  Middlebox traversal of bits 4-6
  Not so good?
  Use Urgent Pointer
  E.g. use 3 bits to define an ACK ratio exponent
Thanks to Bob Briscoe!

## Slide 7: Questions/Comments ?
IETF 106 – Singapore, November 2019
Carles Gomez
Universitat Politècnica de Catalunya
Jon Crowcroft
University of Cambridge