## Slide 1: L-band Digital Aeronautical Communications System (LDACS) draft-maeurer-raw-ldacs-01
Presenter: Nils Mäurer
Authors: Thomas Gräupl, Corinna Schmitt

## Slide 2: Note Well

## Slide 3: https://tools.ietf.org/pdf/draft-bernardos-raw-use-cases-03.pdf
Use Case for LDACS: Aeronautical Networking
Air traffic expected to double by 2040 compared to 2018 However, most aircraft use analogue voice communications today which creates a bottleneck for growth
Aeronautical communication shall therefore transition to IPv6/aeronautical datalinks which is called the “FCI”
  Three aeronautical datalinks for FCI: LDACS, AeroMACS, and SatCOM
  FCI shall support quality of service, diversity, and mobility under the umbrella of the "multi-link concept”
Relevance for RAW:
  Reliability and availability shall be achieved using the “multi-link” concept i.e. multi-homed aircraft networks

## Slide 4: https://tools.ietf.org/pdf/draft-maeurer-raw-ldacs-01.pdf

## Slide 5: https://tools.ietf.org/pdf/draft-maeurer-raw-ldacs-01.pdf

## Slide 6: Essential Updates in Version 01
Clarification of IPv6 network for the Future Communications Infrastructure (FCI)  4. Provenance and Documents
Description of LDACS’s MAC layer design  5.5.1 LDACS Medium Access
Explanation of LDACS’s mobility support & deployment vision  5.5.2 LDACS Mobility, 5.5.3 LDACS Incremental Deployment
Description of protocol layer services  6. Protocol Stack

## Slide 7: LDACS’s Protocol Stack & Services
Physical layer: OFDMA on two FDD radio channels; 500 kHz each; hardened against aeronautical interference.
Data link layer: Resource request/reservation through centralized scheduling (MAC); priority aware; reliable through automatic retransmissions (DLS).
Sub network link layer: LDACS sub-net management (LME); user plane cryptography (SNP)
OFDMA = Orthogonal Frequency-Division Multiplexing Access; FDD = Frequency Division Duplex

## Slide 8: MAC Layer Design – Frame Structure
FL: Forward Link
RL: Reverse Link
DCH: Data Channel
CCCH: Common Control Channel
DCCH: Dedicated Control Channel
BCCH: Broadcast Control Channel
RACH: Random Access Channel
MF: Multi-Frame
SF: Super-Frame

## Slide 9: Mobility Support & Deployment Vision
Mobility service manages in the GSC and LME cell entry, cell exit and handover between cells.
  Internal handovers to different RF channels may be initiated by the aircraft or by the GS.
  External handovers between non-connected LDACS deployments or different aeronautical data links shall be handled by the FCI multi-link concept.
Development is envisioned in an incremental manner.
  Data link provides enhanced capabilities to the future IPv6 based ATN enabling it to better support user needs and new applications.
  The deployment scalability of LDACS allows its implementation to start in areas where most needed to improve immediately the performance of already fielded infrastructure. Later the deployment is extended based on operational demand

## Slide 10: Benefits of LDACS
High data rate (< 2 Mbit) 4G-like data link
Designed for long-range communication (<400 km) in regulated aeronautical spectrum (~ 1 GHz)
Designed with safety-of-life use cases (i.e. air traffic management)  reliability, predictability, and suitable for regulated spectrum (as required by the use case)
Designed with multi-link IPv6 as network layer in mind
Transition of aeronautical networks from ACARS and OSI to IP network protocols
Open standard at ICAO under development

## Slide 11: Benefits of LDACS – Relevance for RAW
High data rate (< 2 Mbit) 4G-like data link
Designed for long-range communication (<400 km) in regulated aeronautical spectrum (~ 1 GHz)
Designed with safety-of-life use cases (i.e. air traffic management  reliability, predictability, and suitable for regulated spectrum (as required by the use case)
Designed with multi-link IPv6 as network layer in mind
Transition of aeronautical networks from ACARS and OSI to IP network protocols
Open standard at ICAO under development