## Slide 1: draft-ietf-lpwan-coap-static-context-hc-15
Authors:
Ana Minaburo
Laurent Toutain
Ricardo Andreasen

## Slide 2: Status
IESG State: 1 Discussion. Enough positions to pass once DISCUSS position is resolved
Reviews:
  SECDIR: Discuss + Nits
  genart, iotdir, opsdir, tsvart: No Objection
Thank you to the reviewers for their valuable inputs
draft-ietf-lpwan-coap-static-context-hc-15
  Benjamin Kaduk
  Francesca Palmobini
  Alexey Melnikov
  Deborah Brungard
  Alissa Cooper
  Roman Danyliw
  Martin Duke
  Erik Kline
  Murray Kucherawy
  Warren Kumari
  (Mirja Kühlewind)
  Barry Leiba
  Alvaro Retana
  (Adam Roach)
  Martin Vigoureux
  Magnus Westerlund
  Robert Wilton
  Theresa Enghardt

## Slide 3: Changes from v13 to v15
Section 2. Applying SCHC to CoAP headers
  Figure 1 has been divided in 3 different scenarios.
draft-ietf-lpwan-coap-static-context-hc-15
CoAP
UDP
IPv6
SCHC
LPWAN
Device
CoAP
UDP
IPv6
NGW
IPv6
SCHC
LPWAN
App
Figure1. C/D at the LPWAN boundaries
Device
NGW
App
Figure2. Standalone CoAP End-to-End C/D
CoAP
SCHC
UDP
IPv6
SCHC
CoAP
SCHC
UDP
IPv6
IPv6
SCHC
LPWAN
LPWAN
Device
NGW
App
Figure3. OSCORE C/D
CoAP inner
SCHC
UDP
IPv6
SCHC
CoAP inner
SCHC
UDP
IPv6
IPv6
SCHC
LPWAN
LPWAN
CoAP outer
CoAP outer

## Slide 4: Changes from v13 to v15
Section 4. Compression of CoAP header fields
  Eliminate the unidirectional/bidirectional confusion
draft-ietf-lpwan-coap-static-context-hc-15
Rule 8724
FID | FL | FP | DI | TV | MO | CDA | Sent bits
CoAP version | 2 | 1 | bi | 01 | equal | Not-sent | 
CoAP Type | 2 | 1 | up | 0 | equal | Not-sent | 
… |  |  |  |  |  |  | 
CoAP URI-Path | var | 1 | up | temperature | equal | Not-sent | 
CoAP Uri-Path | var | 1 | dwn | 0: update 1: inventory 2: password | Match-mapping | Mapping-sent | 2

## Slide 5: Changes from v13 to v15
Section 5. Options
  Defined the solution for the any option
    Options are defined with the D-T L V format
    Any option with this format definition could be compress with SCHC
      D-T => Field ID
      L => Field length
      V => Target value
Section 9. Security
  Improvements on this section
    Security of RFC8724 applies when LPWAN is used
    Security of RFC8613 applies when using OSCORE
    DoS attacks are possible causing excessive resource consumption
    SCHC may avoid some of those attacks because the length sent is the one of the compressed header and not the one of the original header.
    The size of the IV for OSCORE has been rewritten. The size has an impact on the frequency the key is renewed.
draft-ietf-lpwan-coap-static-context-hc-15

## Slide 6: To solve: Discussion – v16
Section 2. Applying SCHC to CoAP headers
  Difficult to follow, more explanation
  Put the difference between dashed and dot lines
Section 3.1 Remain talking about unidirectional and bidirectional
  Update this section and explain how SCHC works on defining the description of each field
Section 5. CoAP Options
  Reflect the Options compression and How to address future options? (explained before)
Section 9. Security Considerations
  Add the inputs from Benjamin DISCUSSion
draft-ietf-lpwan-coap-static-context-hc-15

## Slide 7: Thank you
Questions?
draft-ietf-lpwan-coap-static-context-hc-15