## Slide 1: draft-moran-suit-mud-00
Brendan Moran

## Slide 2: The big question
Who is qualified to define what a device should do when connected to your network?

## Slide 3: Problem Domain
MUD describes rules for a device’s communication
Devices announce MUD URLs.
  Unauthenticated:
    LLDP
    DHCP
  Authenticated:
    802.1X, embedded in client certificate
Unauthenticated model is not resilient
Service hosting MUD URL can set network policies.
  MUD policies are subject to change.
For MUD signatures, Root of Trust requires an audit.
  See RFC8520 section 13.2

## Slide 4: Complexities
Device could report wrong MUD URL (excluding 802.1X)
  MUD manager must track devices changes
The server hosting the MUD URL can set network policy
  Requires audit
  RFC8520 => check web reputation
  MUD Signature
Rogue CA can authorize MUD signer
Device communication may be altered by configuration
  May require multiple MUD URLs for single class of devices

## Slide 5: Simplifying the trust model
The entity that creates IoT device software:
  Signs firmware updates
  Knows how the device communicates
  Knows what policies are required
The entity that creates IoT device configuration
  Knows how that alters device communication
  Knows how that changes device policies
    E.g. IPv4 / IPv6
These entities could specify a MUD file, or explicitly authorize a signer

## Slide 6: MUD + SUIT + EAT
SUIT manifest specifies a MUD file
  Early delivery of MUD files
  Binds firmware/configuration to MUD file
Or, SUIT manifest specifies a MUD signer:
  Normal MUD URL
  Delivers Trust Anchor for MUD Signatures
Attest several values to reduce complexity
  SUIT Manifest digest
  MUD URL
  MUD Digest
  MUD Signer ID
MUD Manager can be a Relying Party
  Verify correspondence between cached SUIT Manifest & reported MUD info

## Slide 7: Advantages
Reduces number of actors
  Provides explicit link from Firmware Authority to MUD
    Simplifies/Eliminates audit for MUD Signer
    Makes Firmware Authority responsible for MUD Signer
    No CA needed => Devices reject Firmware Authority changes
  Removes MUD File hosting from threat model
Multiple MUD files possible
  Composition required
  Augment static MUD file with dynamic MUD file
  Use lookup from database based on attestation information rather than URI
Reduces need for explicit onboarding flow
Provides option for explicit version binding
Provides alternative to 802.1X for MUD URL reporting with authentication

## Slide 8: Next Steps
Send to working group?
  SUIT?
  RATS?
  Other?