## Slide 1: draft-ietf-bier-mld BIER Ingress Multicast Flow Overlay using Multicast Listener Discovery Protocols
Pierre Pfister, pierre.pfister@darou.fr
IJsbrand Wijnands, ice@cisco.com
Markus Stenberg, markus.stenberg@iki.fi
Stig Venaas, stig@cisco.com
Cui (Linda) Wang, lindawangjoy@gmail.com
Zheng (Sandy) Zhang, zhang.zheng@zte.com.cn

## Slide 2: BIER MLD/IGMP Sender Info
Currently the source address is assumed to be the BIER prefix so that one can derive the BFR-ID of the sender, and using configuration and potentially the destination address to determine the sub-domain.
This info can be derived from the BIER header, but the L3 code may not have access to the BIER header.
Latest revision uses an IGMP-MLD extension to include Sender info
  Similar to the pim overlay using a join attribute with Sender Info
  Only for use with this overlay (MLD/IGMP with BIER encapsulation)
The generic IGMP-MLD extension mechanism is defined in draft-ietf-pim-igmp-mld-extension
  Passed pim WGLC and publication has been requested

## Slide 3: Generic IGMP-MLD extension defined by pim wg (1/2)
An MLDv2 report looks like this:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = 143 | Reserved | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|E| Reserved |Nr of Mcast Address Records (M)|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .
. Multicast Address Record [1] .
. .
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .
. Multicast Address Record [M] .
. .
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension |
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 4: Generic IGMP-MLD extension defined by pim wg (2/2)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Type 1 | Extension Length 1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Value 1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+- . -+
. . .
. . .
+- -+
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Type n | Extension Length n |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Value n |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 5: BIER IGMP-MLD extension
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ext Type TBD | Value length 1 + 2 + (4 or 16)|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sub-domain ID | BFR-ID | BFR-Prefix … |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Prefix Continued |
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Note that the BFR-prefix is not aligned here, the total value length is 7 or 19

## Slide 6: Next steps?
Ready for WG last call?