## Slide 1
draft-thubert-intarea-schc-over-ppp
Authors:
Pascal Thubert <pthubert@cisco.com>
IETF 110, Virtual, March 10th, 2021

## Slide 2: draft-thubert-intarea-schc-over-ppp
SCHC over PPP (and then PPP over foo)
Enables SCHC over
  Serial, 3GPP
  Ethernet with PPPoE, Wi-Fi with Ethernet
Signals
  A new compression for PPP (Updates RFC 5172)
  The URL of the data model for the compression
  Dependency on draft-ietf-lpwan-schc-yang-data-model
2
draft-thubert-intarea-schc-over-ppp

## Slide 3: Resulting Packet (no Frag example)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ Source MAC Address +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Destination MAC Address +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ethernet Frame Type(0x8864) | Ver=1 | Type=1| Code=0 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session ID | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| PPP Protocol (IPv6) = 0x0057 |0|0| SCHC RuleID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
... Compression ...
| Residue +-+-+-+
| | Pad |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| |
| Uncompressed |
... Original ...
| Payload |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
draft-thubert-intarea-schc-over-ppp

## Slide 4: Draft status: Stable
Need refresh – expires March 26th
The RuleID for a compression rule is expressed as 2 bytes.
The first (leftmost) 2 bits of that RuleId MUST be set to 0
Frag: Only No-Ack mode => no out-of-order packet
  If used with DetNet => may require PREOF reordering
The RuleID for a fragmentation rule is expressed as 4 bits
  Reserved 1111 for NO ACK
Review from LPWAN cc INT AREA ?
4
draft-thubert-intarea-schc-over-ppp

## Slide 5: Impact on SCHC Architecture
PPP creates a peerwise relationship as opposed to device/gateway
None of the end points own the compression rules
Both fetch them from the same place through URL
5
draft-thubert-intarea-schc-over-ppp

## Slide 6
Ethernet
Pseudowire
WiFi
VxLAN
Switch / Router
(act as device)
Rule base
speaker
Switch / Router (act as GW)
Ethernet
Or Serial
IPv6CP Config. Req. with Option 2 (
IPv6-Compression-Protocol = SCHC,
Rule set URL = https:// blah )
handshake
Protocol determination
Rule set Selection based on device/prot
GET(Rule set URL)
Rule set
GET(Rule set URL)
Rule set
Discovery (RFC 2516 PADx or LISP)
LCP Config. (Magic Nb LCP, no PFC)
IPv6CP Configuration Ack.
listener
draft-thubert-intarea-schc-over-ppp

## Slide 7: Discussion
Co Authors?
Add applicability statement?
Possible extensions?
7
draft-thubert-intarea-schc-over-ppp