## Slide 1: DLEP for RAW
Rick Taylor
Airbus Defence & Space
IETF 110 – RAW Working Group

## Slide 2: What is DLEP?
Dynamic Link Exchange Protocol (DLEP)
  RFC 8175, Standards Track.
  Developed for Mobile Ad-hoc Networks, in the MANET WG, but applicable elsewhere.
A monitoring protocol that runs between a Router (Layer-3 device) and a Modem (Layer-2 wireless device)
  It is not an “over the air” protocol; that is the domain of the link-layer technology.
  But it allows the link-layer information to be passed ‘up’ to the IP layer.
Increasing adoption by radio and network device vendors since publication.
  Now being specified as a requirement in large government contracts in US and EU. IETF Standard, avoiding vendor lock-in, etc.

## Slide 3: What does DLEP provide?
DLEP provides the following information:
  Reachability: What ‘destinations’ are currently reachable via the link-layer?
    Includes Unicast and Multicast, keyed by MAC address.
    Can include Layer-3 information, e.g. IPv4 addresses and routes, to avoid unnecessary ARP/ND and/or act as a basic route sharing mechanism.
  Capability: What are the characteristics of the logical link between the current node, and a reachable destination, e.g.:
    Current raw data-rate for Tx/Rx, allowing for asymmetric links.
    Latency. <- This is very relevant for RAW.
    Theoretical maximum raw data-rate for Tx/Rx, e.g. 11 Mbps for 802.11b.
    Resources available at the destination.
    Relative Link Quality, a percentage heuristic.
    MTU.
Note: In DLEP a ‘destination’ is a device attached to a remote terminal, rather than the remote modem itself. In the case of multicast destinations, it is the set of all reachable destinations participating in the multicast group.
Notes: Link metrics are defined in Layer-3 terms

## Slide 4: DLEP is Dynamic
The clue is in the name :-)
DLEP is session-based, and provides information dynamically throughout a session lifetime.
  Event-driven protocol provides timely information, avoiding the need to repeatedly poll SNMP or other management API.
Link capabilities are intentionally defined in terms that make sense at Layer-3, e.g. Data-rate in bps rather than symbol rate, as the target audience of the metrics is a Layer-3 device.
  This abstracts the modem implementation detail, avoiding every router having to understand how to map radio-signal metrics for modem type X into IP packet throughput.

## Slide 5: DLEP Extensions
The protocol is extensible, with extensions negotiated at session establishment.
Extensions exist (or are being developed):
  Handling modems that operate at Layer-3.
  Flow-control using credit-windowing
  Reporting on multiple traffic flows individually, by DSCP, 3-tuple, etc. This is of interest to RAW.
  Radio signal properties, e.g. SNR, BER.
  Rendezvous-point selection preference, i.e. does the underlying link-layer topology suggest good rendezvous points?

## Slide 6: DLEP + RAW
In the proposed RAW architecture, a Path Selection Element (PSE) attempts to maintain the ‘tracks’ defined by the Path Computation Element (PCE), using knowledge of the local wireless environment.
  When there is no underlying deterministic (TSN) capability provided by the link-layer.
DLEP can provide a generic mechanism for a PSE to monitor the wireless environment.
  Implementations exist using DLEP information to increase stability in MANETs.
  It seems a logical next step is to use DLEP information to increase determinism in wireless networks.
    DetNet over MANET seems unfeasible, but in reasonably controlled wireless environments... this sounds like RAW.

## Slide 7: Link Characteristics Request
DLEP has an additional (and under used) function: The Link Characteristics Request.
This function allows a Router to request a change to the capabilities of a link between itself and another destination.
  The Modem may refuse, if prevented by configuration or the laws of physics.
This mechanism may be extremely useful in a RAW context when attempting to ‘pin down’ deterministic tracks.

## Slide 8: Next Steps
Do we want to add a section to the technologies draft?
  I don’t think this warrants a draft in it’s own right
Do we wish to draft a DLEP extension addressing deterministic capabilities?
  Allow a wireless system to advertise TSN function?

## Slide 9: References
DLEP:
  https://tools.ietf.org/html/rfc8175
RAW technologies draft:
  https://datatracker.ietf.org/doc/draft-ietf-raw-technologies/
RAW architecture draft:
  https://datatracker.ietf.org/doc/draft-pthubert-raw-architecture/

## Slide 10: Questions?