## Slide 1: PCE based BIER Procedures and Protocol Extensions [draft-li-pce-based-bier]
Huanan Li(China Telecom)
Aijun Wang (China Telecom)
Huaimo Chen(Futurewei)
Ran Chen(ZTE Corporation)
IETF 111, July. 2021

## Slide 2
Overview of PCE based BIER solution
Extensions to PCE
Further Action

## Slide 3: Overview of PCE based BIER solution
PE1
receivers
PE2
PE3
IGMP/MLD
Join/Leave
IGMP/MLD
Join/Leave
(S,G) Register
Source
Controller
(PCE)
receivers
PCRpt
Join/Leave
Status synchronize
PCUpd
BitString sending
Status synchronize
PCUpd
PCRpt
(S,G) Register
Main flow for PCE based BIER multicast
PCE receives the registration information from ingress and responds.
PCE gets reports about egresses in PCRpt.
PCE generates BitString and sends it to ingress via PCUpd.
Ingress encapsulate BIER header and forward multicast packets.
The number of receivers is regularly synchronized between egress and PCE, and between PCE and ingress, using PCRpt and PCUpd respectively.
→
→

## Slide 4: Extensions to PCE
Newly defined Objects
  BIER-MULTICAST-CAPABILITY flag in STATEFUL-PCE-CAPABILITY TLV in the OPEN object
  Multicast Source Registration Object
  Multicast Receiver Information Object
  Forwarding Indication Object
  Multicast Receiver Status Object
Extensions to PCEP Message
  Open Message
  PCRpt Message
  PCUpd Message

## Slide 5: Multicast Source Registration Object
Application scenarios:
(S,G) registration/revocation in PCRpt and response in PCUpd
  Flag “R” bit indicates whether the action of the message is a registration request.
  Flag “A” bit indicates whether the request is successful.

## Slide 6: Multicast Receiver Information Object
Application scenarios:
Multicast joining or leaving in PCRpt
  Flag “S” bit indicates whether to join a multicast group.
  Forwarding Label is used for egress to distinguish receivers at the forwarding layer.

## Slide 7: Forwarding Indication Object
Application scenarios:
Informing ingress to forward packets of a specific (S,G) to receivers in PCUpd.
  Flag “F” bit indicates whether to start forwarding multicast data.

## Slide 8: Multicast Receiver Status Object
Application scenarios:
Egress synchronizes receiver information to PCE in PCRpt
PCE synchronizes receiver information to ingress in PCUpd
  Flag “F” bit indicates whether to start forwarding multicast data.
  In PCRpt messages, the number of receivers refers to connected to the egress in a specific (S,G) .
  In PCUpd messages, the number of receivers refers to all receivers in a specific (S,G).

## Slide 9: Extensions to PCEP Message
Open Message
BIER-MULTICAST-CAPABILITY flag in STATEFUL-PCE-CAPABILITY TLV in the OPEN object is set to support BIER multicast.
PCRpt Message includes
MSR object for registration or revocation
MRI object for receivers’ joining or leaving(not the last one)
MRS object for periodic synchronization of receivers’ number
MRI and MRS objects for receiver’s leaving(the last one)
PCUpd Message includes
MSR object for response to registration or revocation
FI object for indicating data forwarding
MRS object for periodic synchronization of receivers’ number

## Slide 10: Next Step
Comments
lihn6@chinatelecom.cn
wangaj3@chinatelecom.cn
Huaimo.chen@futurewei.com
chen.ran@zte.com.cn
IETF111