## Slide 1: Reliable and Available Wireless Architecture/Framework
Presenter: Pascal Thubert
Authors: P. Thubert, G.Z. Papadopoulos, Lou Berger, (+ contributors)

## Slide 2: The RAW Architecture
OODA with 3 new steps:
  Observe (OAM), Orient (PCE), Decide (PSE), Act (PAREO)
PSE:
  DetNet to signal Flow information
  RAW-SRv6 to hint/control DetNet Service Layer
  PSE operate at Track Ingress only (control)
  PSE may be partially distributed (hint)
  PSE may be fully distributed (No SRv6 signaling)
DetNet Service Plane
  Enrich DetNet (PAREO, timing, SR hint/control))
Redundant Radio Access
draft-ietf-raw-architecture
Packet flow / SR, IPPM
Feedback / DLEP, OAM
PSE at Ingress (headend)
(PSE) DetNet Service Layer

## Slide 3: RAW Architecture/Framework draft status
Personal submission bumped from 06 to 09 during WGLC
  Adopted: 09 was then republished as WG document
Lots of new work
  Abstract
  Terminology (more next)
  Review comments around OAM (thanks G. Mirsky and F. Theoleyre)
  RAW OAM extensions, e.g., reverse OAM
What’s missing:
  New Sections ?
  Yaakov’s work / SRv6
  DLEP (Lou?)
draft-ietf-raw-architecture

## Slide 4: New terms (1/4)
Flow (the water):
  A collection of consecutive packets that must be placed on the same Track to receive an equivalent treatment from Ingress to Egress within the Track. Multiple flows may be transported along the same Track. The subTrack that is selected for the flow may change over time under the control of the PSE.
Track (the pipe):
  A networking graph that can be used as a "path" to transport RAW packets with equivalent treatment; as opposed to the usual understanding of a path (see for instance the definition of "path" in section 1.1 of [RFC9049]), a Track may fork and rejoin to enable the PAREO operations.
  In DetNet [RFC8655] terms, a Track has the following properties:
  A Track has one Ingress and one Egress nodes, which operate as DetNet Edge nodes.
  A Track is reversible, meaning that packets can be routed against the flow of data packets, e.g., to carry OAM measurements or control messages back to the Ingress.
  The vertices of the Track are DetNet Relay nodes that operate at the DetNet Service sublayer and provide the PAREO functions.
  The topological edges of the graph are serial sequences of DetNet Transit nodes that operate at the DetNet Forwarding sublayer.
draft-ietf-raw-architecture

## Slide 5: New terms (2/4)
SubTrack:
  A Track within a Track. The RAW PSE selects a subTrack on a per-packet or a per-collection of packets basis to provide the desired reliability for the transported flows.
Segment:
  A serial path formed by a topological edge of a Track.
  East-West Segments are oriented from Ingress (East) to Egress (West).
  North/South Segments can be bidirectional;
  to avoid loops, measures must be taken to ensure that a given packet flows either Northwards or Southwards along a bidirectional Segment, but never bounces back.
Flapping:
  In the context of RAW, a link flaps when the reliability of the wireless connectivity drops abruptly for a short period of time, typically of a subsecond to seconds duration.
Structurally not a DODAG though the packet experiences one
draft-ietf-raw-architecture

## Slide 6: New terms (3/4)
OAM:
  OAM stands for Operations, Administration, and Maintenance, and covers the processes, activities, tools, and standards involved with operating, administering, managing and maintaining any system. This document uses the terms Operations, Administration, and Maintenance, in conformance with the 'Guidelines for the Use of the "OAM" Acronym in the IETF' [RFC6291] and the system observed by the RAW OAM is the Track.
Active OAM:
  See [RFC7799]. In the context of RAW, Active OAM is used to observe a particular Track, subTrack, or Segment of a Track regardless of whether it is used for traffic at that time.
In-Band OAM:
  An active OAM packet is considered in-band for the monitored Track when it traverses the same set of links and interfaces and if the OAM packet receives the same QoS and PAREO treatment as the packets of the data flows that are injected in the Track.
.
draft-ietf-raw-architecture

## Slide 7: New terms (4/4)
Out-of-Band OAM:
  Out-of-band OAM is an active OAM whose path is not topologically congruent to the Track, or its test packets receive a QoS and/or PAREO treatment that is different from that of the packets of the data flows that are injected in the Track, or both.
Limited OAM:
  An active OAM packet is a Limited OAM packet when it observes the RAW operation over a node, a segment, or a subTrack of the Track, though not from Ingress to Egress. It is injected in the datapath and extracted from the datapath around the particular function or subnetwork (e.g., around a relay providing a service layer replication point) that is being tested.
Reverse OAM:
  A Reverse OAM packet is an Out-of-Band OAM packet that traverses the Track from egress to ingress on the reverse direction, to capture and report OAM measurements upstream. The collection may capture all information along the whole Track, or it may only learn select data across all, or only a particular subTrack, or Segment of a Track
draft-ietf-raw-architecture

## Slide 8: Section 4.3 on OAM
“In other words, the best suited OAM method to enable the PSE make accurate PAREO forwarding decisions is a periodic variation of the two-steps method flowing along the reverse Track, as a Reverse OAM technique. [RAW-OAM] provides more information on the RAW OAM problem and solution approaches”
The document makes a recommendation
Are there other recommendations?
In other terms?
draft-ietf-raw-architecture

## Slide 9: Questions ?
draft-ietf-raw-architecture

## Slide 10: Content from IETF 108
Back up slides

## Slide 11: RAW interactions with other IETF WGs
DetNet: RAW is mostly a focused Subset
  Radio specialists, different interests
  Unstable links (bandwidth, flapping), not ‘deterministic’
  OAM is a common interest – cross participation
MANET: Non-Congruent domains
  Non-Mobile & not Ad-Hoc (antagonistic to DetNet)
  Centralized routing
  DLEP a relevant tool but need multihop view (OAM)
CCAMP: May need work from CCAMP for data models
IPPM can be leveraged for in-band OAM, direct export,
and BIER for path selection & control
draft-pthubert-raw-architecture

## Slide 12: Terms
Reliability: Reliability is a measure of the probability that an item will perform its intended function for a specified interval under stated conditions. For RAW, the service that is expected is delivery within a bounded latency and a failure is when the packet is either lost or delivered too late. RAW expresses reliability in terms of Mean Time Between Failure (MTBF) and Maximum Consecutive Failures (MCF). More in [NASA].
Availability: Availability is a measure of the relative amount of time where a path operates in stated condition, in other words (uptime)/(uptime+downtime). Because a serial wireless path may not be good enough to provide the required availability, and even 2 parallel paths may not be over a longer period of time, the RAW availability implies a path that is a lot more complex than what DetNet typically envisages (a Track)
PAREO: Packet (hybrid) ARQ, Replication, Elimination and Ordering. PAREO is a superset Of DetNet's PREOF that includes radio-specific techniques such as short range broadcast, MUMIMO, constructive interference and overhearing, which can be leveraged separately or combined to increase the reliability
draft-pthubert-raw-architecture

## Slide 13: The Gap
Due to uncontrolled interferences, including the self-induced multipath fading, deterministic networking can only be approached on wireless links.
The radio conditions may change -way- faster than a centralized PCE can adapt and reprogram, in particular when the controller is distant and connectivity is slow and limited.
RAW separates the path computation time scale at which a complex path is recomputed from the path selection time scale at which the forwarding decision is taken for one or a few packets.
RAW operates at the path selection time scale. The RAW problem is to decide, within the redundant solutions that are proposed by the PCE, which will be used for each packet to provide a Reliable and Available service while minimizing the waste of resources.
Controller
Wireless
network
FAST
SLOW
LARGE
SMALL
SLOW
Reliability & Availability vs. Energy & Bandwidth
draft-pthubert-raw-architecture

## Slide 14: RAW within (and vs.) DetNet
RAW operates at the DetNet Service Layer in the Network Plane
Controller Plane Functions compute complex Tracks
RAW Nodes provide a PSE function
RAW observes a selection of L2 Links (the others are “infinite”)
RAW observes the L3 end-to-end operation
CPF CPF CPF CPF
Southbound API
_-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-
_-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-
RAW --z RAW --z RAW --z RAW
z-- Node z-- Node z-- Node z-- Node --z
Ingress --z / / z-- Egress
End \ \ .. . End
Node ---z / / .. .. . z-- Node
z-- RAW --z RAW ( non-RAW ) -- RAW --z
Node z-- Node --- ( Nodes ) Node
... .
--z wireless wired
z-- link --- link
draft-pthubert-raw-architecture
Notes: RAW inherits the conceptual model described in section 4 of the DetNet Architecture [RFC8655]. RAW extends the DetNet service layer to provide additional agility against transmission loss. A Controller Plane Function (CPF) called the Path Computation Element (PCE) [RFC4655] interacts with RAW Nodes over a Southbound API. The RAW Nodes are DetNet relays that are capable of additional diversity mechanisms and measurement functions related to the radio interface, in particular the PAREO diversity mechanisms. The PCE defines a complex Track between an Ingress End System and an Egress End System, and indicates to the RAW Nodes where the PAREO operations may be actionned in the Network Plane. The Track may be expressed loosely to enable traversing a non-RAW subnetwork. In that case, the expectation is that the non-RAW subnetwork can be neglected in the RAW computation, that is, considered infinitely fast, reliable and/or available in comparison with the links between RAW nodes.

## Slide 15: RAW Architecture: RAW i/oOAM
RAW OAM operation in the Network Plane observes either a full Track or subTracks that are being used at this time. In the case of Radio Access Protection, the Track is Loose and only the first hop is observed:
... ..
RAN 1 ----- ... .. ...
/ . .. ....
+-------+ / . .. .... +------+
|Ingress|- . ..... |Egress|
| End |------ RAN 2 -- . Internet ....---| End |
|System |- .. ..... |System|
+-------+ \ . ...... +------+
\ ... ... .....
RAN n -------- ... .....
<------------------> <-------------------->
Observed by OAM Opaque to OAM
draft-pthubert-raw-architecture
Notes: The RAW OAM operation in the Network Plane observes either a full Track or subTracks that are being used at this time. This observeation feeds the RAW PSE that makes the decision on which PAREO function in actioned at which RAW Node, for one a small continuous series of packet
In the case of a End-to-End Protection in a Wireless Mesh, the Track is strict and congruent with the path so all links are observed. Conversely, in the case of Radio Access Protection, the Track is Loose and in that case only the first hop is observed; the rest of the path is abstracted and considered infinitely reliable. In the case of the Radio Access Protection, only the first hop is protected; the loss of a packet that was sent over one of the possible first hops is attributed to that first hop, even if a particular loss effectively happens farther down the path. The Links that are not observed by OAM are opaque to it, meaning that the OAM information is carried across and possibly echoed as data, but there is no information capture in intermediate nodes. In the example above, the Internet is opaque and not controlled by RAW; still the RAW OAM measures the end-to-end latency and delivery ratio for packets sent via each if RAN 1, RAN 2 and RAN 3, and determines whether a packet should be sent over either or a collection of those access links.

## Slide 16: RAW Architecture: the PSE
RAW defines path selection engine (PSE) that performs rapid local adjustments of the forwarding tables to avoid excessive use of the resource diversity that the PCE proposes
Exploiting richer forwarding capabilities with PAREO and scheduled transmissions
 | PCE (not in scope) | PSE (in scope)
Operation | Centralized | Source-Routed or Distributed
Communication | Slow, expensive | Fast, local
Time Scale | Long (hours, days) | Short (sub-second)
Network size | Large, many Tracks to compute | Small, within one Track
Metrics | Averaged, Statistical, Shade of grey | Instant values / boolean state
draft-pthubert-raw-architecture

## Slide 17: RAW Architecture: The PSE “Stack”
|
packet | going
down the | stack
+==========v==========+=====================+=====================+
| (iOAM + iCTRL) | (L2 Triggers, DLEP) | (oOAM) |
+==========v==========+=====================+=====================+
| Learn from Learn from |
| packet tagging Maintain end-to-end |
+----------v----------+ Forwarding OAM packets |
| Forwarding decision < State +---------^-----------|
+----------v----------+ | Enrich or |
+ Retag Packet | Learn abstracted > Regenerate |
| and Forward | metrics about Links | OAM packets |
+..........v..........+..........^..........+.........^.v.........+
| Lower layers |
+..........v.....................^....................^..v........+
frame | sent Frame | L2 Ack oOAM | | packet
over | wireless In | In | | and out
v | |
draft-pthubert-raw-architecture
Notes: The PSE sits in the DetNet Service sub-Layer of Edge and Relay Nodes. On the one hand, it operates on the packet flow, learning the Track and path selection information from the packet, possibly making local decision and retagging the packet to indicate so. On the other hand, the PSE interacts with the lower layers and with its peers to obtain up-to-date information about its radio links and the quality of the overall Track, respectively.

## Slide 18: What do we need to do?
Select Appropriate Radios and Effective Use Cases
  Req: Capability to schedule resources
  Opt: Diversity capabilities (frequency, beam, …)
Adapt per-packet activity of a RAW flow along a diverse path
  Determine Specific Data Models to match radio properties (for CCAMP and IPPM?)
  Signal forwarding properties in packets (e.g., BIER-TE)
  Source routed and Distributed forwarding decision (use of PAREO functions)
  In-band control of resource Usage to optimize energy and bandwidth
Enable i/oOAM (in and out-of-band)
  Forward packets or generated placebo packets to measure LQI
  In-band forward and out-of-band backward gathering of metrics across NECM
draft-pthubert-raw-architecture
Notes: In a nutshell: While scheduling transmissions can guarantee the time of delivery, it is impossible, in the ISM band, to keep all possible interferers at bay. Co-channel interference, as well as the self-inflicted Multi-Path fading, which is due to echoes of the transmission, are unavoidable. So there is no way to guarantee the delivery of all frames.
It takes different mitigation techniques to avoid the different issues that affect wireless transmissions. To combat them all, all possible forms of diversity should be leveraged, in the spatial domain by routing over multipath, in the temporal domain by retrying transmissions or sending copies over parallel paths at distinct times, and in the frequency domain with frequency hopping (within frames) or channel hopping (between frames).
Several times along the way to the destination, the work presented in this manuscript replicates and then eliminates the copies of a packet that are forwarded along parallel disjoint paths, hopping between frequencies with each transmission so that a copy along one path does not interfere with a copy along the other