## Slide 1: Neighbor Discovery Unicast Lookup
Pascal Thubert
draft-thubert-6lo-unicast-lookup
IETF 112
Virtual

## Slide 2: 6LoWPAN ND (IPv6 Stateful Address Autoconfiguration)
  RFC 6775 (original 6LoWPAN ND)
        Defines ARO for registration and DAD operations for stateful AAC
  RFC 8505 (extended 6LoWPAN ND)
        Extends ARO, updates the registration procedure
        Allows registering to network services inc. proxy
  RFC 8928 (Address Protection for ND)
        Secures ownership and enables SAVI
  RFC 8929 (Backbone Router – proxy ND)
        Defines a proxy ND operation. Updates EDAR to transport ND options such as SLLAO.
  draft-thubert-6lo-unicast-lookup (Unicast Address lookup on backbone)
        Allows the 6LBR to respond to lookups and saves broadcasts
  draft-ietf-6lo-multicast-registration (Anycast and Multicast Address Registration)
        Registers anycast and multicast addresses (in addition to unicast per RFC 8505

## Slide 3: Changes in draft-thubert-6lo-unicast-lookup
Draft published at 6lo in 2019
Circulated at 6MAN
Failed to raise interest
Note that this is not maintenance but new feature
Republished as 01 at 6lo
Suggestion to work it out here since we did all the work so far.

## Slide 4: Draft operation
EDAR is extended by RFC 8929 to transport SLLA
An abstract 6LBR is placed on backbone
  Maintains registration for unicast and anycast IPv6@
  Contains ROVR and LLA(s) associated with IPv6@
  learns SLLA from NS(EARO) and EDAR
  Answers DAD requests (EDAR/EDAC)
  New: Provides unicast Address Mapping services
New Address Mapping messages
  can have scope > link for off-link query
  Unicast link-scope NS/NA can also be used
New status “not found”

## Slide 5: Next steps
Explain 6LBR is abstract
  can be a distributed database
  E.g., draft-thubert-bess-secure-evpn-mac-signaling
Reference draft-ietf-6lo-multicast-registration
  For anycast address registration