## Slide 1: PCE based BIER Procedures and Protocol Extensions [draft-li-pce-based-bier]
Huanan Li(China Telecom)
Aijun Wang (China Telecom)
Huaimo Chen(Futurewei)
Ran Chen(ZTE Corporation)
IETF 112, November. 2021

## Slide 2
Overview of PCE based BIER solution
Updates
Further Action

## Slide 3: Overview of PCE based BIER solution
PE1
receivers
PE2
PE3
IGMP/MLD
Join/Leave
IGMP/MLD
Join/Leave
(S,*) Register
Source
Controller
(PCE)
receivers
PCRpt
Join/Leave
Status synchronize
PCUpd
BitString sending
Status synchronize
PCUpd
PCRpt
(S,*) Register
Main flow for PCE based BIER multicast
PCE receives the registration information from ingress and responds.
PCE gets reports about egresses in PCRpt.
PCE generates BitString and sends it to ingress via PCUpd.
Ingress encapsulate BIER header and forward multicast packets.
The number of receivers is regularly synchronized between egress and PCE, and between PCE and ingress, using PCRpt and PCUpd respectively.
→
→

## Slide 4: New TLVs

## Slide 5: New TLVs

## Slide 6: Update for Multicast Source Registration Object
Can be used in both BIER and non-BIER scenarios
BIER:
Multicast Source Address TLV, VPN Information TLV, BIER Information TLV
Non-BIER:
Multicast Source Address TLV, VPN Information TLV

## Slide 7: Update for Multicast Receiver Information Object
Can be used in both BIER and non-BIER scenarios
BIER:
Multicast Source Address TLV, Multicast Group Address TLV, VPN Information TLV, BIER Information TLV
Non-BIER:
Multicast Source Address TLV, Multicast Group Address TLV, VPN Information TLV

## Slide 8: Update for Forwarding Indication Object
Can be used in BIER scenario:
Multicast Source Address TLV, Multicast Group Address TLV, VPN Information TLV

## Slide 9: Update for Multicast Receiver Status Object
Can be used in both BIER and non-BIER scenarios
BIER:
Multicast Source Address TLV, Multicast Group Address TLV
Non-BIER:
Multicast Source Address TLV, Multicast Group Address TLV

## Slide 10: Next Step
Comments
lihn6@chinatelecom.cn
wangaj3@chinatelecom.cn
Huaimo.chen@futurewei.com
chen.ran@zte.com.cn
IETF112